## Slide 1: Waveform for AMP
Date: 2024-09-09
Authors:
Name | Affiliation | Address | Phone | Email
Wang Ke | OPPO |  |  | wangke6@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-24/1533r0
Sep 2024

## Slide 2: Abstract
In this contribution, we further discuss waveform for AMP, focusing on MSK, BPSK and OOK.
Doc.: IEEE 802.11-24/1533r0

## Slide 3
Baseband Signal
Wang Ke (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1533r0
Sep 2024

## Slide 4
Spectrum
  Observation 1:
  MSK is the best in terms of occupied bandwidth and side lobe attenuation.
Wang Ke (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1533r0
Sep 2024

## Slide 5
Performance Comparison
  Observation 2:
  MSK and BPSK have the same performance
  As expected, MSK/BPSK has 3dB gain compared to OOK
Wang Ke (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1533r0
Sep 2024
    Chip rate Rb : 1Mbps
    Payload : 96bits
    Sampling rate Fs : 4Mbps
    Channel : AWGN

## Slide 6
Summary
Wang Ke (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1533r0
Sep 2024
 | BW | performance | Complexity (backscattering) | Complexity (active) | Spectrum shape
OOK | 2 Rb | Baseline | low | low | worse
BPSK | 2 Rb | +3 dB gain | Little Higher than OOK | Higher than OOK | good
MSK | 1.5 Rb | +3 dB gain | - | Higher than OOK | best
Proposal 1:
OOK is supported as baseline waveform.

## Slide 7
Potential influence of the timing accuracy
  For AMP uplink transmission, there will be frequency offset due to poor clock accuracy. e.g. maximum frequency of 2.4MHz for ± 1000ppm.
  The influence of timing accuracy needs to be taken into account.
    For OOK, the impact is expected to be negligible since OOK is not sensitive to the frequency offset when using envelope detection
    However, coherent detection is used for BPSK and MSK, which may rely on frequency offset estimation .
  Proposal 2:
  Further study the impact of frequency offset on the performance of BPSK and MSK .
Wang Ke (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1533r0
Sep 2024

## Slide 8
Summary
  Observation 1: MSK is the best in terms of occupied bandwidth and side lobe attenuation.
  Observation 2: MSK and BPSK have the same performance and MSK/BPSK has 3dB gain compared to OOK.
  Proposal 1: OOK is supported as baseline waveform.
  Proposal 2: Further study the impact of frequency offset on the performance of BPSK and MSK .
Wang Ke (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1533r0
Sep 2024

## Slide 9
SP
  Do you agree that OOK is supported as baseline waveform for UL transmission?
    Other waveforms, e.g., MSK/BPSK is TBD.
Wang Ke (OPPO)
Slide 9
Doc.: IEEE 802.11-24/1533r0
Sep 2024