## Slide 1: Wireless connectivity challenges for AMP only IoT devices under 802.11 specification
Date: 2024-09-05
Authors:

## Slide 2: Abstract
In this contribution, we discuss how to specify wireless connectivity for AMP only IOT devices as part of the 802.11 specification.
The IEEE 802.11 standard specifies that:
Data frames are used for end-to-end communication across networks
Non-AP STAs use AP STAs to access the distribution system
The AMP-only IoT device are characterized as ultra-low complexity, ultra-low power consumption, very small form factor and battery-less.
Data frames, as used for data traffic, contain the overhead of multiple network protocol headers, which significantly increases the frame size. The power consumption required to deliver such long frames may be prohibitive for some types of AMP-only IoT devices.
Association and secure authentication with an AP STA requires multiple rounds of long frame exchanges, storing intermediate and final data on the AMP-only device. The computational complexity, memory footprint, and power consumption can be prohibitive for some types of AMP-only IoT devices.
In this contribution we analyze the challenges and suggest solution

## Slide 3: AMP IoT-only devices
Different types of AMP devices have been identified and analyzed in previously presented and published contributions [1] and [2]. There are AMP-only IoT devices.
The AMP-only IoT device are characterized as ultra-low complexity, ultra-low power consumption, very small form factor and battery-less (i.e., not using conventional battery). This also limits the computational complexity, memory footprint and memory retention time, peak device power consumption, and the size of received and transmitted frames.

## Slide 4: 802.11 definition challenges and solutions
The IEEE 802.11 standard specifies that:
Data frames are used for end-to-end communication across networks.
The data frames, as used for data traffic, contain the overhead of multiple network protocol headers, which significantly increases the frame size.
We propose to use non-data frames to deliver the information of AMP-only IoT devices
Non-AP STAs use AP STAs to access the distribution system
Association and secure authentication with an AP STA requires multiple rounds of exchange of long frames, storing intermediate and final data on the AMP-only IoT device.
We propose that an unassociated AMP-only IoT device communicates with an AMP-capable STA that provides access to the distribution system. This can be an AP STA or a non-AP STA

## Slide 5: Data frames versus non-Data frames

## Slide 6: 802 Reference model [6]
MAC data frame header
(30 octets)
LLC header
(8 octets)
TCP/UDP header
(8 octets)
IP header
(40 octets)

## Slide 7: Layer Protocols
Transport layer
Provides the means for transmitting data between the two connected parties, as well as controlling the quality of service. The main protocols used here are TCP and UDP
Network layer
Handles the routing and sending of data between different networks. The most important protocols at this layer are IP (IPV4, IPV6).
5.2.2 LLC (logical link control) sublayer [6]
The higher layer protocol discrimination entity (HLPDE) is used by the LLC sublayer to determine the higher layer protocol to which to deliver an LLC sublayer protocol data unit (PDU).
5.2.3 MAC (media access control) sublayer [6]
The MAC sublayer performs the functions necessary to provide frame-based, connectionless-mode‌ﾠ(datagram style) data transfer between stations in support of the next higher sublayer, as described in 5.1, for networks that support it. In some MAC types, some MAC frames are used in support of the MAC sublayer functionality itself, rather than for transfer of data from the next higher sublayer.

## Slide 8: MAC data frame overhead [4]

## Slide 9: Networking overhead
Protocol layer/ sublayer | Header + trailer size | 
 | Octet | Bit
MAC (PV0/PV1) | 30/18 | 240/144
Addition of Encrypted MAC frame | 24 | 192
LLC | 8 | 64
IPv6 | 40 | 320
UDP | 8 | 64
Total | 110/98 | 880/784
Maximum payload size for AMP use cases = 256 bit [2]

## Slide 10: Recommendation 1
The data frame overhead for directly delivering AMP-only IoT STA information to the network is three times the maximum payload.
To meet AMP-only IoT STA constraints (power, etc.), we propose to provide a solution that does not require AMP-only IoT STA delivering data frames to the network.

## Slide 11: Non-Data frame formats
The base specification [4] uses three approaches to define frames (1, 2, 3)
# | PV | Pros | Cons | Comment
1 | 0 |  | The first three fields Frame Control(16bit), Duration/ID(16bit), and Address 1(48bit) and the last field (FCS) (32bit) are present in all these frames, including reserved types and subtypes. (112bit) | Not all fields are required for AMP IoT RF powered devices. Fields that can be used for AMP IoT RF powered devices may be shorter.
2 | 1 |  | The first three fields Frame Control (16bit), A1(16bit) and A2 (16bit) and the last field FCS (32bit) are always present in PV1 frames (80bit) | 
3 | NA | The shortest frame is 48 bit long |  | 9.9 MAC frame format for WUR frames WUR PHY-dependent MAC frame format, three types are reserved and can be used for AMP IoT
4 | NA | Frame formats optimized for AMP IoT | Requires AMP IoT specific PPDU definition (PHY) | PHY isolated MAC Frame formats

## Slide 12: Recommendation 2
Using the PV0 and PV1 frame formats for frames that do not contain data introduces significant overhead when used to communicate with AMP-only IoT STAs. Shorter frame control and FCS fields and using only one identifier field may be appropriate to save transmit power.
Options 3 and 4 are the frame formats most suitable for communicating with AMP-only IoT devices, while still providing greater flexibility to construct optimal frame formats
  NOTE: The PPDU format allows legacy devices to ignore AMP-only IoT PPDUs and not erroneously decode the PPDU payload.

## Slide 13: Access of AMP-only IoT devices to the distribution system

## Slide 14: Association with AP is a big overhead for an AMP-only IoT device

## Slide 15: Overhead of the management frame exchange (Example of an Association Request frame)
Table 9-64—Association Request frame body
Order | Information | Size (octet)
1 | Capability Information | 2
2 | Listen Interval | 2
3 | SSID element | 3 (min)
8 | RSN Element | 22 (min)
 | Overall size of frame body field | 29
Name | Size (octet) | Size (bit)
Frame Control | 2 | 
Duration | 2 | 
Address 1 | 6 | 
Address 2 | 6 | 
Address 3 | 6 | 
Sequence control | 2 | 
Frame Body | 29 | 
FCS | 4 | 
Total | 57 | 456

## Slide 16: Complexity of the State transition diagram
The association and secure authentication procedure consists of several steps. The procedure involves the exchange of 5 messages from each side. At each step, the AP STA's response may not be instantaneous. Thus, the non-AP STA must store intermediate results.
Once a non-AP STA associates with a BSS infrastructure, it maintains state of associated for a long time, even in low power state. The time spent in the association state can be significantly longer than the time required for association.
An AP STA is always aware of the power state of its associated non-AP STA.

## Slide 17: Impact of State Transition Diagram on AMP-only IoT STA
The size and content of the frames used for state transitions require such energy expenditures for receiving/transmitting and storing the contents of these frames that may be prohibitive for some types of AMP-only IoT devices.
The energy harvesting mechanism cannot guarantee that the AMP-only IoT STA has enough energy to perform the association/authentication steps and maintain memory to save the association state.
The energy harvesting mechanism cannot guarantee that the AMP-only IoT STA will notify the AP STA when the device is running low on energy, and the AP STA has no means to prevent sudden and frequent disassociations under such circumstances.

## Slide 18: An example of how to allow AMP-only IoT devices to access the distribution system
AMP capable Non-AP STA
AMP only IoT STA
AMP-only IoT STA communicates with AMP-capable non-AP STA - no association required
AMP-only IoT STA uses non-data frames to deliver information to AMP-capable non-AP STA
AMP-capable non-AP STA converts information from AMP-only IoT STA into data frames and delivers the frames to the AP with which it is associated.
Another proposal is that non-associated access functionality is integrated into AMP-capable AP STA

## Slide 19: Summary
The power consumption and memory footprint required to deliver data frames may be prohibitive for some types of AMP-only IoT devices.
The computational complexity, memory footprint, and power consumption may be prohibitive for some types of AMP-only IoT devices to provide association with the AP.
We propose that AMP-only IoT STA accesses the distribution system without association. Non-Data frames are used for communication between AMP-only IoT STA and AMP-compatible non-AP STA or AP STA.

## Slide 20: References
11-23-0436-00-0amp-technical-report-on-support-of-amp-iot-devices-in-wlan
11-23-1005-00-0amp-discussion-on-requirements-for-amp-use-cases
ISO/IEC 18000-63:2021(E)
IEEE P802.11-REVme/D6.0, June 2024
IEEE P802.11bf/D4.0, April 2024
IEEE Std 802®-2014 Standard for Local and Metropolitan Area Networks: Overview and Architecture
ISO/IEC 7498-1:1994 Open Systems Interconnection basic reference model (OSI/RM)

## Slide 21: Straw Poll
SP#1
Do you agree that the amendment will define communication with AMP-only IoT devices through non-data frames?
Yes
No
Abstain

## Slide 22: Straw Poll
SP#2
Do you agree that the amendment will define the access of unassociated AMP-only IoT devices to the distribution system?
Yes
No
Abstain

## Slide 23: Straw Poll
SP#3
Do you agree that the amendment will define the access of unassociated AMP-only IoT devices to the distribution system through non-data frames?
Yes
No
Abstain

## Slide 24: Backup

## Slide 25
Requirements [2]
 | Coverage (dBm) | Maximum payload size (bit) | Peak device power consumption (mWatts) | Device density (per m2) | Horizontal Positioning accuracy (m) | Peak data rate (Kbps) | Others
UC1: Smart Manufacturing | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC2: Data Centre | Type1: -30 Type2: -82 | 256 | 1 | 3 | 1-3 | 51.2 kbps | 
UC3: Smart Home | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC4: Logistics and Warehouse | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC5: Smart Agriculture | Type1: -30 Type2: -82 | 256 | 1 | 1 | 10 | 51.2 kbps | 
UC6: Indoor Positioning | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC7: Smart Power Grid | Type1: -30 Type2: -82 | 256 | 1 | 10-2 | 10 | 51.2 kbps | 
UC8: Fresh Food Supply Chain | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
Note 1: Coverage is calculated based on AWGN Channel Note 2: Type 1: RF powered AMP device; Type 2: non-RF powered AMP device, e.g., thermal, solar, etc. Note 3: Others include requirements only applicable to a subset of use cases |  |  |  |  |  |  |