## Slide 1: Wireless connectivity challenges for AMP only IoT STA under 802.11 specification
Date: 2024-11-05
Authors:

## Slide 2: Abstract
In this contribution, we discuss how to specify wireless connectivity for AMP only IOT STA as part of the 802.11 specification.
The IEEE 802.11 standard specifies that:
Data frames are used for end-to-end communication across networks
Non-AP STAs use AP STAs to access the distribution system
The AMP-only IoT STA are characterized as ultra-low complexity, ultra-low power consumption, very small form factor and battery-less.
Data frames, as used for data traffic, contain the overhead of multiple network protocol headers, which significantly increases the frame size. The power consumption required to deliver such long frames may be prohibitive for some types of AMP-only IoT STA.
Association and secure authentication with an AP STA requires multiple rounds of long frame exchanges, storing intermediate and final data on the AMP-only STA. The computational complexity, memory footprint, and power consumption can be prohibitive for some types of AMP-only IoT STA.
In this contribution we analyze the challenges and suggest solution

## Slide 3: AMP-only IoT STA
Different types of AMP STA have been identified and analyzed in previously presented and published contributions [1] and [2]. There are AMP-only IoT STA.
The AMP-only IoT STA are characterized as ultra-low complexity, ultra-low power consumption, very small form factor and battery-less (i.e., not using conventional battery). This also limits the computational complexity, memory footprint and memory retention time, peak device power consumption, and the size of received and transmitted frames.

## Slide 4: 802.11 definition challenges
The known solutions provided by 802.11 do not address the mentioned features, and furthermore, attempting to adopt existing 802.11 approaches may compromise 802.11bp and make it irrelevant for AMP-only IoT STAs.
In particular, there are two main obstacles if we want to adopt the approaches presented in 802.11:
1. access to the distribution system via association with an AP STA
2. direct support by the end device, the AMP-only IoT STA in the role of a non-AP STA, of the full network protocol stack.

## Slide 5: 802.11 definition challenges (cont.)
The first is problematic for AMP-only IoT STAs because:
  - The size and content of the frames used for association/authentication state transitions require such an energy cost for receiving/transmitting and storing the contents of these frames that may be prohibitive for some types of AMP-only IoT STAs.
  - The energy harvesting mechanism cannot guarantee that the AMP-only IoT STA will have enough energy to perform the association/authentication steps and maintain memory to save the association state.
  - The energy harvesting mechanism cannot guarantee that the AMP-only IoT STA will notify the AP STA when the device is running low on energy, and the AP STA has no means to prevent sudden and frequent disconnections in such circumstances.
The second is problematic for AMP-only IoT STAs because:
  - The data frame overhead for directly delivering AMP-only IoT STA information to the network is three times the maximum AMP payload.
  - The energy cost of receiving/transmitting and processing the network protocols of these frames can be prohibitive for some types of AMP-only IoT STAs.

## Slide 6: Proposed TGbp solutions
We propose that the following approach can address these obstacles.
- We introduce the concept of AMP-capable STA.
- An AMP-capable STA supports network protocols above the MAC layer to transmit information received from an AMP-only IoT STA to the network and vice versa.
- The AMP-only IoT STA communicates with the AMP-capable STA.
- The communication between an AMP-only IoT STA and an AMP-capable STA is unassociated. Thus, there is no need to consume power to transmit long management frames to establish communication and store communication state information in memory.
The frames used to communicate with the AMP-only IoT STA do not contain network protocol headers above the MAC layer. Thus, the frames used to communicate with the AMP-only IoT STA contain less overhead.
The AMP-capable STA may be part of an access point

## Slide 7: Access of AMP-only IoT STA to the distribution system

## Slide 8: Association with AP is a big overhead for an AMP-only IoT STA

## Slide 9: Overhead of the management frame exchange (Example of an Association Request frame)
Table 9-64—Association Request frame body
Order | Information | Size (octet)
1 | Capability Information | 2
2 | Listen Interval | 2
3 | SSID element | 3 (min)
8 | RSN Element | 22 (min)
 | Overall size of frame body field | 29
Name | Size (octet) | Size (bit)
Frame Control | 2 | 
Duration | 2 | 
Address 1 | 6 | 
Address 2 | 6 | 
Address 3 | 6 | 
Sequence control | 2 | 
Frame Body | 29 | 
FCS | 4 | 
Total | 57 | 456

## Slide 10: Complexity of the State transition diagram
The association and secure authentication procedure consists of several steps. The procedure involves the exchange of 5 messages from each side. At each step, the AP STA's response may not be instantaneous. Thus, the non-AP STA must store intermediate results.
Once a non-AP STA associates with a BSS infrastructure, it maintains state of associated for a long time, even in low power state. The time spent in the association state can be significantly longer than the time required for association.
An AP STA is always aware of the power state of its associated non-AP STA.

## Slide 11: Impact of State Transition Diagram on AMP-only IoT STA
The size and content of the frames used for state transitions require such energy expenditures for receiving/transmitting and storing the contents of these frames that may be prohibitive for some types of AMP-only IoT STA.
The energy harvesting mechanism cannot guarantee that the AMP-only IoT STA has enough energy to perform the association/authentication steps and maintain memory to save the association state.
The energy harvesting mechanism cannot guarantee that the AMP-only IoT STA will notify the AP STA when the device is running low on energy, and the AP STA has no means to prevent sudden and frequent disassociations under such circumstances.

## Slide 12: An example of how to allow AMP-only IoT STA to access the distribution system
AMP capable Non-AP STA
AMP-only IoT STA
AMP-only IoT STA communicates with AMP-capable non-AP STA - no association required
AMP-only IoT STA uses frames other than the data type frames to deliver information to AMP-capable non-AP STA
AMP-capable non-AP STA converts information from AMP-only IoT STA into data frames and delivers the frames to the AP with which it is associated.
Another proposal is that non-associated access functionality is integrated into AMP-capable AP STA
Un-Associated mode
Associated mode

## Slide 13: Frame formats

## Slide 14: Frame formats. General frame format
9.2.3 General frame format
PV0 Frame control field
PV1 Frame control field
The general frame format contains Protocol Version and Type subfields that allow the identification of a frame transmitted in any PPDU format in all PHY types.

## Slide 15: Frame formats. WUR frame format
The WUR frame format is incompatible with the general frame format and is unique to the WUR PPDU format. The WUR PPDU shall include a WUR frame

## Slide 16: Frame types
Protocol Version 0 | 
Type value B3 B2 | Type description
00 | Management
01 | Control
10 | Data
11 | Extension
Protocol Version 1 | 
Type value B2 B4 | Type description
0 | QoS Data
1 | Management
2 | Control
3 | QoS Data
4-6 | Reserved
7 | Reserved for extension
WUR frame format No Protocol Version field | 
Type value B0 B2 | Type description
0 | WUR Beacon
1 | WUR Wake-up
2 | WUR Vendor specific
3 | WUR Discovery
4 | WUR Short Wake-up
5-7 | Reserved

## Slide 17: 802 Reference model [6]
MAC data type frame header
(30 octets)
LLC header
(8 octets)
TCP/UDP header
(8 octets)
IP header
(40 octets)

## Slide 18: Layer Protocols
Transport layer
Provides the means for transmitting data between the two connected parties, as well as controlling the quality of service. The main protocols used here are TCP and UDP
Network layer
Handles the routing and sending of data between different networks. The most important protocols at this layer are IP (IPV4, IPV6).
5.2.2 LLC (logical link control) sublayer [6]
The higher layer protocol discrimination entity (HLPDE) is used by the LLC sublayer to determine the higher layer protocol to which to deliver an LLC sublayer protocol data unit (PDU).
5.2.3 MAC (media access control) sublayer [6]
The MAC sublayer performs the functions necessary to provide frame-based, connectionless-mode‌ﾠ(datagram style) data transfer between stations in support of the next higher sublayer, as described in 5.1, for networks that support it. In some MAC types, some MAC frames are used in support of the MAC sublayer functionality itself, rather than for transfer of data from the next higher sublayer.

## Slide 19: MAC data frame overhead [4]

## Slide 20: Networking overhead
Protocol layer/ sublayer | Header + trailer size | 
 | Octet | Bit
MAC (PV0/PV1) | 30/18 | 240/144
Addition of Encrypted MAC frame | 24 | 192
LLC | 8 | 64
IPv6 | 40 | 320
UDP | 8 | 64
Total | 110/98 | 880/784
Maximum payload size for AMP use cases = 256 bit [2]

## Slide 21: Recommendation 1
The data frame overhead for directly delivering AMP-only IoT STA information to the network is three times the maximum AMP payload.
To meet AMP-only IoT STA constraints (power, etc.), we propose to provide a solution that does not require AMP-only IoT STA delivering data type frames to the network.

## Slide 22: Frame formats other than the data type frame format
The base specification [4] uses three approaches to define frames (1, 2, 3)
# | PV | Pros | Cons | Comment
1 | 0 |  | The first three fields Frame Control(16bit), Duration/ID(16bit), and Address 1(48bit) and the last field (FCS) (32bit) are present in all these frames, including reserved types and subtypes. (112bit) | Not all fields are required for AMP-only IoT STA. Fields that can be used for AMP-only IoT STA may be shorter. .
2 | 1 |  | The first three fields Frame Control (16bit), A1(16bit) and A2 (16bit) and the last field FCS (32bit) are always present in PV1 frames (80bit) | 
3 | NA | The shortest frame is 48 bit long |  | 9.9 MAC frame format for WUR frames WUR PHY-dependent MAC frame format, three types are reserved and can be used for AMP-only IoT communication
4 | NA | Frame formats optimized for AMP-only IoT | Requires AMP IoT specific PPDU definition (PHY) | PHY isolated MAC Frame formats

## Slide 23: Recommendation 2
Using PV0 and PV1 frame formats different from the data type frame format still results in significant overhead when used for communication with AMP-only IoT STAs.
  Shorter frame control and FCS fields, as well as using only one identifier field, may be beneficial to save transmit power.
Options 3 and 4 are the frame formats most suitable for communicating with AMP-only IoT STA, while still providing greater flexibility to construct optimal frame formats
  NOTE1: The PPDU format allows legacy STA to ignore AMP-only IoT PPDUs and not erroneously decode the PPDU payload.
  NOTE2: See [8] for an example of using optimized .11bp frame formats other than the data type frame format for communicating with an AMP-only IoT STA.

## Slide 24: Summary
To meet the requirements of AMP-only IoT STA, we propose the following:
  The AMP-only IoT STA communicates with the AMP-capable STA.
  AMP-capable STA supports network protocols above the MAC layer to transmit information received from the AMP-only IoT STA to the network and vice versa. Thus, frames used to communicate with AMP-only IoT STA contain less overhead by not transmitting network protocol headers above the MAC layer.
  Communication between AMP-only IoT STA and AMP-capable STA is unassociated. Thus, there is no need to consume energy to communicate long management frames to establish the association and retain the association state information in the memory

## Slide 25: References
11-23-0436-00-0amp-technical-report-on-support-of-amp-iot-devices-in-wlan
11-23-1005-00-0amp-discussion-on-requirements-for-amp-use-cases
ISO/IEC 18000-63:2021(E)
IEEE P802.11-REVme/D6.0, June 2024
IEEE P802.11bf/D4.0, April 2024
IEEE Std 802®-2014 Standard for Local and Metropolitan Area Networks: Overview and Architecture
ISO/IEC 7498-1:1994 Open Systems Interconnection basic reference model (OSI/RM)
11-24-1180-02-00bp-reference-model-of-amp-only-iot-devices

## Slide 26: Straw Poll
SP#1
Do you agree that the amendment will define an “AMP-capable STA” (name TBD)?
  AMP-only STAs communicate only with AMP-capable STAs
  The AMP-capable STA provides access to the DS for the AMP-only STA
Note: the AMP-capable STA may be part of an access point.
Yes
No
Abstain

## Slide 27: Straw Poll
SP#2
Do you agree that the amendment will define communication with AMP-only IoT STA through optimized .11bp frames?
Yes
No
Abstain

## Slide 28: Straw Poll
SP#3
Do you agree that the amendment will define communication with unassociated AMP-only IoT STA?
Yes
No
Abstain

## Slide 29: Straw Poll
SP#4
Do you agree that the amendment will define communication with unassociated AMP-only IoT STA through optimized .11bp frames?
Yes
No
Abstain

## Slide 30: Backup

## Slide 31
Requirements [2]
 | Coverage (dBm) | Maximum payload size (bit) | Peak device power consumption (mWatts) | Device density (per m2) | Horizontal Positioning accuracy (m) | Peak data rate (Kbps) | Others
UC1: Smart Manufacturing | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC2: Data Centre | Type1: -30 Type2: -82 | 256 | 1 | 3 | 1-3 | 51.2 kbps | 
UC3: Smart Home | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC4: Logistics and Warehouse | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC5: Smart Agriculture | Type1: -30 Type2: -82 | 256 | 1 | 1 | 10 | 51.2 kbps | 
UC6: Indoor Positioning | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC7: Smart Power Grid | Type1: -30 Type2: -82 | 256 | 1 | 10-2 | 10 | 51.2 kbps | 
UC8: Fresh Food Supply Chain | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
Note 1: Coverage is calculated based on AWGN Channel Note 2: Type 1: RF powered AMP device; Type 2: non-RF powered AMP device, e.g., thermal, solar, etc. Note 3: Others include requirements only applicable to a subset of use cases |  |  |  |  |  |  |