## Slide 1: Power Imbalance Issue Analysis for DRU
Date: 2024-09-05
Authors:
Name | Affiliations | Address | Phone | Email
Bo Gong | Huawei |  |  | gongbo8@huawei.com
Jian Yu (Ross) |  |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com

## Slide 2: Background
Sep 2024
In [1], several motions related to STF transmission for DRU have been passed. They illustrate that the STF for DRU is transmitted over the whole distribution bandwidth and uses a triggered based STF sequence.
In this proposal, we analyze the power imbalance issue between STF and Data and propose to use different transmission modes for different DRU sizes.

## Slide 3: Power Imbalance Issue
For 6GHz LPI scenario, denote the maximum power per MHz as P;
For trigger based STF sequence, since the tone space is 8, the maximum per tone power is P/2;
For trigger based STF sequence, there are 30 tones for 20M BW, 60 tones for 40M BW, 124 tones for 80M BW and 248 tones for 160M BW.
BW | DRU Size | Maximum tones per MHz | Maximum power for Data Field | Maximum power for STF of TB PPDU
20M | 26 | 2 | P/2*26 = 13P | P/2*30 = 15P
20M | 52 | 3 | P/3*52 = 17.33P | P/2*30 = 15P
20M | 106 | 6 | P/6*106 = 17.67P | P/2*30 = 15P
40M | 26 | 1 | P*26 = 26P | P/2*60 = 30P
40M | 52 | 2 | P/2*52 = 26P | P/2*60 = 30P
40M | 106 | 3 | P/3*106 = 35.33P | P/2*60 = 30P
40M | 242 | 7 | P/7*242 = 34.57P | P/2*60 = 30P
BW | DRU Size | Maximum tones per MHz | Maximum power for Data Field | Maximum power for STF of TB PPDU
80M | 52 | 1 | P*52 = 52P | P/2*124 = 62P
80M | 106 | 2 | P/2*106 = 53P | P/2*124 = 62P
80M | 242 | 4 | P/4*242 = 60.5P | P/2*124 = 62P
80M | 484 | 7 | P/7*484 = 69.14P | P/2*124 = 62P
160M | 106 | 1 | P*106 = 106P | P/2*248 = 124P
160M | 242 | 2 | P/2*242 = 121P | P/2*248 = 124P
160M | 484 | 4 | P/4*484 = 121P | P/2*248 = 124P
160M | 996 | 7 | P/7*996 = 142.29P | P/2*248 = 124P
Sep 2024

## Slide 4: Proposed Solution
In the above tables, the values labeled in red represent power imbalance, which means the maximum power of STF is lower than the maximum power of Data. Thus, two transmission modes are proposed for DRU.
Transmission mode-1: For a 26-tone DRU in a 20MHz DBW, a 26/52-tone DRU in a 40MHz DBW, a 52/106/242-tone DRU in an 80MHz DBW, and a 106/242/484-tone DRU in a 160MHz DBW, the transmit power of STF and Data are the same.
Transmission mode-2: For a 52/106-tone DRU in a 20MHz DBW, a 106/242-tone DRU in a 40MHz DBW, a 484-tone DRU in an 80MHz DBW, and a 996-tone DRU in a 160MHz DBW, there exist two options for the transmit power of STF and Data.
  Opt1: The transmit power of STF and Data shall be the same.
  Opt2: The transmit power of STF and Data could be different.
Sep 2024

## Slide 5: Summary
Sep 2024
In this proposal, we analyze the power imbalance issue for DRU STF and Data. Then propose two transmission modes for different DRU sizes.

## Slide 6: References
[1] 11-24-0209-02-00bn-specification-framework-for-tgbn
Sep 2024

## Slide 7: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
- For a 26-tone DRU in a 20MHz DBW, a 26/52-tone DRU in a 40MHz DBW, a 52/106/242-tone DRU in an 80MHz DBW, and a 106/242/484-tone DRU in a 160MHz DBW, the transmit power of STF and Data in UHR TB PPDU are the same.
Y/N/A: //
Sep 2024

## Slide 8: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
- For a 52/106-tone DRU in a 20MHz DBW, a 106/242-tone DRU in a 40MHz DBW, a 484-tone DRU in an 80MHz DBW, and a 996-tone DRU in a 160MHz DBW, the transmit power of STF and Data in UHR TB PPDU
    Option-1: shall be the same.
    Option-2: could be different.
    Option-3: abstain.
Y/N/A: //
Sep 2024