## Slide 1: In-device Coexistence Follow Up
Date: 2024-09-08
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: ICF and ICR
In [1], the requirement of ICF is discussed and various options for ICF are mentioned.
In [2], the unified ICR is proposed for both DL and UL.
In [3], BSRP Trigger is proposed as ICF to solicit TB PPDU to carry ICRs

## Slide 3: BSRP Trigger as ICF 1
As the first frame exchange of a TXOP, the frame exchange of BSRP Trigger and Multi-STA BA should provide the similar TXOP protection as (MU-)RTS + CTS.
Based on such observation, the spec should allow that when an AP transmits BSRP Trigger as ICF to a single STA, the BSRP Trigger can solicit non-HT duplicate PPDU.
  With such PPDU selection, the TXOP protection per Duration in MAC header is provided.
  The CS Required allows the similar behavior when the TXOP responder decides whether it can transmit the responding Multi-STA BA.

## Slide 4: BSRP Trigger as ICF 2
Similar to ICR selection, when a non-AP STA solicits the available information and unavailable information for P2P, the BSRP Trigger can be used to solicit Multi-STA BA.

## Slide 5: UL Common Info Consideration
The Common Info is carried in ICF when soliciting non-TB PPDU:
  The Common Info carries CS Required that is useful if the TXOP holder would like the TXOP protection similar to RTS/CTS.
  The Common Info carries the BW Information that needs to be used by the addressed AP to decide the responding PPDU BW.
  The Responding PPDU Type can be acquired through repurposing the current reserved bits in EHT variant Common Info field.
  The Common Info can carry the security related information (Key ID, Protection Indication) when the ICF needs to be protected.
  In the future, the explicit indication of solicited feedback can be carried in Common Info field.

## Slide 6: Special User Info field
The Special User Info field is carried in ICF when soliciting non-TB PPDU and the BW is wider than 320MHz

## Slide 7: User Info field
User Info field for a STA being used to allocate RU etc. to the STA is not needed.

## Slide 8: Summary
The BSRP Trigger frame as ICF is discussed:
  BSRP Trigger addressed to a single recipient can solicit non-HT duplicate PPDU.
  The PPDU format of non-HT duplicate PPDU is explicitly indicated in BSRP Trigger frame addressed to a recipient.
  The format of BARP Trigger soliciting a non-HT duplicate PPDU is defined.

## Slide 9: SP 1
Do you support to amend the SP as follows:
Do you support to use BSRP Trigger frame as a UHR Initial Control frame (ICF) sent:
  From an AP for soliciting response in TB PPDU format from one or more scheduled STAs, and to allow an M-BA frame to be included in the TB PPDU sent by the UHR scheduled STAs in response, when carrying feedback (i.e. unavailability) information or when the response is protected
    BSRP Trigger frame follows baseline rules for the format of the solicited TB-PPDU
  From an AP for soliciting an M-BA response in non-HT (duplicate) PPDU format from one non-AP STA, when the M-BA is expected to carry feedback (i.e., unavailability) information or when the response is protected.

## Slide 10: Reference
[1] 11-24/0494 in device coexistence follow up
[2] 11-24/0857 ICR consideration
[3] 11-24/1226 ICF ICR design