## Slide 1: Harmonization of .11bn simulation assumptions
Date: 2024-09-06
Authors:
Name | Affiliation | Address | Phone | Email
Klaus Doppler | Nokia |  |  | Klaus.doppler@nokia.com
Behnam Dezfouli |  |  |  | 
Mika Kasslin |  |  |  | 
Salvatore Talarico |  |  |  | 
Enrico Rantala |  |  |  | 

## Slide 2: Introduction
Simulation topology in .11bn is often the following 2 APs scenario, e.g. [1]
  Distance(D) between APs is X meters/; Radius(R) of the cell is D * 0.33
  N STAs are dropped randomly within the cell for each BSS.
Such a simulation topology is likely too simple to capture all the interactions between BSSs when evaluating e.g. TXOP sharing, TXOP preemption or c-TDMA, c-TWT.
In this contribution we will review the simulation scenarios proposed in .11ax and make suggestions for .11bn for simulations related to multi-AP coordination techniques like TXOP sharing, TXOP preemption, CBF, and c-TDMA, c-TWT
We don’t need to specify the topology as done in .11ax, but we firmly believe that performing simulations in different setups is beneficial also for TGbn
AP2
AP1
R
D

## Slide 3: .11ax Residential Scenario [2]
Environment description | Multi-floor building 100 Appartments Apartment size:10m x 10m x 3m
APs location | In each apartment, place AP in random xy-locations (uniform distribution) at z = 1.5 m above the floor level of the apartment.
STAs location | In each apartment, place STAs in random xy-locations (uniform distribution) at z = 1.5m above the floor level of the apartment
Channel Model And Penetration Losses | Fading model TGac channel model D NLOS for all the links.
 | Pathloss model PL(d) = 40.05 + 20*log10(fc/2.4) + 20*log10(min(d,5)) + (d>5) * 35*log10(d/5) + 18.3*F^((F+2)/(F+1)-0.46) + 5*W d = max(3D distance [m], 1) fc = frequency [GHz] F = number of floors traversed W = number of walls traversed in x-direction plus number of walls traversed in y-direction
 | Shadowing Log-normal with 5 dB standard deviation, iid across all links

## Slide 4: .11ax Enterprise Scenario [2]
Topology
  Single floor office building,
    8 offices: 4 APs per office i.e. 32 APs
    64 cubicles per office
    Each cubicle has 4 STAs so 8*64*4 = 2048 STAs
8 offices
1 Office = 64 cubicles
1 Cubicle = 4 STAs

## Slide 5: .11ax Enterprise Scenario
Channel allocation: 5GHz
  Four 80MHz channels (Ch1 to Ch4)
Four 80MHz channels
AP
Channel
1
2
3
4

## Slide 6: Considerations on Number of STAs and APs
We don’t need to specify the topology as done in .11ax, but we must consider feature performance in networks of different size and type
Simulations should show how the proposed feature works in networks from 2 APs up to e.g., 8 or 32 APs
Similarly, simulations should show how the proposed feature copes when the number of connected STAs per AP increases from 2 up to e.g., 20 or 50
Do you agree that networks of different sizes should be considered when evaluating the proposed features?

## Slide 7: Considerations on Traffic Models
We want to see that LL traffic can be delivered efficiently in the presence of broadband traffic, e.g.
  Uplink/downlink broadband traffic—modeled as a file transfer protocol (FTP) service—, and
  Uplink/downlink low-latency traffic—modeled as an application with support for both periodic and aperiodic packet generation
Do you agree that both broadband traffic and both periodic and aperiodic LL traffic should be considered in the simulations?
Broadband (BB) FTP3 model [A]
File size = 0.5 MBytes
Offered traffic = 100 Mbps
Latency-sensitive (LS) model [B]
File size = 32 bytes
Constant arrival rate, frequency = 10 ms (periodic/B.1)
Random arrival rate (aperiodic/B.2)
time
Per STA traffic
time
Per STA traffic

## Slide 8: Considerations on Mapping Traffic to STAs
We want to see how the proposed feature peform with different traffic type combinations in combination with networks of different types and size
  LL/BB traffic ratio in the network from e.g., 10 % up to 60 %
  From fully dedicated LL/BB STAs to a mixture of STAs which have both the traffic types active
Do you agree that different traffic mix should be analyzed in simulating the proposed features?

## Slide 9: Considerations on Baseline and KPIs
We want to show how the proposed feature performs in comparison to a “baseline”
  Default baseline is network performance without the proposed feature but otherwise with the same setup in terms of network size, channelization, operating parameters, etc.
  Additional results can be provided to show how the proposed feature performs in comparison with “competing” features targeted for same purpose
In many cases, we want to see that LL traffic (periodic/aperiodic) can be delivered efficiently even with broadband traffic present
  Relevant KPIs include delay distribution, network throughput, etc.
Do you agree that comparison between feature-on and feature-off scenarios is beneficial? (1)
Do you agree that evaluations should have as KPIs at least the delay distribution and the network throughput? In addition, a per STA UL and DL throughput would give even further insights (2)

## Slide 10: Other considerations
Even if we are not after a commonly agreed simulation scenario with all the details fixed, it would be beneficial to use some common basics like
  Channel model and AP/STA deployment, e.g., using the ones defined and used .11ac and .11ax
  Other parameters like number of antennas, transmit power, mobility, etc.

## Slide 11: Summary
We would like to see TGbn contributors to consider providing simulation results which
  Indicate how the proposed feature performs in networks of different type and size
  Indicate how different types of LL traffic is delivered in presence of broadband traffic
  Indicate how the proposed feature performs with different combinations of traffic-to-STAs mapping
  Provide basic common KPIs including delay distribution and throughput
  Build upon common basics like channel model

## Slide 12: References
[1] Kosuke Aio et.al., “System-Level Evaluation of Coordinated Spatial Reuse,” 24/0839r1, May 2024.
[2] Ron Borat et.al., “11ax Evaluation Methodology,” 14/0571r12, Jan 2016