## Slide 1: Harmonization of .11bn simulation assumptions
Date: 2024-09-06
Authors:
Name | Affiliation | Address | Phone | Email
Klaus Doppler | Nokia |  |  | Klaus.doppler@nokia.com
Behnam Dezfouli |  |  |  | 
Mika Kasslin |  |  |  | 
Salvatore Talarico |  |  |  | 
Enrico Rantala |  |  |  | 
Kerstin Johnsson |  |  |  | 

## Slide 2: Introduction
Simulation topology in .11bn is often the 2 APs scenario, e.g. [1], where
  D is distance between APs
  R = 0.33D is radius of the cell
  N STAs are dropped randomly within each cell
This topology is likely too simple to capture all relevant interactions among BSSs when evaluating TXOP sharing, TXOP preemption, CBF, c-TDMA, c-rTWT.
In this contribution, we will review .11ax simulation scenarios and make suggestions for the evaluation of multi-AP coordination techniques proposed for .11bn.
We are not proposing the creation of an official evaluation methodology, but rather seek consensus on the general need for certain simulation features to accurately evaluate new concepts.
AP2
AP1
R
D

## Slide 3: .11ax Residential Scenario [2]
Environment description | Multi-floor building with 100 apartments Each apartment is 10m x 10m x 3m
APs location | In each apartment, place AP in random xy-locations (uniform distribution) at z = 1.5 m above the floor level of the apartment.
STAs location | In each apartment, place STAs in random xy-locations (uniform distribution) at z = 1.5m above the floor level of the apartment
Channel Model and Penetration Losses | Fading model TGac channel model D NLOS for all the links.
 | Pathloss model PL(d) = 40.05 + 20*log10(fc/2.4) + 20*log10(min(d,5)) + (d>5) * 35*log10(d/5) + 18.3*F^((F+2)/(F+1)-0.46) + 5*W d = max(3D distance [m], 1) fc = frequency [GHz] F = number of floors traversed W = number of walls traversed in x-direction plus number of walls traversed in y-direction
 | Shadowing Log-normal with 5 dB standard deviation, iid across all links

## Slide 4: .11ax Enterprise Scenario [2]
Topology
  Single floor office building,
    8 offices: 4 APs per office i.e. 32 APs
    64 cubicles per office
    Each cubicle has 4 STAs so 8*64*4 = 2048 STAs
8 offices
1 Office = 64 cubicles
1 Cubicle = 4 STAs

## Slide 5: .11ax Enterprise Scenario
Channel allocation: 5GHz
  Four 80MHz channels (Ch1 to Ch4)
Four 80MHz channels
AP
Channel
1
2
3
4

## Slide 6: Considerations on Number of STAs and APs
We propose that simulations should show how the proposed feature works in networks from 2 APs up to e.g., 8 or 32 APs
Similarly, simulations should show how the proposed feature copes when the number of connected STAs per AP increases from 2 up to e.g., 20 or 50
Do you agree that networks of different sizes should be considered when evaluating the proposed features?

## Slide 7: Considerations on Traffic Models
We want to see that LL traffic can be delivered efficiently in the presence of broadband traffic, e.g.
  Uplink/downlink broadband traffic—modeled as a file transfer protocol (FTP) service—, and
  Uplink/downlink low-latency traffic—modeled as an application with support for both periodic and aperiodic packet generation
Do you agree that both broadband traffic and both periodic and aperiodic LL traffic should be considered in the simulations?
Broadband (BB) FTP3 model [A]
File size = 0.5 MBytes
Offered traffic = 100 Mbps
Latency-sensitive (LS) model [B]
File size = 32 bytes
Constant arrival rate, frequency = 10 ms (periodic/B.1)
Random arrival rate (aperiodic/B.2)
time
Per STA traffic
time
Per STA traffic

## Slide 8: Considerations on Mapping Traffic to STAs
We want to see how the proposed feature peform with different traffic type combinations in combination with networks of different types and size
  LL/BB traffic ratio in the network from e.g., 10 % up to 60 %
  From fully dedicated LL/BB STAs to a mixture of STAs which have both the traffic types active
Do you agree that different traffic mix should be analyzed in simulating the proposed features?

## Slide 9: Considerations on Baseline and KPIs
We want to show how the proposed feature performs in comparison to a “baseline”
  Default baseline is network performance without the proposed feature but otherwise with the same setup in terms of network size, channelization, operating parameters, etc.
  Additional results can be provided to show how the proposed feature performs in comparison with “competing” features targeted for same purpose
In many cases, we want to see that LL traffic (periodic/aperiodic) can be delivered efficiently even with broadband traffic present
  Relevant KPIs include delay distribution, network throughput, etc.
Do you agree that comparison between feature-on and feature-off scenarios is beneficial? (1)
Do you agree that evaluations should have as KPIs at least the delay distribution and the network throughput? In addition, a per STA UL and DL throughput would give even further insights (2)

## Slide 10: Other considerations
Even if we are not after a commonly agreed simulation scenario with all the details fixed, it would be beneficial to use some common basics like
  Channel model and AP/STA deployment, e.g., using the ones defined and used .11ac and .11ax
  Other parameters like number of antennas, transmit power, mobility, etc.

## Slide 11: Summary
We would like to see TGbn contributors to consider providing simulation results which
  Indicate how the proposed feature performs in networks of different type and size
  Indicate how different types of LL traffic is delivered in presence of broadband traffic
  Indicate how the proposed feature performs with different combinations of traffic-to-STAs mapping
  Provide basic common KPIs including delay distribution and throughput
  Build upon common basics like channel model

## Slide 12: References
[1] Kosuke Aio et.al., “System-Level Evaluation of Coordinated Spatial Reuse,” 24/0839r1, May 2024.
[2] Ron Borat et.al., “11ax Evaluation Methodology,” 14/0571r12, Jan 2016