## Slide 1: Guard Interval Coordination for Coordinated Beamforming
Date: 2024-09-09
Authors:

## Slide 2: Abstract
In this contribution, we discuss the guard interval (GI) used for coordinated beamforming (CBF) and propose some methods of GI coordination for the CBF.

## Slide 3: Background
TGbn defines multi-AP Coordinated Beamforming (CBF) [1].
CBF aspects
  Inter-BSS/OBSS coordination set establishment and maintenance
  CSI acquisition from devices both in own and inter-BSS/OBSS
  Allocation and communication of nulling capabilities to enable concurrent transmissions without power reduction

## Slide 4: Background
EHT MU PPDU and EHT TB PPDU define different guard intervals (GIs), e.g., 0.8 μs, 1.6 μs, and 3.2 μs, for 1×, 2×, and 4× EHT-LTF and Data fields.
  Determining the GI duration required for a transmission may be based on various factors (e.g., DFT size, delay spread of CSI, and the MCS order).
Example: AP1 transmits PPDU1 (e.g., with transmit beamforming TxBF) using GI1 (e.g., 0.8 μs) for STA1 and PPDU2 (e.g., w/TxBF) using GI2 (e.g., 3.2 μs) for STA2, respectively.

## Slide 5: CBF using Individual GIs
In a multi-AP group (or AP candidate set), AP1 is a sharing AP, and AP2 is a shared AP.
AP1 and AP2 can perform multi-AP sounding to obtain CSI or beamforming feedback based on estimation by STA1 associated with and STA2 associated with AP2.
AP1 and AP2 can respectively prepare beamforming steering/nulling matrix to perform CBF with STA1 and STA2.
AP1 and AP2 respectively apply GI1 (e.g., 0.8 μs) to PPDU1 and GI2 (e.g., 3.2 μs) to PPDU2 carrying data frames for concurrent transmissions to STA1 and STA2.
However, different lengths of GIs, i.e., GI duration, in PPDUs may cause issue in PPDU-level synchronization during the concurrent transmission.

## Slide 6: CBF using Uncoordinated GIs
A sharing (e.g., AP1) sends to a shared AP (e.g., AP2) a trigger frame (e.g. MAP trigger) to initiate a MAP transmission. The trigger frame indicates a GI duration to be used by the sharing AP and AP2 for DL transmission to STA1 and STA2.
AP1 chooses the GI duration or the GI type based on local information of AP1. AP1 further decides the GI indicated in the trigger frame based on a GI duration required for transmitting a data frame to STA1.
AP1 and AP2 concurrently send PPDU1 and PPDU2 for data transmissions using the GI indicated in the MAP trigger frame.
However, as the selected GI indicated in the trigger frame is shorter than required to transmit/receive the data frame transmitted by AP2, STA2 experiences inter-symbol interference (ISI) while receiving the PPDU2 from AP2.

## Slide 7: CBF using Coordinated GI
A sharing AP (e.g., AP1) and a shared AP (e.g., AP2), within a multi-AP group, may broadcast beacon frames exchanging capability information of supporting GI coordination.
After multi-AP sounding, AP2 transmits to AP1 a frame (e.g., notification) indicating a GI1 that AP2 intends to use for a data transmission to STA2 during a TXOP of AP1.
  Alternatively, AP1 transmits to AP2 a frame (e.g., request) soliciting the GI1 that AP2 intends to use.
AP1 transmits to AP2 a trigger frame (e.g., MAP trigger) indicating a GI2 for the data transmission of PPDU2 to STA2, where the GI2 is based on the GI1.
Both AP1 and AP2 apply the GI2 to PPDU1 for the data transmission to STA1 and PPDU2 for the data transmission to STA2, respectively.

## Slide 8: Summary
In this contribution, we shared some thoughts of GI coordination for CBF.

## Slide 9: References
11-24/0209, Specification Framework for TGbn
11-24/0880, CBF Recap and Way Forward, Okan Mutgan (Nokia)
11-24/0142, Residual Interference in CBF, Dana Ciochina (Sony)
11-24/1204, Coordinated Beamforming for 11bn, Insik Jung (LGE)
11-24/1211, Coordinated BF Goodput Discussion, Genadiy Tsodik (Huawei)
11-24/0010, Coordinated Beamforming for 802.11bn, Okan Mutgan (Nokia)
11-24/0444, Considerations on Joint Transmission, Kazunobu Serizawa (ATR)
11-23/1843, Multi-AP Joint Transmission Simulations with Impairments, (Maxlinear Inc)
11-24/1092, Multi-AP Coordinated Concurrent Transmission Protocol, Kosuke Aio (Sony)
11-24/0454, Multi-AP Sounding, Xiaofei WANG (InterDigital)
11-23/0084, Considerations on Multi-AP Operation - Follow Up, Jiayi Zhang (Ofinno)
11-23/2009, Multi-AP for reliability with Coherent and Non-coherent transmissions, Yanchun Li (Huawei)
11-20/0099, Coordinated Beamforming for 802.11be, Roya Doostnejad (intel)
11-19/1594, Coordinated Beamforming/Null Steering Protocol in 802.11be, David Lopez-Perez (Nokia)
11-19/0638, Nulling and coordinated beamforming, Sigurd Schelstraete (Quantenna)