## Slide 1: Non-Primary Channel Access During R-TWT Coordination
Date: 2024-11-11
Authors:

## Slide 2: Abstract
R-TWT Coordination is a candidate feature for improving the network performance of multiple BSSs in terms of latency.
In R-TWT coordination, APs and/or STAs may need to terminate their TXOPs prior to the start of an R-TWT service period scheduled by an OBSS AP.
In [1], the authors addressed the issue of overprotection of OBSS R-TWT SPs by reducing TXOP terminations for OBSS R-TWT SPs.
In this contribution, we provide further considerations regarding overprotection of OBSS R-TWT SPs in regard to NPCA.

## Slide 3: Non Primary Channel Access
NPCA allows transmissions in the secondary channel even if the primary channel is busy. If the designated secondary channel(s) are available (also called the NPCA channel), an AP/STA transmits on the available secondary channel(s)
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
time
20MHz PPDU
(interference, OBSS)
80MHz PPDU
Busy
Busy
frequency
40MHz PPDU
(interference, OBSS)
(STA to AP or AP to STA)
STA can transmit a packet on the secondary channels while the primary channel is busy
60MHz PPDU
40MHz PPDU

## Slide 4: R-TWT SPs
AP 1
AP 2
Frame
R-TWT SP 1
R-TWT SP 1
AP1 Frame exchanges
AP2 Frame exchanges
TGbn may support R-TWT schedule coordination between APs. There may be multiple levels of coordination:
In the most restrictive case, one coordinating AP (e.g. AP 1) and STAs associated to the coordinating AP end their TXOP at the SP (e.g. R-TWT SP1) start boundary as if the R-TWT SP is scheduled by the coordinating AP.
In a less restrictive case, only APs (e.g. AP 1) end their TXOP at the SP start boundary.

## Slide 5: NPCA at the R-TWT Start Boundary
When an OBSS transmission is detected by AP1 near the start of a coordinated R-TWT, AP 1 may want to terminate the TXOP in the NPCA primary channel. This gives the frame exchange by AP 2 in the R-TWT SP better protection. For example, if the bandwidth of the frame exchange includes the NPCA channel.
AP 2
AP 1
NPCA PCH (AP1)
PCH
PCH
R-TWT SP 1
AP2 Frame exchanges
AP1 Frame exchanges
OBSS Tx
NPCA PCH (AP 1)
Frame
R-TWT SP 1

## Slide 6: Overprotection of R-TWT SP
However, in some cases terminating the NPCA TXOP during a coordinated R-TWT SP may be unnecessary. For example, if the AP 2 frame exchange does not use the NPCA channel. Another example, is if AP 2 hears the same OBSS transmission, AP 2 will only be able to transmit after the OBSS transmission. In both cases, there is no need to terminate the NPCA TXOP.
AP 2
AP 1
PCH
PCH
R-TWT SP 1
AP2 Frame exchanges
AP1 Frame exchanges
OBSS Tx
Unused
NPCA PCH (AP1)
NPCA PCH (AP 1)
Frame
R-TWT SP 1

## Slide 7: Proposal
One possible solution is to include the bandwidth of frame exchanges to be done in a coordinated R-TWT SP. An AP may set the NPCA channel not to overlap with the coordinated R-TWT SP bandwidth. An AP may then continue its NPCA TXOP without termination at the coordinated R-TWT SP boundary.
AP 2
AP 1
NPCA CH
PCH
PCH
R-TWT SP 1
AP2 Frame exchanges
AP1 Frame exchanges
OBSS Tx
NPCA CH
frame
R-TWT SP 1
Bandwidth

## Slide 8: Discussion
An AP receiving a request for R-TWT SP coordination may accept or reject the request based on the requested R-TWT SP protection bandwidth.
Another possible (and simpler) solution is to make an exception for NPCA TXOPs not to terminate the TXOP during coordinated R-TWT SP.
- Equivalent to a R-TWT SP protection bandwidth of 20 MHz.

## Slide 9: DSO at the R-TWT Start Boundary
The same idea can be applied for DSO at the R-TWT start boundary.
AP 2
AP 1
SCH
PCH
PCH
R-TWT SP 1
AP2 Frame exchanges
AP1 Frame exchanges
SCH
frame
R-TWT SP 1
Bandwidth
ICF
ICF
ICR
AP1 Frame
exchanges (cont)

## Slide 10: Conclusion
NPCA TXOPs may be subject to TXOP termination during R-TWT SP start boundaries.
We showed that in some cases, TXOP termination may be unnecessary.
We proposed to signal a protection bandwidth for coordinated R-TWT SPs for APs to know whether it may continue its NPCA TXOP at the R-TWT SP start boundary.

## Slide 11: References
https://mentor.ieee.org/802.11/dcn/24/11-24-1206-01-00bn-considerations-on-coordinated-r-twt.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1154-00-00bn-discussion-on-coordination-of-twt.pptx

## Slide 12: Strawpoll
Do you agree to include in the 11bn SFD
TGb shall define a mechanism for a STA/AP to continue a TXOP obtained in the NPCA primary channel during a start of a coordinated R-TWT SP.