## Slide 1: Reducing CSD Collisions for DRU STF
Date: 2024-10-17
Authors:

## Slide 2: Abstract
802.11bn has recently adopted 11ax/11be trigger based STF sequences for DRUs (i.e. STF for DRU PPDU uses RRU tones)
In order to prevent unintentional beamforming, 11bn also adopted the use of global CSD for the UHR-STF.
When there are at least 4 users each with 2 spatial streams, CSD collisions is unavoidable for additional users using the current procedures.
In this contribution, we propose a technique to reduce CSD collisions when multiple STAs transmit multiple spatial streams.

## Slide 3: CSD Collisions
In the TGbn SFD [1],
  Global CSD is used for DRU UHR-STF transmission to solve unintentional beamforming issue
  DRU transmission reuses the 8 CSD table/values in 11ax/be for global CSD allocation
A STA can transmit up to 2 spatial streams in a TB PPDU when using DRU [2].
This means that 4 STAs each with 2 spatial streams use up the entire CSD table. Additional users will bring unintentional beamforming.
  This may cause inaccurate AGC setting, and hence lower performance for DRU transmissions.

## Slide 4: Proposal
Available RRU Tones
Spatial stream 1
Spatial stream 2
Frequency Domain
Baseline
Proposal
The proposal is to create tone orthogonality for the STF within a single STA by interleaving/splitting the RRU tones of the STF into the number of spatial streams of the transmitted TB PPDU.
  STA uses the entire available tones across the two streams (i.e. no power boost)
Each STA uses a single CSD index regardless of transmitting 1 or 2 spatial streams.
  Frees up the CSD index used by the second spatial stream for use exclusively by other STAs.
Spatial stream 1
Spatial stream 2

## Slide 5: Simulations (2 Users)
Distribution Bandwidth = 80 MHz
Channel – Channel D-NLOS, 30 dB SNR
User 1 – 2SS, 52-tone DRU
User 2 – 1SS, 52-tone DRU
Case 1: CSD Collision (2 CSDs)
Case 2: No Collision (3 CSDs)
Case 3: No Collision (2 CSDs w/ split)

## Slide 6: Simulations (3 Users)
Distribution Bandwidth = 80 MHz
Channel – Channel D-NLOS, 30 dB SNR
User 1 – 2SS, 52-tone DRU
User 2 – 1SS, 52-tone DRU
User 3 – 1SS, 52-tone DRU
Case 1: CSD Collision (3 CSDs)
Case 2: No Collision (4 CSDs)
Case 3: No Collision (3 CSDs w/ split)

## Slide 7: Simulations (8 Users)
Distribution Bandwidth = 40 MHz
Channel – Channel D-NLOS, 30 dB SNR
Users 1-8 - 52-Tone DRU
Case 1: CSD Collision, 8 users x 2ss
Case 2: No Collision, 8 users x 1ss
Case 3: No Collision, 8 users x 2ss + split

## Slide 8: Simulations (8 Users)
Distribution Bandwidth = 40 MHz
Channel – Channel B-LOS, 30 dB SNR
Users 1-8 - 52-Tone DRU
Case 1: CSD Collision, 8 users x 2ss
Case 2: No Collision, 8 users x 1ss
Case 3: No Collision, 8 users x 2ss + split

## Slide 9: Discussions
Based on simulations, the power estimation performance with splitting for UHR-STF is very similar compared to the case without CSD collisions.
With splitting, an AP can schedule up to 8 STAs without CSD collisions regardless of the number of spatial streams per user.
In terms of complexity, the proposal requires very little changes.
- no changes in DRU/RRU tone plans.
- no changes in the AP TB PPDU decode procedure.
- may not need any signaling if all STAs are configured to split the DRU UHR-STF tones.

## Slide 10: Conclusion
We have introduced splitting of DRU UHR STF tones as a way to reduce CSD collisions for DRU UHR STF.
- eliminates CSD collisions occurring when one or more STAs transmit multiple spatial streams.
We showed that with splitting, the AP power estimation performance is near the case when no CSD collision occurs without any changes to the AP’s decoding procedure.

## Slide 11: References
[1] https://mentor.ieee.org/802.11/dcn/24/11-24-0209-04-00bn-specification-framework-for-tgbn.docx
[2] https://mentor.ieee.org/802.11/dcn/24/11-24-0171-15-00bn-tgbn-motions-list-part-1.pptx

## Slide 12: Strawpoll
Do you agree to include the following into the 11bn SFD?
11bn defines a mechanism that allows a STA to use one CSD value for the DRU UHR-STF when transmitting two spatial streams. The STA splits the tones of the DRU UHR STF to the two spatial streams.