## Slide 1: Dynamic Subband Operation - Configurations
Date: 2024-09-05
Notes: November 2012

## Slide 2: Overview
This presentation discusses preferred combinations for the following:
Non-APs that can receive DSO allocations in a PPDU.
Operating bandwidths of non-APs that receive DSO allocations in 5GHz and 6GHz.

## Slide 3: Definitions
DSO PPDU: a PPDU that contains DSO allocations. Such a PPDU can additionally contain non-DSO allocations too.
Primary sub-band: For a non-AP, the channel with bandwidth equaling its operating bandwidth and including the BSS primary channel is referred to as primary sub-band.
DSO sub-band: For a non-AP, a channel with the bandwidth equaling its operating bandwidth outside of its primary sub-band where it can be allocated resources by the AP is referred to as DSO sub-band.
DSO STA: A non-AP STA that supports the above DSO mechanism is referred to as a DSO STA.

## Slide 4: Motivation for the proposed DSO configurations (1)
The motivation for the proposed DSO configurations is to simplify the architecture, memory requirements, sounding and scheduling options for DSO.
Simplify AP scheduling by not downgrading a PPDU with DSO allocations from UHR to EHT/HE
⇒ limit PPDUs with DSO allocations to only UHR non-APs.
Enable the following simplifications to the DSO architecture:
  AP doesn’t need to dynamically indicate the DSO sub-band to the non-AP.
  AP doesn’t need to sound a non-AP on multiple bandwidths (DSO sub-bands) outside its operating bandwidth.
  Non-APs don’t have to store channel state information for multiple bandwidths (DSO sub-bands) outside their operating bandwidth.
⇒ A PPDU with DSO allocations can have only one DSO sub-band i.e only one DSO switching position outside its operating bandwidth

## Slide 5: Motivation for the proposed DSO configurations (2)
Notes:
The proposal is only about the operating bandwidth of non-APs that receive DSO allocations.
In a PPDU with DSO allocations, UHR non-APs with any operating bandwidth can have non-DSO allocations on the primary bandwidth.
The proposal does not limit the actual RU allocations in a PPDU with DSO allocations.

## Slide 6: DSO configurations in 5GHz
PPDU bandwidth with DSO allocations: 160 MHz in DL/UL
  Minimum operating bandwidth for a non-AP to receive DSO allocation: 80 MHz
    80S is a DSO sub-band
    80 MHz DSO capable non-APs can switch from 80P to 80S via DSO

## Slide 7: DSO configurations in 6GHz
PPDU bandwidth with DSO allocations: 160 MHz and 320 MHz in DL/UL
  160 MHz PPDU
    Minimum operating bandwidth for a non-AP to receive DSO allocation: 80MHz
      80S is a DSO sub-band. 80 MHz DSO capable non-APs can switch from 80P to 80S via DSO
  320 MHz PPDU
    Minimum operating bandwidth for a non-AP to receive DSO allocation: 80MHz and 160MHz
      160S is a DSO sub-band. 160 MHz DSO capable non-APs can switch from 160P to 160S via DSO
      There is only one 80 MHz DSO sub-band. 80 MHz DSO capable non-APs can switch from 80P to that sub-band.
        TBD if there can be more than one 80 MHz DSO sub-band.

## Slide 8: Straw Poll
SP 1: Do you agree that:
Only 80MHz UHR STAs and 160MHz UHR STAs can be DSO STAs
The DSO ICF-ICR exchange and the PPDUs that follows it shall only be between UHR STAs
One 80MHz subband in 320MHz BSS can be a DSO subband
  Whether more than one 80MHz subband can be a DSO subband in 320MHz BSS is TBD
Secondary 80MHz in 160MHz BSS can be a DSO subband
Secondary 160MHz in 320MHz BSS can be a DSO subband

## Slide 9: Reference
[1] 11-24/0209 Specification framework for TGbn
[2] 11-22/2204 Dynamic Subband Operation
[3] 11-23/2141 Further discussion on Dynamic Subband Operation