## Slide 1: Thoughts on Seamless Roaming and NPCA
Date: 2024-09-04
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Chaoming Luo |  |  |  | luochaoming@oppo.com
Liuming Lu |  |  |  | luliuming@oppo.com
Yapu li |  |  |  | liyapu1@oppo.com
Liangxiao Xin |  |  |  | v-xinliangxiao@oppo.com
Dong Wei |  |  |  | v-dong.wei@oppo.com

## Slide 2: Introduction
Seamless Roaming enables context transfer or data transfer between current AP MLD and target AP MLD so as to make the roaming procedure faster.
NPCA enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other conditions.
In this contribution, we share some thoughts which take the seamless roaming and NPCA into consideration at the same time.

## Slide 3: Problem
Assume a seamless roaming scenario where a target AP MLD and a non-AP MLD are capable of NPCA operation on the same link.
If the non-AP MLD roams when the target AP MLD is currently working on a NPCA primary channel, they may not be able to exchange frames with each other immediately.
Because, non-AP MLD didn’t know which primary channel the target AP MLD is currently working on.
As a result, a delayed roaming-related signaling frame make the seamless roaming less effective in terms of roaming latency. (e.g. Reassociation Req/Rsp frame, RAR frame)

## Slide 4: Potential Solutions
Option 1: Allow NPCA in seamless roaming and sync channel status between non-AP MLD and target AP MLD
  Pros: minimize roaming latency with the help of NPCA.
  Cons: synchronization complexity and channel status expiration.
Option 2: Allow NPCA in seamless roaming but without channel status synchronization
  Pros: reduce roaming latency in some degree.
  Cons: NPCA may not work in some cases.
Option 3: Disallow NPCA in seamless roaming
  Pros: baseline, easy for implementation
  Cons: may result in a large roaming latency especially in a dense deployment environment.

## Slide 5: Summary
Seamless roaming and NPCA are considered together in this contribution.
NPCA may benefit seamless roaming but still faces a problem.
Three potential solutions are provided to tackle the problem.
Further discussion on this topic is needed.

## Slide 6: SP 1
Do you agree that NPCA should be allowed in seamless roaming procedure?
  Yes/No/Abstain

## Slide 7: SP 2
Do you agree that target AP MLD and non-AP MLD should sync channel status in roaming procedure?
  Yes/No/Abstain