## Slide 1: Thoughts on Seamless Roaming and NPCA
Date: 2024-12-16
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Chaoming Luo |  |  |  | 
Liuming Lu |  |  |  | 
Liangxiao Xin |  |  |  | 
Dong Wei |  |  |  | 
Yapu li |  |  |  | 

## Slide 2: Introduction
Seamless Roaming enables context transfer or data transfer between current AP MLD and target AP MLD so as to make the roaming procedure faster.
NPCA enables a STA to access the NPCA primary channel while the BSS primary channel is known to be busy due to OBSS traffic or other conditions.
In this contribution, we share a special different view problem when take the seamless roaming and NPCA into consideration at the same time.

## Slide 3: Scenario
Assume an NPCA enabled seamless roaming scenario where a target AP MLD and a current AP MLD are connected over-the-DS.
After roaming preparation phase, the target AP MLD or the non-AP MLD are eager to establish connection with each other so as to finish the roaming procedure as soon as possible.
However, due to a special different view problem caused by NPCA, the non-AP MLD and target AP MLD may not able to exchange frames with each other quickly through the NPCA Primary Channel.

## Slide 4: Special Different View Problem
The special different view problem is:
  If the non-AP MLD enables the link with target AP MLD after OBSS RTS/CTS frames, it will miss those control frames and access to the BSS P-CH by default.
  But the target AP MLD received these OBSS RTS/CTS frames and the switched to the NPCA P-CH.
  So, the target AP MLD could not exchange frames with the non-AP MLD within this NPCA TXOP.
A delayed roaming-signaling frame (e.g. Reassociation Request frame[1], RAR frame[2]) make the seamless roaming less effective in terms of roaming latency.

## Slide 5: Proposed Solution
Target AP MLD informs non-AP MLD of its NPCA status and expiration time through the current AP MLD during context transfer phase
The time to transmit the NPCA status and expiration time is variable.
If the received NPCA status is not expired, non-AP MLD may access to the NPCA P-CH directly once the link is enabled.
Otherwise, non-AP MLD should access to the BSS P-CH by default.
This method could minimize roaming latency when NPCA is enabled in roaming procedure.

## Slide 6: Summary
A special different view problem is introduced when NPCA is enabled in seamless roaming.
This special different view problem could lead to a larger roaming latency.
A solution that transfers the NPCA status and expiration time of target AP MLD to the non-AP MLD is proposed to solve this problem.
Further discussion on this problem may be needed.

## Slide 7: Reference
[1] 11-23-1897-00-00bn-thoughts-on-improving-roaming-under-existing-architecture, Guogang Huang
[2] 11-23-1884-00-00bn-seamless-roaming, Duncan Ho
[3] 11-23-0961-00-0uhr-uhr-secondary-channel-access, Minyoung Park

## Slide 8: SP 1
Do you agree that the special different view problem (shown in slide 3) should be considered when NPCA is enabled in seamless roaming procedure?
  Yes/No/Abstain