## Slide 1: Scope of MAPC and Roaming Standardization
Sep 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Pelin Salem | Cisco Systems |  | 
Binita Gupta | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Introduction
Various presentations and discussions propose that certain aspects of Multi-AP Coordination and Seamless Roaming be standardized and/or be implementation-dependent
On the one hand, the less we standardize, the less IEEE/WFA work there is; and the greater opportunity for vendor differentiation
On the other hand, there is specific stakeholder value from standardization, and we should be cognizant and responsive to it …

## Slide 3: Standardization Sometimes Brings Value … And Sometimes Doesn’t
Value when …
End users want system vendors to compete on price / performance / features / etc
A feature creates greater value the more products that support it, with interoperability (network effect)
System vendors want:
  Multiple silicon sources for business redundancy
  Silicon vendors to compete on price / performance / features / etc
  Their system products to interoperate, regardless of the underlying silicon vendor
Silicon vendors need to see broad market potential before investing in a new feature
Industry members’ marketing efforts synergistically promote the same core capabilities
Lack of Value when …
A feature is entirely contained within a product
A feature is entirely delivered by a system vendor specifically for its customers
There are no expectations for interoperability between system vendors

## Slide 4: Standardization Brings Specific Value to MAPC and Seamless Roaming
Areas of MAPC with standardization value:
Net-admin:
  Although the safe space of MAPC is APs within the same administrative domain, we can’t control our neighbors, so MAPC’s value continues to increase when MAPC extends across administrative boundaries
AP system vendor:
  Needs feature enablement and interoperability across AP SKUs that use different silicon vendors & over generations
  Achieving a common core feature-set requires silicon vendor deliverables for HW-enabled or real-time capabilities:
    Feature-set: C-TDMA/RTWT/SR/OFDMA/BF/JT …
    Capabilities: Slot/SIFS/TXOP-level tasks (AP2AP resource exchanges, triggering, STPR etc)
Areas of seamless roaming with standardization value:
Net-admin:
  No need for roaming between administrative domains
  Invariably use the same system vendor for each seamless roaming zone
AP system vendor
  Feature enablement and interoperability across AP SKUs that use different silicon vendors & over generations
  Achieving a common core feature-set requires silicon vendor deliverables for real-time or HW-enabled capabilities:
    MLME interface for (basic) context transfer to/from lower MAC
    AP2AP data transfer, if supported, would require new and low-level AMSDU/MPDU/AMPDU-related state get+set capabilities

## Slide 5: AP Interfaces for MAPC, where Three Interfaces Should Be Defined
AP SME2
MAPC Policy Engine
Secure AP2AP comms
AP MLME2
MAPC Negotiation Engine
MLME primitives for MAPC framework req+resp mgmt. frames
MAPC AP2AP mgmt. frames sent over the air
MLME primitives for MAPC AP2AP frames that are sent out of band rather than over the air
MLME primitives for measurements to inform policy // not standardized
Note: SME is the responsibility of AP system vendor, etc
AP MAC1
AP MLME1
Sniffer
AP SME1
MAPC Policy Engine
MAPC Negotiation Engine
Scheduler
Secure AP2AP comms
MAPC Execution Engine
1
4
3
AP MAC2
Sniffer
Scheduler
MAPC Execution Engine
2

## Slide 6: AP Interfaces for Roaming, where Two Interfaces Should Be Defined
SME2
Roaming Engine
Secure AP2AP comms
MLME2
MLME primitives for Roaming preparation+ execution mgmt. frames sent over the air
MLME primitives for STA get+set context
  (and get+set data if applicable)
Note: keys not addressed in this figure
Note: SME is the responsibility of AP system vendor, etc
MAC1
MLME1
SME1
Roaming Engine
Datapath
Secure AP2AP comms
Context
1
MAC2
Datapath
Context
Client
2

## Slide 7: We will learn a lot as 802.11bn products are developed and deployed
Standardization should provide for a lowest common denominator
  … that is sufficient to show considerable end-user value
Standardization should not preclude enhancements beyond this
  … via System/silicon vendor specific extensions for experimentation / enhancements, etc

## Slide 8: Summary
In addition to the usual MLME interface and frame formats for req+resp mgmt. frames, we show there is considerable stakeholder value for:
  MAPC
    When a (lowest common denominator) MLME primitive for APs is defined that provides for MAPC management out-of-band (e.g., over the wire) for use by SMEs (and thence a system vendor) to enable the MAPC feature across APs from different system/silicon vendors
    … While allowing vendor specific extensions
  Seamless roaming
    When a (lowest common denominator) MLME primitive for APs is defined that provides get/set context semantics for use by SMEs (and thence a system vendor) to deliver seamless roaming across AP MLDs from different silicon vendors
      And get/set data semantics if applicable
    … While allowing vendor specific extensions

## Slide 9: Strawpoll 1
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn amendment will define:
    AP-to-AP frames including frame formats to enable interoperable MAPC across APs
    MLME primitive(s) so that the SME can orchestrate the transmission and reception of these same frames
    MLME primitive(s) so that the SME can create a “bent pipe” such that the AP-to-AP frames may be sent AP-MLME-to-AP-MLME instead of AP PHY-to-AP PHY
  Note: this allows for feature enablement across different system and silicon vendors, and both wireless and out-of-band MAPC
Y / N / A

## Slide 10: Strawpoll 2
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn amendment will define an MLME primitive that provides get/set context semantics for use by SMEs in order to deliver seamless roaming across AP MLDs
    And get/set data semantics if applicable[Note 2]
  Note 1: this allows for feature enablement across different silicon vendors
  Note 2: the SFD includes “The current AP MLD may forward DL data to the target AP MLD.”
Y / N / A