## Slide 1: Co-ordinated R-TWT agreement for MAP Coordination updates
Date: 2024-09-09
Authors:

## Slide 2: Abstract
In TGbn, Multi-AP (MAP) Coordination is being discussed as one of the major topics.
Several proposals have been made for MAP set-up [1], communication and framework [2]
In this contribution, we discuss enhancing and using R-TWT, having a C-RTWT agreement [3-5] for exchange of MAP coordination updates
  Discussion on using R-TWT schedule across APs/MAP services for MAP coordination updates
  Discussion on harmonization of R-TWT schedule for AP to AP communication and AP to STA R-TWT data transmission
  Discussion on differentiation/prioritization of AP-AP, AP-STA R-TWT based communication

## Slide 3: Introduction
- For MAP coordination, information needs to be exchanged among APs in vicinity
For features like C-SR, C-BF
  Periodic measurements are required to be shared among APs to update coordination parameters
For features like C-TDMA, other TxOP sharing features
  Before the operation, information related to buffer status, TxOP sharing/time sharing/resource sharing feasibility has to be updated among APs
  This updates need to happen with higher probability of guaranteed transmission
We propose using R-TWT for sharing MAP coordination updates
  R-TWT schedule established between APs for coordination. AP-AP communication happens within R-TWT SPs
  R-TWT schedule harmonization for AP-AP, AP-STA communication in MAP network

## Slide 4: R-TWT for AP-AP communication
An R-TWT schedule agreement is established among multiple APs for AP-AP communication.
  AP-AP communication includes exchange of updates of parameters required for the MAP feature(s) negotiated among APs
An AP can establish a R-TWT schedule agreement for AP-AP communication
  with an AP or a set of APs
  per MAP feature or across all MAP features
  An R-TWT schedule agreement can be a combination of the above options
An R-TWT schedule which is agreed among multiple APs or agreed for multiple MAP features is called a common/shared R-TWT schedule
  Communication within common/shared R-TWT SPs can be contention based or Trigger based

## Slide 5
AP 1
AP 3
AP 2
AP 4
Parameter exchange for C-SR
Parameter exchange for C-SR
Parameter exchange for C-BF
R-TWT SP1
Common R-TWT SP2 (Trigger based)
Parameter exchange for C-TDMA
Parameter exchange for C-TDMA
Common R-TWT SP3 (Contention based)
Fig 1: Multiple R-TWT SPs for AP-AP communication
Trigger
Trigger

## Slide 6: Harmonization of R-TWT schedule – AP-AP, AP-STA
An AP has to coordinate with existing R-TWT schedules in the MAP network for AP-STA communication for latency sensitive traffic while accomodating R-TWT schedule agreement for AP-AP communication
  Type A: An AP can agree on separate R-TWT SPs for AP-AP communication and AP-STA data transmission
  Type B: An AP can agree on a common R-TWT SP for both AP-AP communication and AP-STA data transmission
    Note 1: A sharing AP can decide priority among its own R-TWT SPs for AP-STA data transmission, OBSS R-TWT SPs for AP-STA data transmission and AP-AP communication within a common R-TWT SP so that they do not collide while operation
    Note 2: Trigger based operation of AP-AP communication, AP-STA data transmission in a R-TWT SP can be enabled for optimized operation and avoiding collisions.

## Slide 7: Harmonization of R-TWT schedule – AP-AP, AP-STA
AP 1
AP 2
STA 11
Data transamissions DL/UL
Parameter exchange for C-SR
R-TWT SP1
R-TWT SP2 (Trigger based)
AP 1
AP 2
STA 11
Parameter exchange for C-SR
R-TWT Data Transmissions (Dl/UL)
Common R-TWT SP1 (Trigger based) – For AP-AP, AP-STA communication
Parameter exchange for C-TDMA
R-TWT Data Transmissions (DL/UL)
Common R-TWT SP2(Contention based)
Fig 2a: Separate R-TWT SPs for AP-AP communication and AP-STA data transmission
Fig 2b: Common R-TWT SPs for AP-AP communication and AP-STA data transmission
Trigger
Trigger
Trigger

## Slide 8: More thought and next steps
Initial setting up of C-RTWT SPs before MAP is set-up needs to be addressed
  Post discovery, during negotiation and setup of MAP service, C-RTWT agreement to be setup between APs
Specifics of triggering e.g., which AP is a triggering AP needs to be looked into for details
Differentiation/prioritization between AP-AP and AP-STA R-TWT transmissions if a common R-TWT SP is used
Identify more suitable type of C-RTWT operation for MAP coordination (Type A, Type B in slide 6) for various MAP features, e.g., Type A can be more suitable for ... And Type B can be for …

## Slide 9: References
[1] IEEE 802.11-24/639, MAC protocol aspects of multi-AP coordination
[2] IEEE 802.11-24/0511, Requirements and Functionalities for Multi-AP Coordination
[3] IEEE 802.11-23/1916, R-TWT Coordination in Multi-BSS
[4] IEEE 802.11-23/1932, Further considerations on coordinated TWT
[5] IEEE 802.11-23/1952, Coordinated R-TWT for Multi-AP scenarios - Follow up

## Slide 10: Straw Poll 1
Do you agree to define a mechanism in 802.11bn to enable using C-RTWT agreements among APs for exchange of MAP coordination updates?

## Slide 11: Straw Poll 2
Do you agree to define a mechanism in 802.11bn to have a common C-RTWT agreement for AP-AP communication as well as AP-STA data transmission?

## Slide 12: Straw Poll 3
Do you agree to define a mechanism in IEEE 802.11bn for differentiating/prioritizing AP-AP and AP-STA communication when a common C-RTWT agreement is used for AP-AP communication and AP-STA data transmissions?