## Slide 1: TGbi – TID anonymization
Date: 2024-09-10
Authors:
Name | Affiliations | Address | Phone | email
D. Ficara | Cisco |  |  | dficara@cisco.com
J. Contreras | Cisco |  |  | jacontre@cisco.com
U. Campiglio | Cisco |  |  | ucampigl@cisco.com
J. Henry | Cisco |  |  | jhenry@cisco.com
F. Lovison | Cisco |  |  | flovison@cisco.com
S. Orr | Cisco |  |  | sorr@cisco.com

## Slide 2: Why TID?
Part of the 11bi requirements
11-23/1216 – discussion on TID requirements
Recent analysis by UniPisa (11-24/1234) showed TID as one of the main elements that can leak enough information to help track a STA

## Slide 3: Problem statement
Space:
MAC = 48 bits, AID = 12 bits … TID = 4bits
  Not much space to rotate its values
Time:
TID indicates traffic. Traffic patterns might be visible (and hence spot traffic-type and TID mapping) with only a few frames (e.g.: voice).
[See 11-24/1618 about breaking patterns]

## Slide 4: Coming up with a proposal
Small domain, like AID… what about some solution like the AID one in 11-24/1105r1?
Won’t work as-is: A STA can have multiple traffic flows, hence multiple TIDs and protecting each one is critical for STA’s ability of not being tracked.
So, we can have a matrix for each STA:
AP shares a 16xM matrix (for the next M epochs) to each STA.
Better, but:
Messaging cost
won’t solve ”Time” problem: few-frames to detect a TID
=> We might need to avoid keeping same TID mapping within same epoch

## Slide 5: Proposal A
In order to solve space and time problems: XOR the TID with a pseudo-random stream (aka stream-cypher)
TID for packet i (i == PN):
OTIDi = TIDi ⊕ Ci
Ci = i-th 4-bit chunk of PRF-M’s output [computed every M/K packets]
e.g:
PRF-256: split in 64 x 4bit
OTID1 = TID1 ⊕ 1st-chunk
OTID63 = TID63 ⊕ 63th-chunk
…
OTID65 = TID65 ⊕ 1st-chunk from another run of PRF-256

## Slide 6: Proposal A - tuning
Such scheme can be applied:
- per-frame
- each N frames (e.g.: N=3 => 3 consecutive frames have same chunk XOR-ed):
TIDi XOR-ed with Cj, j = i/N
- each epoch (all frames in the epoch have same XOR-ed value)
Of course:
first option gives better privacy but it’s more computational expensive
last option costs less but less secure

## Slide 7: Proposal B
Extend GCMP/CCMP scope to TID
Only 4 more bits
GCMP/CCMP stream already computed per-frame
GCM has also speed advantages
If traffic-patterns are visible, and TID is guessable, are we leaking info?
  Implication of potential known-plaintext attack on 4 bits per frame?

## Slide 8: Summary
TID recap
Problem Statement
Proposals

## Slide 9: Straw Poll #1
Do you support a mechanism where TIDs are obfuscated with different mappings within the same EDP epoch (i.e.: within the same EDP epoch, different frames of the same traffic flow can have different OTID values) ?
Yes
No
Abstain

## Slide 10: Straw Poll #2
Do you support a mechanism where TID is protected via stream-cypher?
Yes
No
Abstain

## Slide 11: Straw Poll #3
Do you support stream-cypher for TID based on PRF (proposal A) or extension of current frame encryption (proposal B)?
PRF (proposal A)
Extending CCMP/GCMP scope (proposal B)
Abstain