## Slide 1: DS MAC Collision Warning
Date: 2024-09-09
Authors:

## Slide 2: Abstract
Proposal for a collision warning mechanism for the non-AP MLD DS MAC

## Slide 3: Background
DS MAC is advertised by the non-AP MLD at association time
  Its goal is to inform the AP on what MAC address the non-AP MLD would like to be known as, over the DS
  Draft 0.5 cl. 9.4.2.336:
 | Element ID | Length | Element ID Extension | DS MAC Address
Octets: | 1 | 1 | 1 | 6
DS MAC Address element format |  |  |  | 
The DS MAC Address element is used by a non-AP STA that is not affiliated with a non-AP MLD or a non-AP MLD to provide the DS MAC address to the AP or an AP MLD, respectively, to be used for the DS mapping.
The format of the DS MAC Address element is shown in Figure 9-1001de (DS MAC Address element format).

## Slide 4: DS MAC Challenge
The AP acts as a bridge between the 802.11 and the DS (e.g. Ethernet) mediums
When the AP receives a frame on the DS, it needs to know if it should forward the frame to the 802.11 medium or not
What happens if the non-AP MLD ‘signals’ a DS MAC that is an already existing entity on the DS?
DS
1. I am a.b.c

## Slide 5: DS MAC Challenge
The AP acts as a bridge between the 802.11 and the DS (e.g. Ethernet) mediums
When the AP receives a frame on the DS, it needs to know if it should forward the frame to the 802.11 medium or not
What happens if the non-AP MLD ‘signals’ a DS MAC that is an already existing entity on the DS?
DS
2. My DS MAC shall be a.b.c
a.b.c

## Slide 6: DS MAC Challenge
The AP acts as a bridge between the 802.11 and the DS (e.g. Ethernet) mediums
When the AP receives a frame on the DS, it needs to know if it should forward the frame to the 802.11 medium or not
What happens if the non-AP MLD ‘signals’ a DS MAC that is an already existing entity on the DS?
DS
a.b.c
a.b.c
TA = a.b.c
?? Er.. Is this the STA (forward) or the DS box (ignore)?

## Slide 7: DS MAC Challenge
The AP acts as a bridge between the 802.11 and the DS (e.g. Ethernet) mediums
When the AP receives a frame on the DS, it needs to know if it should forward the frame to the 802.11 medium or not
What happens if the non-AP MLD ‘signals’ a DS MAC that is an already existing entity on the DS?
a.b.c
a.b.c
TA = a.b.c
?? Er.. Left or right?

## Slide 8: DS MAC Collision
If the DS MAC signaled by the non-AP MLD is already known on the DS, then the AP should tell the non-AP MLD
  We need a DS MAC collision warning frame. Could work like this:
  The non-AP MLD sends the DS MAC in the (re)assoc Request
  If the MAC is already known on the DS, the AP replies (in the (re)assoc Response
    Path 1: the AP uses a temporal DS MAC, the non-AP MLD sends post-assoc an action frame with the next DS MAC
    Path 2: the non-AP MLD sends a (re)assoc request with a new DS MAC
    Path 3: the non-AP MLD uses the MAC suggested by the AP (does the non-AP MLD care which MAC is seen over the DS?)

## Slide 9: Conclusion
DS MAC signaled by the non-AP MLD can collide with over-the-DS entities
When such collision happens, the AP should tell the non-AP MLD
Remediation mechanisms should allow the non-AP MLD to use another, non-colliding DS MAC

## Slide 10: Straw Poll
Do you agree to insert a DS MAC collision warning in 802.11bi?
  Yes
  No
  Abstain