## Slide 1: Compact User field encodings
Nov 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Pelin Salem | Cisco Systems |  | 
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Executive Summary
Situation[3]-[6]
More PHY features in UHR requires more parameters to be signaled in the User field
Legacy User field is 22 bits
Separate fields for NSS, MCS, UEQM pattern are simplest
Problem
Current direction is 3-4b for NSS, 5b for MCS, 1b for (U)EQM, 2b for UEQM patterns, 1b for 2xLPDC
… a lot of bits, and will exceed 22 bits
Solution
Explore compressed encodings while recognizing the spectrum of device complexity

## Slide 3: Situation and Problem: Current direction for User field bit allocation leads to a substantial increase in the size of the User field
Field | 11be | Current direction for 11bn | 
MCS | 4 | 5 | MCS as a distinct field in failed Motion 41[2]
Reserved | 1 | 0 | ?
NSS | 4 | 3 (or 4*?) | NSS as a distinct field in failed Motion 41[2]
isUEQM | 0 | 1 | 1b in passed Motion 40[2]
UEQM Pattern | 0 | 2 | Pattern as a distinct 2b field in failed Motion 41[2]
Subtotal | 9 | 11 (or 12*?) | 
STA-ID | 11 | 11? | Following legacy
isBeamformed | 1 | 1? | Following legacy
isLdpcCoding | 1 | 1? | Following legacy
is2xLDPC | 0 | 1? | 
Total | 22 | 25 (or 26*?) | 
*A desire was expressed to leave room to continue to enable (VS signaling of) up to 16SS |  |  | 

## Slide 4: 11 or 12 bits for (NSS,MCS,isUEQM,UEQM-pattern) is inefficient due the relatively low entropy in each field
  UEQM is not defined for NSS = 1/5/6/7/8
  The lowest constellations defined per code rate cannot use UEQM
    See next slide
  The second-lowest constellations defined per code rate cannot use UEQM involving constellationIndex-2
    See next slide
  18 MCSs need just log2(18) = 4.17b
    Also, if we continue EHT MCS 14 and 15, they are only defined for NSS = 1
  2/3/4 SS have 2/3/4 UEQM patterns respectively; but many (client) devices do not support 4SS
  Indeed, devices exist on a spectrum, from very low capability to very high capability
Product Tier | NSS | MCS | EQM/UEQM?
Very low | 1 | No more than 16 (e.g., 0-7, 0-9, 0-11, or 0-13; and perhaps EHT MCS14-15 | N/A
Low | 2 | 0-17 | Y (EQM + 2 patterns)
Mid | 3 | 0-17 | Y (EQM + 2/3 patterns)
High | 4 | 0-17 | Y (EQM + 2/3/4 patterns)
Very high | 8 (or perhaps 16*) | 0-17 | Y (EQM + 2/3/4 patterns)

## Slide 5: How many (NSS,MCS,isUEQM,UEQM-pattern)-tuples are there? … Just 246+2, which fits into 8b
Code Rate Constellation | 1/2 | 2/3 | 3/4 | 5/6
BPSK | MCS0 |  |  | 
QPSK | MCS1 | MCS2 | MCS3 | 
16QAM | MCS4 | MCS5 | MCS6 | MCS7
64QAM |  | MCS8 | MCS9 | MCS10
256QAM |  | MCS11 | MCS12 | MCS13
1KQAM |  |  | MCS14 | MCS15
4KQAM |  |  | MCS16 | MCS17
Orange = no UEQM possible
Yellow+Green = “M-1” UEQM pattern is possible (one pattern for 14 MCSs and NSS=2/3/4)
Green = “M-2” UEQM patterns are possible (1/2/3 patterns for NSS = 2/3/4 respectively; for 10 MCSs)
NSS | #EQM | #UEQM “M-1” patterns | #UEQM “M-2” patterns | Total
1 | 18+2& |  |  | 18
2 | 18 | 14 | 10 | 42
3 | 18 | 14 | 10+10 | 52
4 | 18 | 14 | 10+10+10 | 62
5 | 18 |  |  | 18
6 | 18 |  |  | 18
7 | 18 |  |  | 18
8 | 18 |  |  | 18
Total | 144+2& | 42 | 60 | 246+2&
SS NSS | 1 | 2 | 3 | 4
2 | M | M-1 |  | 
2 | M | M-2 |  | 
3 | M | M | M-1 | 
3 | M | M | M-2 | 
3 | M | M-1 | M-2 | 
4 | M | M | M | M-1
4 | M | M | M | M-2
4 | M | M | M-1 | M-2
4 | M | M-1 | M-1 | M-2
Yellow = “M-1” UEQM patterns
Green = “M-2” UEQM patterns
Count up the number of distinct tuples, noting that many NSSs and MCSs cannot use certain UEQM patterns
&+2 assuming we carry forward EHT MCS 14 and 15 for NSS = 1

## Slide 6: Corollary: We have great freedom to encode these tuples
  Although we have 8b is possible, we have the choice of 8 (or 9/10/11) bits to express the (NSS,MCS,isUEQM,UEQM-pattern)-tuples
  And we have complete freedom to assign a (NSS, MCS, EQM/UEQM, UQMpattern)-tuple to any 8/9/10/11b value
  What do we optimize for?
  Proposed design principle:
    Lower-capability devices should be given less (de)compression work to do (e.g., bit slicing)
      Since they are appreciably helped by a low-complexity encoding
    Higher-capability devices should bear the brunt of the (de)compression work
      Since they can amortize a more complicated compression scheme
        Via a small Look-Up Table (e.g., HW ROM which might be synthesized to just a few gates; or an array in SW), or
        Via if+else/switch statements (e.g., HDLgates if HW, or code if SW)

## Slide 7: Example for Context: Optimizing for very low to low-tier devices, given an 8b field
EQM/UEQM pattern MCS | 0 | 1 | 2 | 3
0-17 |  |  |  | 
18-31 |  |  |  | 
  NSS = 1
EQM/UEQM pattern MCS | 0 | 1 | 2 | 3
0-17 |  |  |  | 
18-31 |  |  |  | 
  NSS = 2
Product Tier | NSS | MCS | EQM/UEQM
Very low to low | 1-2 | 0-17 | Y (EQM + 2 patterns)
Bit allocation | Nominally 1 bit | Nominally 5 bits | Nominally 2 bits (NSS=2 only needs to signal EQM and two more UEQM patterns)
Impact on higher-tier devices | NSS3-8 use the unused values | Values 18-31 are unused and can be repurposed to encode NSS=3-8 with EQM+UEQM + EHT MCS14+15 | Some values are unused and can be repurposed to encode NSS=3-8 with EQM+UEQM + EHT MCS14+15
As a secondary allocation, the remaining 246-18-42+2 = 186+2 tuples (NSS=3-8 with EQM+UEQM + EHT MCS14+15) can be blockwise assigned to the 110+86 = 196 remaining values[1]
(Very) Low capability devices never use these more complex tuples, so these tuples’ encoding is a don’t care
128-18 = 110 unused values
128- 18-14-10= 86 unused values
18 used values
18+14+10=42 used values

## Slide 8: But there are many other possible encodings we can consider, with different pros and cons. Some more promising options are:
#Secondary values = number of values used outside of nominal
#Secondary blocks = number of blocks with the same NSS + EQM/UEQMpattern (i.e., after aggregating over MCSs) that are positioned outside of nominal
#Secondary compressed blocks: given UEQM with “M-1” (14 MCSs) or “M-2” (10 MCSs), number of blocks where these (14 or 10) MCSs are allocated contiguously (and are positioned outside of nominal)
#Secondary blocks not aligned with power of 2: number of blocks where the lowest actual MCS (i.e., MCS0; or higher in a compressed block) doesn’t align with a nominal MCS0
#Secondary small blocks: number of blocks with 4 entries or fewer
Best for these product tiers | #tuple bits | NSS Nominal | EQM/UEQM Nominal | MCS Nominal | #Secondary values | #Secondary blocks | #Secondary compressed blocks | #Secondary blocks not aligned with power of 2 | #Secondary small blocks
Very low + low | 8 | 1b (1-2SS) | 2b (EQM + 3 patterns) | 5b (0-17) | 186 | 15 | 6 | 2 | 11
Ditto + mid (OK for high) | 9 | 2b (1-4SS) | 2b (EQM + 3 patterns) | 5b (0-17) | 82 | 6 | 0 | 1 | 0
Ditto + high | 10 | 2b (1-4SS) | 3b (EQM + 4 patterns) | 5b (0-17) | 72 | 4 | 0 | 0 | 0
Ditto + very high | 11 | 3b (1-8SS) | 3b (EQM + 4 patterns) | 5b (0-17) | 0 | 0 | 0 | 0 | 0
Very low (OK for low, mid, high) | 8 | 2b (1-4SS) | 2b (EQM + 3 patterns) | 4b (0-15) | 106 | 25 | 0 | 21 | 13
All (see next slide) | 9 | 4b (1-7SS, all patterns) |  | 5b (0-17) | 18 | 2 | 0 | 2 | 0

## Slide 9: Lumping NSS together with EQM/UEQM and pattern into a single field yields quite a clean encoding …
5 bits for MCSnominal
4 bits for NSS + EQM/UEQM and pattern (nominal)
  See RHS table
  Fits everything except for 8SS, which can be located at (say) Index = 6 with MCSnominal = 18-31 and Index = 7 with MCSnominal = 18-21
Index | NSS | EQM (0) / UEQM Pattern
0 | 1 | 0
1 | 2 | 0
2 | 2 | 1
3 | 2 | 2
4 | 3 | 0
5 | 3 | 1
6 | 3 | 2
7 | 3 | 3
8 | 4 | 0
9 | 4 | 1
10 | 4 | 2
11 | 4 | 3
12 | 4 | 4
13 | 5 | 0
14 | 6 | 0
15 | 7 | 0

## Slide 10: Summary
We are currently heading towards 11 bits to indicate the (NSS,MCS,isUEQM,UEQM-pattern)-tuples
This enables trivial bit slicing for all implementations, but grows the User field
We show that there are only 246+2 (NSS,MCS,isUEQM,UEQM-pattern)-tuples in total
  So we can choose to allocate 8/9/10 bits for these tuples instead
The mapping from (NSS,MCS,isUEQM,UEQM-pattern)-tuple to field value may be based on:
  a primary assignment that enables simple clean bit slicing up to a max tuple and
  a secondary assignment thereafter (using the unused values from the primary assignment)
Merging NSS, isUEQM, and UEQM-pattern into a single field is also an attractive design

## Slide 11: References
[1] 24/1665 “Compact User field encodings – detailed examples”, Brian Hart
[2] 24/0171, “TGbn Motions List - Part 1”, Alfred Asterjadhi
[3] 24/1411, “Signaling for UHR PPDU”, Ross Jian Yu
[4] 24/1427, “Signaling for MCS and UEQM in 11bn”, Dongguk Lim
[5] 24/1431, “A-Unified-Signaling-Scheme-for-EQM-and-UEQM”, Aiguo Yan
[6] 24/1461 “UHR preamble signaling”, Sigurd Schelstraete

## Slide 12: Strawpoll 1
Do you agree to remove the following text from the 11bn SFD:
  For a (non-ELR) UHR MU PPDU, there exists a 1-bit EQM/UEQM indication in a User field for non-MU-MIMO in the UHR-SIG field.
Do you agree to add the following text to the 11bn SFD:
  The fields related to NSS, MCS, isUEQM, and UEQM-pattern in the User field enable simple bit slicing for lower-capability devices
  The fields related to NSS, MCS, isUEQM, and UEQM-pattern in the User field may be allocated 8/9/10/11 bits (TBD)
Y / N / A

## Slide 13: Backup (see also [1] for details)

## Slide 14: Optimizing for very low to low-tier devices, given an 8b field
EQM/UEQM pattern MCS | 0 | 1 | 2 | 3
0-17 |  |  |  | 
18-31 |  |  |  | 
  NSS = 1
EQM/UEQM pattern MCS | 0 | 1 | 2 | 3
0-17 |  |  |  | 
18-31 |  |  |  | 
  NSS = 2
Product Tier | NSS | MCS | EQM/UEQM
Very low to low | 1-2 | 0-17 | Y (EQM + 2 patterns)
Bit allocation | Nominally 1 bit | Nominally 5 bits | Nominally 2 bits (NSS=2 only needs to signal EQM and two more UEQM patterns)
Impact on higher-tier devices | NSS3-8 use the unused values | Values 18-31 are unused and can be repurposed to encode NSS=3-8/more UEQM patterns/EHT MCS14+15 | Some values are unused and can be repurposed to encode NSS=3-8/more UEQM patterns/EHT MCS14+15
As a secondary allocation, the remaining 246-18-42+2 = 186+2 tuples (NSS=3-8 with EQM+UEQM + EHT MCS14+15) can be blockwise assigned to the 110+86 = 196 remaining values[1]
(Very) low capability devices never use these more complex tuples, so these tuples’ encoding is a don’t care
128-18 = 110 unused values
128- 18-14-10= 86 unused values
18 used values
18+14+10=42 used values

## Slide 15: Optimizing for mid tier devices, given a 9b field
Product Tier | NSS | MCS | EQM/UEQM
Mid | 1-4 | 0-17 | Y (EQM + 3 patterns)
Bit allocation | Nominally 2 bits | Nominally 5 bits | Nominally 2 bits (NSS=3 only needs to signal EQM and three more UEQM patterns)
Impact on higher-tier devices | NSS=4 is unused; NSS4-8 use the gaps | Some combinations of these values are unused and can be repurposed to encode NSS=4-8/4th UEQM pattern/EHT MCS14+15 | 
As a secondary allocation, the other 246-18-42-52+2 = 134+2 tuples (NSS=4-8 with 4th UEQM pattern + EHT MCS14+15) can be blockwise assigned to the 110+86+76+128 = 400 remaining values[1]
Very low/low/mid capability devices never use these more complex tuples, so these tuples’ encoding is a don’t care for the devices
Plenty of space for 16SS too
  NSS = 3
3*18+4*14 = 110 unused values
EQM/UEQM pattern MCS | 0 | 1 | 2 | 3
0-17 |  |  |  | 
18-31 |  |  |  | 
128-18-14-10-10 = 76 unused
  NSS = 1/2
Same as previous slide
18+14+10+10=52 used values

## Slide 16: Optimizing for high tier devices, given a 9b field
Product Tier | NSS | MCS | EQM/UEQM
High | 1-4 | 0-17 | Y (EQM + 4 patterns)
Bit allocation | Nominally 2 bits | Nominally 5 bits | Wants 3 bits but allocate 2 nominal bits. NSS=4 with the 4th pattern doesn’t fit, must use the secondary allocation
Impact on higher-tier devices | NSS5-8 use the unused values | Some combinations of these values are unused and can be repurposed to encode NSS=5-8/4th UEQM pattern/EHT MCS14+15 | 
As a secondary allocation, the other 246-18-42-52-62+ 10+2 = 82+2 tuples (NSS=4 with 4th UEQM pattern, NSS=5-8 + EHT MCS14+15) can be blockwise assigned to the 110+86+76+76 = 348 remaining values[1]
For (very) low/mid tier devices never use these more complex tuples, so these tuples’ encoding is mostly a don’t care for the devices. For high tier devices, due to 4SS + 4th UEQM pattern, these tuples’ encoding is mostly a don’t care.
Plenty of space for 16SS too
  NSS = 4
3*18+4*14 = 110 unused values
EQM/UEQM pattern MCS | 0 | 1 | 2 | 3
0-17 |  |  |  | 
18-31 |  |  |  | 
128-18-14-10-10 = 76 unused
  NSS = 1/2/3
Same as previous slides
18+14+10+10=52 used values

## Slide 17: Optimizing for high tier devices given a 10b field
Product Tier | NSS | MCS | EQM/UEQM
High | 1-4 | 0-17 | Y (EQM + 4 patterns)
Bit allocation | Nominally 2 bits | Nominally 5 bits | Nominally 3 bits
Impact on higher-tier devices | NSS5-8 use the unused values | Some combinations of these values are unused and can be repurposed to encode NSS=5-8/EHT MCS14+15 | 
NSS=1: 256 – 18 = 238 unused; NSS=2: 256 – 42 = 214 unused
NSS=3: 256 – 52 = 204 unused; NSS=4: 256 – 62 = 194 unused; Total of 850 unused values
As a secondary allocation, the other 18+18+18+18+2 =72+2 tuples (NSS=5-8 + EHT MCS14+15) can be blockwise assigned to the 850 remaining values
Very low/low/mid/high capability devices never use these more complex tuples, so these tuples’ encoding is mostly a don’t care for the devices
Plenty of space for 16SS too