## Slide 1: Discussion on OOO problem
Date: 2024-05-05
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | OPPO |  |  | v-xinliangxiao@oppo.com
Liuming Lu |  |  |  | 
Chaoming Luo |  |  |  | 
Wei Dong |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 

## Slide 2: Introduction
Out-of-order (OOO) delivery [1, 2, 3] has been discussed during UHR and TGbn.
Current in-order delivery may cause the extra processing (HOL blocking) delay at receive reordering buffer and replay detection for LL traffic.
In this contribution, we discuss the possible solutions for OOO delivery.

## Slide 3: Recap of OOO delivery issue
Problem 1:
  According to current spec, MSDUs (SN=X+1, X+2) cannot be passed to the next process when MSDU (SN=X) is not received.
  However, MSDUs (SN=X+1, X+2) should be passed to the next process before expiration time T1
Problem 2:
  If MSDUs (SN=X+1, X+2) is passed to replay detection earlier than MSDU (SN=X), then MSDU (SN=X) can no loner pass replay detection.
Receive Reordering Buffer (Per TA/TID) |  | 
MSDUs | Received? | Expiration Time
SN = X | N | T0
SN = X+ 1 | Y | T1
SN = X+ 2 | Y | T1
… | … | 
Replay Detection (Per TA/TID)
Replay Counter R1
Notes: highlight it is a problem not a solution
wording more like suggestion
Should be used in which scenarios

## Slide 4: Receive Reordering Buffer Scenario
Scenario 1: Receive Reordering Buffer (per TA/TID) only contains one LL traffic stream.
  For dedicated devices such AR/VR headset and game console, it is possible that one TID is only served for one LL traffic stream. Such LL traffic stream can also be SCS traffic stream.
  All the MSDUs in the receive reordering buffer share the same QoS requirement, such as delay bound.
  If the MSDU with greater SN is expired, then the MSDU with smaller SN is also expired.
Scenario 2: Receive Reordering Buffer (per TA/TID) contains multiple traffic streams.
  For universal devices such laptop, one TID may serve multiple traffic streams. Some of them are SCS traffic streams and others are not.
  The MSDU with greater SN does not always have later expiration time.

## Slide 5: Proposed Solution
In both scenarios, OOO delivery should be enabled to avoid the HOL blocking at the receive reordering buffer.
OOO delivery should be applied only for SCS traffic streams.
  Receiver reordering buffer can classify which SCS traffic stream a MSDU belongs to based on the TCLAS element of SCS traffic stream.
  Receiver reordering buffer can know the delay requirement of a MSDU based on the QoS characteristics element of the corresponding SCS traffic stream.
  Receiver STA can decide which MSDUs should use OOO delivery to satisfy the latency requirement of the MSDUs.
Current BA operation is almost not changed!
Notes: Give an example of how to use

## Slide 6: Thoughts on Replay Detection
When OOO delivery is enabled, the current replay detection cannot handle the MSDUs with OOO PN.
  In other word, a replay counter can handle one in-order PN stream.
Receive reordering buffer classifies which SCS traffic stream a MSDU belongs to.
  MSDUs or their PNs belonging to one SCS traffic stream will be delivered to replay detection in order.
  Each SCS traffic stream can have its own replay counter to solve the problem.
There are also other solutions proposed in [1, 2, 3]. Since it is only the operation at receiver STA, the improvement of replay detection can be an implementation issue.

## Slide 7: Summary
In this contribution, we discuss the scenarios of OOO delivery and propose the possible solution.

## Slide 8: SP1
Do you support to include the following in SFD?
  11bn shall define a mechanism to enable OOO delivery at the receiver.
    Note: OOO deliver is only enabled for SCS traffic stream

## Slide 9: Reference
[1] 11-24-1076-00-00bn-some-thoughts-on-preemption
[2] 11-23-0697-00-0uhr-qos-enhancements-for-uhr
[3] 11-24-0463-01-00bn-qos-enhancements-for-uhr