## Slide 1: The trust model between STA and OBSS AP in MAPC scheme

## Slide 2: Introduction
11bn agreed on the C-BF with the following motioned text:
  TGbn defines multi-AP Coordinated Beamforming (Co-BF).
  Other multi-AP coordination modes are TBD.
  [Motion #29, [1] and [49-65]]
In this contribution, we would like to discuss the trust mode between STA and OBSS AP, which can be applied but not restricted to C-BF scheme

## Slide 3: Recap: One proposed sounding sequences in C-BF
  Reference[2] proposes one frame exchange sequences in sounding procedure
  E.g., as shown in the red box, NDPA and BFRP are sent by AP1, while NDP is sent by AP2 and CSI report is sent by STA1.

## Slide 4: Trust and CSI protection issue
The latest 11bi draft defines the protected CSI frame between AP and the associated STA. Need to consider the CSI protection between OBSS AP and STA the following aspects in 11bn
  The trust mode between STA and OBSS AP
  The initiator and responder of C-BF negotiation are two APs,STA is unaware of the target AP information in C-BF scheme.
Motivation
  We propose to set up a trust mode and protection between OBSS AP and STA before the sounding procedure

## Slide 5: The proposed security model between STA and OBSS AP
Assuming STA1 is associating with AP1, and STA2 is associating with AP2, and a trust link is set up between AP1 and AP2.
  After successfully C-BF negotiation between AP1 and AP2
  AP1 provides the participated STA list to AP2, and vice versa.
  AP2 forwards AP1 information to STA2.
  STA2 generates PTK with AP1 via the current PASN procedure.
  STA2 reports the PASN result to AP1

## Slide 6: The following figure depicts one example of the trust model and PTK generation between STA and OBSS AP
Association
AP(1)
AP(2)
（1）STAs lists(non-AP STA2x) for C-BF
non-AP STA2
non-AP STA1
Trust link
Association
Precondition
（3）Synchronize the C-BF target AP to each STA
（2）STAs lists(non-AP STA1x) for C-BF
（4）Synchronize the C-BF target AP to each STA
（5）PASN procedure
（6）PASN report(successful or not)

## Slide 7: Summary
Analyze the trust issues between STA and OBSS AP in the proposed frame exchange sequences in C-BF
Provide an approach to set up the trust issue and generate PTK to protect CSI between STA and OBSS AP

## Slide 8
THANK YOU 

## Slide 9: Reference
1. 20/0123r0 Channel Sounding for Multi-AP CBF
2. 24/1542r0 Sounding Schemes for Coordinated Beamforming
3. 24/209r5 Specification Framework for TGbn
4. 802.11bi draft 0.6

## Slide 10: SP1
Do you agree to have a mechanism to protect the CSI frame between STA and OBSS AP in the sounding of C-BF procedure