## Slide 1: The trust model between STA and OBSS AP in MAPC scheme

## Slide 2: Introduction
In Co-BF,11bn agreed on two new sounding sequences: Joint sounding and sequential sounding.
  In Joint/Sequential sounding, the CSI report may address to the associated AP, and the association AP forward the CSI report to the OBSS AP if necessary
  In sequential sounding, the CSI report may address to OBSS AP
But the direction of CSI feedback is missing from the passed motion.
In this contribution, we would like to discuss the direction of CSI feedback, and the trust mode between STA and OBSS AP.

## Slide 3: The direction of CSI feedback discussion
CSI only address to the associated AP in sequential/Joint sounding
  Pros:It will be more simple in the implementation. And leave the CSI forwarding between APs to the implementation.
  Cons: The OTA forwarding between APs cause a serious overhead issue
CSI may address to the OBSS AP in sequential sounding
  Pros: The overhead issue will be mitigated.
  Cons: Only for UHR STA as the additional signalling design is needed.
CSI address to the both associated AP and OBSS AP in Joint sounding
  Never define the procedure that the STA can DL MU-PPDU including the group addressed MGMT. frame to APs in baseline.
  A lot of change in the baseline will be made if we walk on this direction

## Slide 4: Proposal
The CSI only address to the associated AP as the basic approach in Sequential/Joint sounding procedure.
Additionaly, the CSI from UHR STA may address to the OBSS AP in sequential sounding procedure.

## Slide 5: The following figure depicts CSI addressing to the associated AP in sequential sounding(highlighted in dashed box)
NDPA
AP1
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
BSS 1 STAs being sounded
BSS 2 STAs being sounded
Forwarding
Forwarding
The forwarding may be implimented via the wireless or wired backhaul
?
?

## Slide 6: The following figure depicts CSI addressing to the associated AP in Joint sounding(highlighted in dashed box)
NDPA
NDP
AP1
AP2
NDP
STA1 associated
with AP1
STA2 associated
with AP2
BFRP
BFRP
NDPA
NDP
NDP
Large V
based feedback
Large V
based feedback
BSS 1 STAs being sounded
BSS 2 STAs being sounded
Forwarding
Forwarding
The forwarding may be implimented via the wireless or wired backhaul
?
?

## Slide 7: The following figure depicts the CSI addressing to the target AP in sequential sounding(highlighted in dashed box)
NDPA
AP1
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
BSS 1 STAs being sounded
BSS 2 STAs being sounded

## Slide 8: Trust mode and CSI protection issue when CSI address to the OBSS AP
The latest 11bi draft defines the protected CSI frame between AP and the associated STA. Need to consider the CSI protection between OBSS AP and STA the following aspects in 11bn
  The trust mode between STA and OBSS AP
  The initiator and responder of C-BF negotiation are two APs,STA is unaware of the target AP information in C-BF scheme.
Motivation
  We propose to set up a trust mode and protection between OBSS AP and STA before the sounding procedure

## Slide 9: The proposed security model between STA and OBSS AP
Assuming STA1 is associating with AP1, and STA2 is associating with AP2, and a trust link is set up between AP1 and AP2.
  AP1 and AP2 set up a Co-BF agreement.
  AP1 provides the participated STA list to AP2, and vice versa.
  AP2 forwards AP1 information to STA2.
  STA2 generates PTK with AP1 via the current PASN procedure.
  STA2 reports the PASN results to AP1
  STA2 encrypts the CSI frame via the generated PTK and sends it to AP1.

## Slide 10: The following figure depicts one example of the trust model and PTK generation between STA and OBSS AP
Association
AP(1)
AP(2)
（1）STAs lists(non-AP STA2x) for C-BF
non-AP STA2
non-AP STA1
Trust link
Association
Precondition
（3）Synchronize the C-BF target AP to each STA
（2）STAs lists(non-AP STA1x) for C-BF
（4）Synchronize the C-BF target AP to each STA
（5）PASN procedure
（6）PASN report(successful or not)

## Slide 11: Summary
Analyze two CSI addressing approach in sequential/Joint sounding procedure.
  Propose CSI only address to the associated AP as the basic operation for two sounding procedures.
  Propose the CSI address to the OBSS AP as additional feature in sequential sounding procedure.
Propose to protect the CSI if CSI is allowed to address the OBSS AP
  Provide an approach to address the trust issue and generate PTK to protect CSI between STA and OBSS AP

## Slide 12
THANK YOU 

## Slide 13: Reference
1. 20/0123r0 Channel Sounding for Multi-AP CBF
2. 24/1542r0 Sounding Schemes for Coordinated Beamforming
3. 24/209r5 Specification Framework for TGbn
4. 802.11bi draft 0.7

## Slide 14: SP1
Do you agree the following:
As part of sequential/Joint sounding procedure, CSI from STA addressing to the associated AP is the basic approach?

## Slide 15: SP2
Do you agree the following:
As part of sequential sounding procedure, CSI from UHR STA may address to the OBSS AP shown in the figure?
NDPA
AP1
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
BSS 1 STAs being sounded
BSS 2 STAs being sounded

## Slide 16: SP3
Do you agree to have a mechanism to protect the CSI frame between STA and OBSS AP in sequential sounding procedure?

## Slide 17: Appendix: Sequential sounding in motion[#100]

## Slide 18: Appendix: Joint sounding sequence in motion[#101]