## Slide 1: Considerations on NPCA
Date: 2025-01-14
Authors:
Name | Affiliation | Address | Phone | Email
Hirohiko Inohiza | Canon |  |  | inohiza.hirohiko@mail.canon
Mitsuyoshi Yukawa |  |  |  | 
Yuki Yoshikawa |  |  |  | 
Masatomo Ouchi |  |  |  | 
Yuki Tsujimaru |  |  |  | 
Kazuyuki Tota |  |  |  | 

## Slide 2: Introduction
TGbn has agreed to define Non Primary Channel Access (NPCA) operation to enable a STA to access the nonprimary channel while the primary channel is known to be busy due to OBSS traffic.
This contribution discusses consideration for the following aspects of NPCA.
  NPCA capability setting conditions
  NPCA mode setting conditions
  Constraints in NPCA

## Slide 3: NPCA capability setting conditions
There are several contributions proposing capability of NPCA operation indicating whether NPCA operation is supported or not supported. (E.g.[1])
It is necessary to set NPCA capability properly according to particular conditions.
Proposal: Define conditions for STAs to set NPCA capability.
  NPCA capability shall be set to “not supported” in a STA when,
    The operating band of an AP is 2.4GHz band. (since 2.4GHz band is always congested)
  NPCA capability may be set to “supported” in a STA when,
    The operating band of an AP is 5GHz or 6GHz band.
  NPCA capability may be indicated in Beacon frame, Probe Request/Response frame, or (Re)Association Request/Response frame.

## Slide 4: NPCA mode setting conditions
There are several contributions proposing NPCA mode indicating whether NPCA operation is enabled or disabled. (E.g.[2])
NPCA mode should be set properly according to particular conditions.
  Assumption: NPCA capable STA operating in 20MHz cannot switch outside of its operating channel width
Proposal: Define conditions for STAs to dynamically enable/disable NPCA mode.
  NPCA mode shall be disabled in a STA when,
    The operating channel width of a non-AP STA or AP is changed from channel width more than TBD MHz to equal or less than TBD MHz.
  NPCA mode may be disabled in a STA when,
    Any other conditions depending on implementation. (e.g. power saving, congestion status of NPCA primary channel, QoS requirement)
  NPCA mode may be enabled in a STA when,
    The operating channel width of a non-AP STA or AP is changed from equal or less than TBD MHz to channel width more than TBD MHz.
    Any other conditions depending on implementation. (e.g. power saving, congestion status of NPCA primary channel, QoS requirement)
  NPCA mode may be indicated in Action frames or MAC header.

## Slide 5: Constraints in NPCA
NPCA should be performed only when the primary channel (PCH)’s NAV is set due to OBSS traffic.
  Before NAV duration elapse, a STA switches back to PCH
According to the rule above, a communication in NPCA primary channel with a STA not intending to operate in NPCA mode may lead to a situation degrading the communication efficiency.
  A non-associated STA transmitting a Probe Request frame and receiving Probe Response frame from an AP in NPCA primary channel may start authentication and association process in NPCA primary channel. In such case, after the AP switches back to PCH, the Non-AP STA cannot find the AP and cannot continue authentication and association process in NPCA primary channel.
Proposal: To prevent the situation above, transmission of frames in NPCA primary channel shall be restricted. For example:
  Prohibit transmission of Beacon, Probe Response, Authentication, (Re)Association Response, etc.
  An NPCA AP shall only respond to a frame in the NPCA primary channel received from a NPCA STA that is associated to the NPCA AP.
  An NPCA STA shall only respond to a frame in the NPCA primary channel received from another NPCA STA which is the destination of ICF or the source of ICF.
Probe Rsp
PCH
NPCH
Time
Probe Req
Auth
NAV (set by OBSS)
Non-AP
STA
(Non-associated)
AP
Auth(ReTx)
PCH
NPCH

## Slide 6: Summary
This contribution discusses consideration for the following aspects of NPCA
  NPCA capability setting conditions
  NPCA mode setting conditions
  Constraints in NPCA

## Slide 7: Reference
[1] Secondary Channel Access and Frame Transmission, https://mentor.ieee.org/802.11/dcn/23/11-23-1911-00-00bn-secondary-channel-access-and-frame-transmission.pptx
[2] Enabling Non-Primary Channel Access, https://mentor.ieee.org/802.11/dcn/24/11-24-0427-00-00bn-enabling-non-primary-channel-access.pptx
[3] Secondary Channel Usage Follow Up, https://mentor.ieee.org/802.11/dcn/23/11-23-1935-01-00bn-secondary-channel-usage-follow-up.pptx

## Slide 8: SP1
Do you agree to include the following into the 11bn SFD?
  An NPCA STA may dynamically indicate a mode of NPCA indicating whether NPCA operation is enabled or disabled
  Detailed signaling is TBD

## Slide 9: SP2
Do you agree to include the following into the 11bn SFD?
  An AP shall indicate in the capability that the NPCA operation is not supported when the operating band of an AP is 2.4GHz band

## Slide 10: SP3
Do you agree to include the following into the 11bn SFD?
  An NPCA STA shall indicate in the NPCA mode that NPCA operation is disabled when the operating channel width of the NPCA STA is changed from channel width more than TBD MHz to equal or less than TBD MHz

## Slide 11: SP4
Do you agree to include the following into the 11bn SFD?
  An NPCA AP shall not transmit TBD frames when operating in the NPCA primary channel

## Slide 12: SP5
Do you agree to include the following into the 11bn SFD?
  An NPCA AP shall only respond to a frame in the NPCA primary channel received from a NPCA STA that is associated to the NPCA AP.

## Slide 13: SP6
Do you agree to include the following into the 11bn SFD?
  An NPCA STA shall only respond to a frame in the NPCA primary channel received from another NPCA STA which is the destination of ICF or the source of ICF.