## Slide 1
October 2024
NAV protection for C-TDMA follow up
Date: 2024-10-17
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Introduction
TGbn defines a mechanism for returning remainder of the allocated time (if any) back to the Co-TDMA sharing AP as part of Co-TDMA operation [1]
In this contribution, we discuss the protection aspects in the Co-TDMA procedure especially the scenario where the TXOP return for the remainder of a shared TXOP is requested

## Slide 3: TXOP return in Co-TDMA
TXOP return may depend on specific scenarios and condition
  Scenarios :
    S1) Two or more APs show interest to participate in Co-TDMA, via a response, after receiving ICF from the sharing AP
      After the sharing AP allocates the TXOP to the first shared AP, it may need a TXOP return to allocate TXOP for the next shared AP
    S2) The sharing AP might be need TXOP to serve in-BSS clients after Co-TDMA
      For potential aperiodic LL traffic / predictable periodic LL traffic
  Condition :
    The shared AP is expected to have a margin to transmit the TXOP return frame (i.e., there must be a remainder of the shared TXOP time)
At what phase can the indication for a TXOP return be provided?
  ICF in polling phase
  MU-RTS TXS in TXOP allocation phase
    If the sharing AP having knowledge which candidate shared AP(s) interest to participate in Co-TDMA through polling phase, it can request TXOP return more effectively

## Slide 4: Considering TXOP return scenario
We assume the sharing AP transmits an MU-RTS TXS with an indication of requesting the TXOP return
  However, the sharing AP cannot ensure receiving TXOP return frame from the shared AP due to the limited protection provided by the MU-RTS TXS/CTS frame exchange
Problem definition
  We only focus on STA(e.g., STA2-1) and the scenario when it try to access the channel after MU-RTS TXS/CTS frame exchange
    The STA2-1 is associated to the sharing AP and is hidden to the shared AP
  As discussed in [2-6], the OBSS STA(e.g., OBSS STA1) was excluded from consideration due to concerns regarding overprotection/fairness
    Since the duration field of the MU-RTS TXS is set to the response frame plus one SIFS, it is naturally understood that OBSS STA1 was not considered
  Moreover, even if STA(e.g., STA2-2) resumes contending the channel after MU-RTS TXS/CTS, shared AP start TX after SIFS following the CTS transmission, we did not take this account
STA2-1
Sharing AP
Shared AP
Shared AP
Sharing AP
STA1-1
STA2-1
STA1-2
OBSS STA1
STA2-2
SIFS
MU-RTS TXS with indication of TXOP return is requested
Response (CTS)
TXOP
return
Shared AP’s BSS frame exchanges
OBSS STA1
NAV protection of (MU-RTS TXS/CTS)
UL PPDU
OBSS STA’s frame exchange
Allocated time

## Slide 5: Considering TXOP return scenario
To improve the reception of the TXOP return frame from the shared AP, we can consider a protection method to prevent collisions that may occur when non-AP STAs transmit UL PPDUs to the sharing AP while the shared AP transmits the TXOP return frame to the sharing AP
Proposal 1 : Extend protection until the end of allocation duration
  Non-AP STAs can implicitly determine how much protection needs to be extended by decoding the MU-RTS TXS
    The allocation duration subfield of the MU-RTS TXS specifies allocated time
    The extension value can be set to the difference between the allocated time and the sum of the CTS duration plus SIFS
  It can increase the probability of grabbing the TXOP return frame, however only the UHR device is able to clearly interpret it
STA2-1
Sharing AP
Shared AP
Shared AP
Sharing AP
STA1-1
STA2-1
STA1-2
OBSS STA1
STA2-2
SIFS
MU-RTS TXS with indication of TXOP return is requested
Response (CTS)
TXOP
return
Shared AP’s BSS frame exchanges
OBSS STA1
CTS duration + SIFS
OBSS STA’s frame exchange
Allocated time
Extended protection

## Slide 6: Considering TXOP return scenario
Proposal 2 : Employ MU EDCA and/or RTS enablement
  Before transmitting MU-RTS TXS to the shared AP, the sharing AP may use its obtained TXOP for in-BSS devices
  We can apply the MU EDCA parameters to reduce the opportunity/probability for STA(e.g., STA2-1) to uplink to the sharing AP during allocated time
    The condition is that when the sharing AP uses the TXOP for in-BSS STAs, the STA that has successfully transmitted a QoS data frame(i.e., TB PPDU) is eligible for MU EDCA
    We can set MU EDCA timer until the end of allocated time
  However, we cannot ensure that all non-AP STAs associated to the sharing AP will apply MU EDCA parameter
    It means that not all the non-AP STAs may transmit the QoS data frame successfully in a TB PPDU before allocating TXOP
  Therefore, we can also apply RTS enablement to reduce the uplink transmission probability of non-AP STAs
  It can increase the probability of grabbing the TXOP return frame, and the legacy device (e.g., HE/EHT) is able to interpret it
STA2-1
Sharing AP
Shared AP
Shared AP
Sharing AP
STA1-1
STA2-1
STA1-2
OBSS STA1
STA2-2
SIFS
MU-RTS TXS with indication of TXOP return is requested
Response (CTS)
TXOP
return
Shared AP’s BSS frame exchanges
OBSS STA1
NAV protection of (MU-RTS TXS/CTS)
OBSS STA’s frame exchange
Allocated time
MU EDCA Timer
Frame exchange
TF
TB
PPDU
STA2-1
Sharing AP
Shared AP
SIFS
MU-RTS TXS with indication of TXOP return is requested
Response (CTS)
TXOP
return
Shared AP’s BSS frame exchanges
OBSS STA1
OBSS STA’s frame exchange
Allocated time
Frame exchange
(not with the STA2-1)
TF
TB
PPDU
NAV protection of (MU-RTS TXS/CTS)
RTS
<MU EDCA>
<RTS enablement>

## Slide 7: Conclusion
Even through previous proposals, it does not fully guarantee that the sharing AP can recognize the TXOP return from the shared AP and there may be a more effective approach to increase probability of the sharing AP not losing its obtained TXOP
Therefore, it is important to take proactive measure to ensure the TXOP can be returned as effectively as possible
Without such measures, it could lead to increased collisions, negatively impacting the network throughput

## Slide 8: Reference
[1] 24/0209r9, Specification Framework for TGbn
[2] 23/1846r1, Protection of Extended TXOP sharing
[3] 24/0093r3, NAV setting for Coordinated TDMA
[4] 24/0375r1, NAV protection for C-TMA
[5] 24/0432r0, NAV Rules in C-TDMA
[6] 24/0227r1, TXOP Protection in C-TDMA

## Slide 9: SP1
Do you agree that a sharing AP shall send a TXOP allocation frame(exact name TBD) to a single shared AP to share a time portion of its TXOP?
The Duration field of the frame is set to the length of time required to transmit the solicited response frame plus one SIFS

## Slide 10: SP1
Do you agree that, as part of the Co-TDMA procedure, TGbn defines a mechanism for a Co-TDMA sharing AP to solicit TXOP return to a Co-TDMA coordinated AP by including a return indication in the MU-RTS TXS Trigger frame?

## Slide 11: SP2
Do you agree that, as part of the Co-TDMA procedure, TGbn defines a mechanism for protecting returned TXOP of Co-TDMA coordinated AP when an indication of TXOP return is requested from Co-TDMA sharing AP
How to protect is TBD

## Slide 12: SP3
Do you agree that, as part of the Co-TDMA procedure, when TXOP return is requested, TGbn defines a mechanism to extend protection of non-AP STA which is associated to the sharing AP and is hidden to a shared AP’s BSS
The mechanism(s) are TBD