## Slide 1: TXOP sharing in contention style
Date: 2025-04-15
Authors:
Name | Affiliation | Address | Phone | Email
Junbin Chen | TP-Link Systems Inc. |  |  | chenjunbin@tp-link.com.hk
Yunpeng Yang |  |  |  | yangyunpeng@tp-link.com.hk
Renfang Zhou |  |  |  | zhourenfang@tp-link.com.hk
Yaoshen Cui |  |  |  | cuiyaoshen@tp-link.com.hk
Haozheng Li |  |  |  | lihaozheng@tp-link.com.hk
Qingwei Fu |  |  |  | fuqingwei@tp-link.com.hk
Shuyu Shi |  |  |  | shishuyu@tp-link.com.hk
Yu Zhu |  |  |  | zhuyu@tp-link.com.hk

## Slide 2: Abstract
In TGbn D0.2 [1-2] we have defined the Co-TDMA to enable an AP to share a time portion of an obtained TXOP with one or more other APs to transmit one or more PPDUs.
  The procedure contains a polling phase, a TXOP allocation phase and a possible TXOP return phase [1-5].
Basically, the TXOP allocation is scheduled by the sharing AP based on the information collected during the polling phase.
  However, sometimes the polled AP may not be able to report it in time during the polling phase.
  E.g., due to aperiodic IDC issues occurred in the polled AP [6]; or, the event-based low latency (EBLL) traffic [7-9] just arrives after the polling phase.
  Besides, the EBLL traffic may come to the sharing AP during the TXOP allocated to shared AP.
In this presentation, we’d like to discuss about the Co-TDMA for handling the issues above.

## Slide 3: The Co-TDMA in TGbn
There still remains several issues in the Co-TDMA of previous contributions:
If the LL traffic of sharing AP arrives during the TXOP allocation phase, it waits until TXOP return.
The sharing AP needs to collect the information of the pending LL traffic of multiple shared APs and determines which shared AP to be the TXOP Sharing (TXS) responder based on such information.
  However, the information collection can be quite difficult for the event-based Low Latency (EBLL) traffic.
MU-RTS TXS
CTS
Data transmission
LL traffic arrives and suffers delay
TXOP return
Data transmission
Sharing AP
Shared AP
MU-RTS TXS
CTS
Data transmission
Sharing AP1
Shared AP2
TXOP return
MU-RTS TXS
CTS
Data transmission
TXOP return
Shared AP3
Shared AP4
BSRP
BSR
BSR
BSR
LL traffic arrives
LL traffic arrives
EBLL traffic arrives and suffers delay

## Slide 4: Proposal 1: TXS with puncturing mode
We propose to define a mode that:
  The sharing AP can share a subset of its bandwidth to the shared AP(s), and operate with the remaining bandwidth in the puncturing mode during the allocated duration.
  In such mode, the sharing AP is still available to deliver any possible LL traffic arrived during the allocated TXS duration in puncturing mode.
  Further, the sharing AP may announce multiple bandwidth units (BWUs) for multiple shared APs.
    The granularity of BWUs here can be 20MHz for simplicity.
MU-RTS TXS
CTS
Data transmission on BWU1
BWU1 shared to AP2
Data transmission in puncturing mode
Sharing AP1
Shared AP2
Data transmission
LL traffic arrives to AP1 and can be delivered
CTS
Data transmission on BWU2
Shared AP3
BWU2 shared to AP3
ICF
ICR
ICR

## Slide 5: Proposal 2: allow contention in TXS duration
Considering the mode that sharing AP do not require for a TXOP return:
  The shared AP may finish the transmission earlier than the allocated duration ends.
  The other APs can try to contend for such a remaining duration.
  The number of shared APs allowed to participate in the contention can be limited by sharing AP (will be discussed later).
MU-RTS TXS
CTS
Data transmission
Sharing AP1
Shared AP2
Data transmission
Win the remaining TXOP
Shared AP3
ICF
ICR
ICR
Allocated duration

## Slide 6: Combine with both proposals
If combined with both the proposals, then we can achieve such a flexible Co-TDMA scheme:
  A sharing AP may announce more than one BWUs to more than one shared APs.
  The sharing AP may assign a contention-free period of a RA-BWU to a specific shared AP, after which the other polled APs can start to contend for the RA-BWU.
  Polled APs that does not successfully report its requirement can try to contend for a BWU.
  The contention can be P-EDCA-based or UORA-based, TBD.
MU-RTS TXS
CTS
Data transmission on BWU1
RA-BWU2, (AP3 contention-free)
BWU1 for AP2
Sharing AP1
Shared AP2
Data transmission
Shared AP3
Data transmission in puncturing mode
Win RA-BWU2
Shared AP4
ICF
ICR
ICR
ICR
CTS
Data transmission
Contention-free

## Slide 7: The priority of shared APs
The BWU is determined to be RA-BWU based on different value between allocation duration and contention-free period.
The shared AP that is assigned a specific BWU is of the highest priority during the contention.
The sharing AP can announce some constraints (e.g. the delay bound requirement) to alleviate the contention.
  For example, only the shared APs whose delay bound of the pending LL data is lower than the announced requirement can participate in the contention.
  An exemplary of the MRTT frame can be defined as follow.
The contention here can be performed in a similar way as EDCA, or in the UORA contention style.
  In P-EDCA style, the shared APs shall initiate a TXS back-off counter based on the delay bound of pending LL data.
  In UORA style, the shared AP shall invoke the OBO contention procedure and transmit a RTS to protect its following transmission.
MAC Header
Common info
User info list
Padding
FCS
APID
BWU index
BWU size
Allocation duration
Contention-free period
Delay requirement

## Slide 8: Summary
The polled AP might not be able to report its requirements in time during the polling phase.
  The polled AP might suffer aperiodic IDC issues.
  The arrival of event-based low-latency (EBLL) traffic is unpredictable to the sharing AP.
  The sharing AP has to query the buffer status of multiple shared APs over and over again.
  The EBLL traffic of sharing AP may also arrive during the TXS procedure and suffer significant delay.
In this presentation, we proposed a special TXS mode for EBLL traffic/aperiodic IDC.
  The sharing AP can reserve some BWUs to serve its associated STA during the TXOP allocation phase.
  The other BWUs can be assigned to or contended by multiple shared APs with LL traffic.
  The priority of multiple shared APs can be distinguished by designing the contention procedure.

## Slide 9: References
[1] P802.11bn D0.2
[2] 25/0521 PDT-MAC-Co-TDMA-CR-CC50-Part-1, Sanket Kalamkar (Qualcomm Technologies Inc.)
[3] 23/1871 M-AP Coordinated Transmission framework, Arik Klein (Huawei)
[4] 24/0512 Considerations for Coordinated TDMA, Rubayet Shafin (Samsung Electronics)
[5] 24/0411 TXOP Return in C-TDMA, Geonhwan Kim (LG Electronics)
[6] 24/1504 Considerations on Aperiodic In-device Coexistence, Hyeonjun Sung (WILUS Inc.)
[7] 24/0811 Overlapped indication for aperiodic low latency traffic, Daniel Verenzuela (Sony Group Corporation)
[8] 24/0091 Enhanced Scheduling Method for Low Latency Traffic Follow up, Serhat Erkucuk (Ofinno)
[9] 23/1229 Preemption for Low Latency Application (follow up), Juan Fang (Intel)

## Slide 10: Straw Poll 1
Do you agree to define a Co-TDMA mode in 11bn, in which mode the sharing AP can still serving its associated STA during the allocated period?
  The sharing AP may share a subset rather than the whole of its operating bandwidth to shared AP(s).
  The sharing AP may operate with a reserved bandwidth in puncturing mode for the allocated period.
  Operation details for such mode are TBD.

## Slide 11: Straw Poll 2
Do you agree to define a Co-TDMA mode in 11bn, in which mode the remaining allocated TXOP can be contended by polled AP(s) other than the assigned shared AP(s)?
  In such mode the sharing AP does not require for a TXOP return.
  The polled APs other than the assigned shared AP(s) may initiate the contention only after a BWU is released.
  The contention can be P-EDCA-based or UORA-based, details are TBD.
  The sharing AP may announce some constraints to alleviate the contention.