## Slide 1: TXOP Sharing for Multi-AP Scenarios
Date: 2025-02-20
Authors:
Name | Affiliations | Address | Phone | email
Dana Ciochina | Sony Group Corporation |  |  | Dana.Ciochina@sony.com
Thomas Handte |  |  |  | Thomas.Handte@sony.com
Daniel Verenzuela |  |  |  | 
Qing Xia |  |  |  | 
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka@sony.com
Kosuke Aio |  |  |  | 
Ryuichi Hirata |  |  |  | 
Ken Tanaka |  |  |  | 

## Slide 2: Introduction
Coordinated Channel Access for multi-AP transmissions has been discussed in [1]-[3]
  Goal of coordinating transmissions is avoiding interference and improving throughput
  Most discussions focused on coordinated TDMA
    One AP gains the medium, allows another AP to use the part of the obtained TXOP
    Sharing AP needs no specific information about how the remaining TXOP would be used by the shared AP
There are however use cases in which an AP has a specific incentive to allow usage of its obtained TXOP by another AP
In this presentation, we discuss some of these use cases and propose enhancements to enable a task-oriented TXOP sharing, better suited for such cases

## Slide 3: Motivation
Considering collaborative multi-AP tasks such as:
  Preparation for a concurrent transmission scheme such as CSR or CBF
    Performing sounding
  Speeding up roaming procedure when overlapping bandwidths are being used by the two APs
    Individual, over the air transmission of buffered data at the source AP towards the roaming STA is preferred
      The buffered data can correspond to any or all ACs (not necessarily high priority)
    If only single link roaming is possible, the target AP should start transmitting to the roaming STA after the source AP has finished or after a timer elapses.
    If dual link roaming with eMLSR on the same channel, coordination of same TID traffic transmissions is beneficial
TXOP Sharing provides a useful framework for such tasks
  As a coordinated sequential use of the spectrum
  However, the only constraints so far are on the AC, thus not helping in the use cases mentioned above

## Slide 4: TXOP Sharing for Multi-AP Sounding (1/2)
Coordinated Sounding
  Baseline sounding scheme is designed as a sequence of NDPA-NDP-BFRP-Fbk, with channel reserved based on the NDPA
  For COBF,
    AP1 needs feedback from STAs associated with AP2.
      AP1 needs AP2’s cooperation for obtaining the feedback
    The sounding consists of 4 parts, for determining all channels from (APi) to , i,j={1,2}
      it is beneficial to keep the sounding blocks together and at the same time allow some flexibility
      Ex1: AP1 may only require missing feedback segments from the participating STAs associated with AP2
      Ex2: AP2 may have fresh CSI from but not of (due to AP1 unavailability)

## Slide 5: TXOP Sharing for Multi-AP Sounding (2/2)
Coordinated Sounding
  An AP, capable of performing CSR or CBF, shares an obtained TXOP with APs from the cooperation group to obtain channel measurements
    AP1 gives the control to AP2 in the second part of the TXOP
      AP2 exchanges control frames with STAs associated with itself
      AP2 should however limit the exchanges to sounding related frames, according to AP1 request
  ICF / ICR exchange information on the sounding requirements,
    Which sequences would be performed, duration, parameters
Allow for sounding

## Slide 6: TXOP Sharing for Seamless Roaming (1/2)
Speeding up the transmission of outstanding MPDUs during a roaming procedure
  A target AP obtaining a TXOP while a roaming procedure is ongoing with a source AP
    shares a part of an obtained TXOP with the source AP and
    prioritizes or restricts the use of part of its TXOP to allow the source AP to finalize the buffered data transmission
    allows any AC as long as corresponding to the respective rSTA (roaming STA)
AP2 should already have the data available

## Slide 7: TXOP Sharing for Seamless Roaming (2/2)
Further particular cases:
  If the source AP is ready for the transmission, the target AP as sharing AP may allow the source AP to transmit first:
    especially useful when the target AP already started having data for rSTA or for same TID transmissions

## Slide 8: TXOP Sharing for SCS Agreements
Respecting established SCS agreements
  A sharing AP may assist the polled AP in respecting the SCS agreements e.g.,
    for a time interval during or after the roaming procedure or
    based on co-RTWT negotiations
  If the STA should be triggered within an interval which corresponds to the time in which the shared AP has obtained a TXOP:
    AP1 can “plan” the TXOP to allow the polled AP to schedule the respective STA

## Slide 9: Standard Support
Simple extensions to the TXOP Sharing Framework defined for CTDMA
  ICF/ICR frames defined as Poll/Announce frames
  ICF design should indicate that a part of the obtained TXOP can be used by one or more APs only for a specific purpose or under specific conditions
  BSRP based ICF as proposed in [4],[5] can be further used
    Minimum additional signaling is a “sharing TXOP mode” indicating the conditions under which a shared AP can use the shared portion
      For sounding purposes, measurement type and configuration should be either known (if scheduling periods for measurements are defined) or need to be exchanged e.g., sounding dimensions, feedback format
      For roaming purposes, further conditions do not need an explicit signaling. Can be handled by behavior description
      For respecting SCS agreements: the SCS ID (for operation in Slide 8) or TID (for operation in slide 7) and rSTA can be helpful

## Slide 10: Summary
Several use cases have been shown, which require coordinated channel access between APs
  Coordinated sounding
  Multi-AP collaboration for buffered data transmission in case of roaming
  Multi-AP collaboration for respecting SCS agreements
These cases require a more specific TXOP sharing, allowing a sharing AP to indicate a TXOP purpose
  and restrict or prioritize the TXOP usage to frame exchanges serving the respective purpose
We proposed an implementation, which can be easily integrated in the current framework

## Slide 11: References
[1] 23/0261r0, “C-TDMA procedure in UHR”
[2] 23/0093r2, “C-TDMA Follow-up”
[3] 23/0423, “NAV Rules in C-TDMA”
[4] 24/1226r0, “Initial control frames and initial control response design”
[5] 24/1225, “Initial Control Frames in C-TDMA”
[6] 24/1016, “C-TDMA follow-up: Additional details on framing sequence”

## Slide 12: SP1
Do you agree to define a mechanism that enables a sharing AP to prioritize or limit the shared use of an obtained TXOP by shared AP to an intended operational mode or frame exchange?

## Slide 13: SP2
Do you agree to include in the SFD
  A sharing AP, which is involved in a COBF scheme may transmit an initial control frame with an indication that the shared part of the obtained TXOP shall be used by the shared AP for performing sounding or for exchanging sounding related frames?

## Slide 14: SP3
Do you agree to include in the SFD
  A sharing AP which is involved in a seamless roaming procedure with another AP operating over the same bandwidth, may indicate within an ICF to the other AP that at least part of the shared TXOP shall be used for the transmission of outstanding MPDUs from the other AP to the common roaming STA?