## Slide 1: 20 MHz UHR-LTF Sequence for DRU
Date: 2024-11-10
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
In [1], we proposed to design a new 4x UHR-LTF sequence for DRU in each distribution bandwidth
In this contribution, we propose 20 MHz 4x UHR-LTF sequences by considering two DRU tone plans
  The tone plan and pilot tones proposed in [2]
  The tone plan proposed in [3] with pilot tones proposed in [4]

## Slide 3: 20 MHz UHR-LTF Sequence for Tone Plan [2] (1/2)
The 20 MHz DRU tone plan in [2] is as follows
The 20 MHz DRU pilot tone in [2] is as follows
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-115:9:-7, 11:9:119] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-113:9:-5, 4:9:112] | DRU5 [-117:9:-9, 9:9:117]
 | DRU6 [-112:9:-4, 5:9:113] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-119:9:-11, 7:9:115] | DRU9 [-114:9:-6, 12:9:120] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 2] |  | DRU2 26-tone [DRU6~9], [-2, 3] |  | 
Pilot indices for DRU transmission over 20MHz | 
DRU size | KdRxx_i
DRU26, i = 1:9 | { -93 33 }, { -43 83 }, { -73 53 }, { -23 103 }, { -63 63 }, { -103 23 }, { -53 73 }, { -83 43 }, { -33 93 }
DRU52, i = 1:4 | { -93 -43 33 83 }, { -73 -23 53 103 }, { -103 -53 23 73 }, { -83 -33 43 93 }
DRU106, i = 1:2 | { -73 -23 53 103 }, { -103 -53 23 73 }

## Slide 4: 20 MHz UHR-LTF Sequence for Tone Plan [2] (2/2)
We propose the following 20 MHz 4x UHR-LTF sequence
  DLTF-122:122 = [0 0 -1 -1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 -1 1 -1 -1 -1 -1 1 1 1 -1 1 1 1 -1 1 -1 1 -1 1 -1 1 1 1 -1 1 -1 -1 1 1 -1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 -1 -1 1 -1 1 -1 1 1 -1 -1 -1 1 -1 -1 -1 -1 -1 -1 1 -1 1 -1 -1 1 -1 1 1 -1 1 -1 1 1 -1 -1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 1 1 -1 1 1 1 1 -1 -1 1 -1 1 1 1 1 -1 -1 -1 -1 0 0 0 -1 -1 -1 -1 1 1 1 1 -1 1 -1 -1 1 1 1 1 1 1 1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 -1 -1 1 1 1 1 -1 1 1 -1 1 -1 -1 1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 1 1 1 -1 1 -1 1 -1 1 1 -1 -1 1 -1 1 1 1 -1 1 -1 -1 -1 1 -1 1 1 1 -1 1 1 1 -1 -1 -1 -1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 -1 -1 -1 -1 -1 0 0]
PAPR [dB]
26 RU_1 | 26 RU_2 | 26 RU_3 | 26 RU_4 | 26 RU_5 | 26 RU_6 | 26 RU_7 | 26 RU_8 | 26 RU_9
3.3616 4.0911 | 3.4751 3.7545 | 3.4346 4.1705 | 3.4689 4.3489 | 2.8591 2.8591 | 3.4689 4.3489 | 3.4346 4.1705 | 3.4751 3.7545 | 3.3616 4.0911
52 RU_1 |  | 52 RU_2 |  |  | 52 RU_3 |  | 52 RU_4 | 
4.4512 4.5587 |  | 4.6713 4.3916 |  |  | 4.6713 4.3916 |  | 4.4512 4.5587 | 
106 RU_1 |  |  |  |  | 106 RU_2 |  |  | 
4.6043 4.6713 |  |  |  |  | 4.6043 4.6713 |  |  | 
Upper values denote PAPRs for 1 SS
Lower values denote PAPRs when either data or pilot tones are multiplied by -1 which can cover 2 SS and LTF extension (2 / 4 LTF symbols)
8 times IFFT is applied

## Slide 5: 20 MHz UHR-LTF Sequence for Tone Plan [3][4] (1/2)
The 20 MHz DRU tone plan in [3] is as follows
The 20 MHz DRU pilot tone in [4] is as follows
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 3] |  | DRU2 26-tone [DRU6~9], [-2, 2] |  | 
Pilot indices for DRU transmission over 20MHz | 
DRU size | KdRxx_i
DRU26, i = 1:9 | { -111 15 }, { -89 37 }, { -100 26 }, { -78 48 }, { -67 59 }, { -56 70 }, { -34 92 }, { -45 81 }, { -23 103 }
DRU52, i = 1:4 | { -111 -89 15 37 }, { -100 -78 26 48 }, { -56 -34 70 92 }, { -45 -23 81 103 }
DRU106, i = 1:2 | { -111 -78 15 48 }, { -56 -23 70 103 }

## Slide 6: 20 MHz UHR-LTF Sequence for Tone Plan [3][4] (2/2)
We propose the following 20 MHz 4x UHR-LTF sequence
  DLTF-122:122 = [0 0 -1 -1 -1 1 1 -1 1 1 -1 1 1 1 -1 -1 -1 -1 1 1 1 -1 -1 -1 1 -1 1 -1 -1 -1 -1 -1 1 1 1 -1 -1 1 1 1 -1 -1 1 1 1 1 -1 1 -1 1 1 1 -1 -1 -1 1 1 1 1 1 1 1 -1 1 -1 1 1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 1 -1 -1 -1 1 1 -1 1 1 -1 -1 1 1 -1 -1 1 -1 1 1 1 1 -1 1 -1 1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 -1 1 -1 1 -1 -1 1 0 0 0 1 1 1 1 -1 -1 -1 -1 1 -1 1 1 1 1 1 -1 1 -1 -1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 1 1 -1 -1 -1 1 1 -1 -1 1 1 -1 -1 -1 1 -1 1 1 -1 -1 1 -1 -1 -1 -1 1 -1 1 1 1 -1 -1 -1 1 1 -1 1 1 -1 1 1 -1 -1 1 1 1 -1 1 1 1 -1 -1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 1 1 -1 -1 -1 -1 1 -1 1 -1 -1 -1 -1 -1 1 1 1 -1 1 0 0]
PAPR [dB]
26 RU_1 | 26 RU_2 | 26 RU_3 | 26 RU_4 | 26 RU_5 | 26 RU_6 | 26 RU_7 | 26 RU_8 | 26 RU_9
3.7005 3.7578 | 3.4374 3.9121 | 3.3326 4.7265 | 3.4154 3.7085 | 2.9596 2.9734 | 3.2973 4.4461 | 3.6052 4.5655 | 3.5581 4.3706 | 3.5181 4.6082
52 RU_1 |  | 52 RU_2 |  |  | 52 RU_3 |  | 52 RU_4 | 
4.6443 4.6529 |  | 4.6624 4.7054 |  |  | 4.6434 4.6361 |  | 4.6021 4.5254 | 
106 RU_1 |  |  |  |  | 106 RU_2 |  |  | 
4.6803 4.7328 |  |  |  |  | 4.6113 4.6533 |  |  | 
Upper values denote PAPRs for 1 SS
Lower values denote PAPRs when either data or pilot tones are multiplied by -1 which can cover 2 SS and LTF extension (2 / 4 LTF symbols)
Note that the maximum PAPR of the 20 MHz 4x UHR-LTF sequence proposed in [5] is 3.7970 / 4.8499 / 4.7948 dB for 26 / 52 / 106 DRUs
8 times IFFT is applied

## Slide 7: Conclusion
We have proposed 20 MHz 4x UHR-LTF sequences for two 20 MHz DRU tone plans
We have confirmed that our proposed sequences guarantee low PAPR for a DRU transmission
  1 / 2 SS and LTF extension (i.e., 2 / 4 LTF symbols) has been considered for a PAPR assessment
  The maximum PAPR is lower than that of [5]

## Slide 8: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  20 MHz 4x UHR-LTF sequence for a DRU transmission is defined as follows
    DLTF-122:122 = [0 0 -1 -1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 -1 1 -1 -1 -1 -1 1 1 1 -1 1 1 1 -1 1 -1 1 -1 1 -1 1 1 1 -1 1 -1 -1 1 1 -1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 -1 -1 1 -1 1 -1 1 1 -1 -1 -1 1 -1 -1 -1 -1 -1 -1 1 -1 1 -1 -1 1 -1 1 1 -1 1 -1 1 1 -1 -1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 1 1 -1 1 1 1 1 -1 -1 1 -1 1 1 1 1 -1 -1 -1 -1 0 0 0 -1 -1 -1 -1 1 1 1 1 -1 1 -1 -1 1 1 1 1 1 1 1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 -1 -1 1 1 1 1 -1 1 1 -1 1 -1 -1 1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 1 1 1 -1 1 -1 1 -1 1 1 -1 -1 1 -1 1 1 1 -1 1 -1 -1 -1 1 -1 1 1 1 -1 1 1 1 -1 -1 -1 -1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 -1 -1 -1 -1 -1 0 0]
Y/N/A: //

## Slide 9: Straw Poll #1-1
Do you agree to add the following text to the TGbn SFD?
  20 MHz 4x UHR-LTF sequence for a DRU transmission is defined as follows
    DLTF-122:122 = [0 0 -1 -1 -1 1 1 -1 1 1 -1 1 1 1 -1 -1 -1 -1 1 1 1 -1 -1 -1 1 -1 1 -1 -1 -1 -1 -1 1 1 1 -1 -1 1 1 1 -1 -1 1 1 1 1 -1 1 -1 1 1 1 -1 -1 -1 1 1 1 1 1 1 1 -1 1 -1 1 1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 1 -1 -1 -1 1 1 -1 1 1 -1 -1 1 1 -1 -1 1 -1 1 1 1 1 -1 1 -1 1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 -1 1 -1 1 -1 -1 1 0 0 0 1 1 1 1 -1 -1 -1 -1 1 -1 1 1 1 1 1 -1 1 -1 -1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 1 1 -1 -1 -1 1 1 -1 -1 1 1 -1 -1 -1 1 -1 1 1 -1 -1 1 -1 -1 -1 -1 1 -1 1 1 1 -1 -1 -1 1 1 -1 1 1 -1 1 1 -1 -1 1 1 1 -1 1 1 1 -1 -1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 1 1 -1 -1 -1 -1 1 -1 1 -1 -1 -1 -1 -1 1 1 1 -1 1 0 0]
Y/N/A: //

## Slide 10: References
[1] 11-24-1097-00-00bn-thoughts-on-uhr-ltf-for-dru
[2] 11-24-1096-00-00bn-mirror-symmetric-20-mhz-dru-tone-plan-within-242-rru-boundary
[3] 11-24-0468-02-00bn-dru-tone-plan-for-11bn
[4] 11-24-1230-01-00bn-pilot-tone-design-in-dru-transmission
[5] 11-24-1567-00-00bn-ltf-design-for-dru