## Slide 1: In-device-coexistence use cases follow-up
Date: 2024-11-xx
Authors:
Name | Affiliation | Address | Phone | Email
Hongwon Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hongwon.lee@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St, San Diego CA 92131 , USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
The Motion related to defining a mechanism for a non-AP STA to report unavailability, which is related to both periodic and aperiodic in-device-coexistence(IDC), was passed in the July F2F meeting
Several use cases for the IDC mechanism are discussed from the perspective of device roles, such as non-AP STA and Mobile AP[1]-[5]
We should check if there are any other use cases we haven't discussed but should consider
This contribution summarizes the use cases for the IDC mechanism that we have already discussed and focuses on identifying additional use cases we should consider

## Slide 3: IDC use cases for non-AP STAs
There are clear use cases we should consider for a mechanism that can report the unavailability information of a non-AP STA
  Periodic events
    Bluetooth Low Energy(BLE) Advertising, for example, experiences unavailability for 100us every 500 milliseconds due to in-device coexistence (IDC) between Wi-Fi and BLE
    Bluetooth Audio Play(BR/EDR A2DP streaming), for example, experiences unavailability for 2ms every approximately 11.61ms due to IDC between Wi-Fi and Bluetooth
    UWB(Narrow-band assisted) ranging frame exchange between a non-AP STA and a non-WiFi device
    Etc.
  Aperiodic events
    Bluetooth(BT) Connection request from a peer non-Wi-Fi device; BT Connection response may occupy the medium for an unexpected duration in a device which has both Wi-Fi and BT
    UWB(Narrow-band assisted) ranging session initialization occurs through user interaction (e.g. for ranging measurement with an access control device)
    Etc.

## Slide 4: IDC use cases for Mobile APs
There are clear use cases we should consider for mechanism which can report unavailability information of a Mobile AP
  Periodic events
    A Smart Phone user listens to music via Bluetooth while using Wi-Fi tethering
    A Smart Phone user transfer a picture via BT while using Wi-Fi tethering
    UWB(Narrow-band assisted) ranging frame exchange between non-AP STA and non-WiFi(e.g. UWB) device while using Wi-Fi tethering
    Etc.
  Aperiodic events
    Bluetooth(BT) Connection request from peer non-WiFi device while using Wi-Fi tethering; BT Connection response may occupy the medium for an unexpected duration in a device which has both Wi-Fi and BT
    UWB(Narrow-band assisted) ranging session initialization occurs through user interaction(e.g. for ranging measurement with an access control device) while using Wi-Fi tethering
    Etc.

## Slide 5: IDC use cases for infrastructure APs (?)
Should we really not consider the IDC mechanism for infrastructure APs? If not, why?
It is true that most infrastructure APs for non-enterprise environments currently only have Wi-Fi connectivity in the field
However, if we look at infrastructure APs in an enterprise environment, many APs are not standalone but have multiple connectivity options
Can it be guaranteed that most infrastructure APs will always have only Wi-Fi connectivity in the future?
There may be an answer if we look at the smart home industry; other industries can also be considered

## Slide 6: Infrastructure AP in the future
The requirements for multiple connectivity technologies in infrastructure APs are necessary due to the evolution of various industries; Wi-Fi may be no longer the only connectivity technology for infrastructure APs
An infrastructure AP that has both Wi-Fi and non-WiFi connectivity (e.g., Thread Border Router, BLE, UWB, Zigbee, and more) can be deployed in specific environments such as smart home
  Multiple connectivity technologies are already applied to some Wi-Fi AP products such as Nest Wifi pro, Amazon eero Pro 6 and Edge-corE Wi-Fi Access Point, etc.
We can also predict that many infrastructure APs with multiple connectivity will be feasible in the future by studying the architecture defined by the Matter standard (CSA)
  Matter considers Wi-Fi, Bluetooth/BLE, Thread(802.15.4) as connectivity technologies
  Some Matter devices can have the functionalities of Wi-Fi AP and Thread Border Router(to connect with Matter controlees)

## Slide 7: Wi-Fi Access Point types example
Wi-Fi AP Products (e.g., IoT gateways) can currently cover Type A and/or Type B
Type C may be feasible based on evolving standards and/or implementations aligned with future IoT requirements
  Type C has already become routine in the enterprise environment
Type A | Type B | Type C
Device 2
Device 3
Device 2
Device 3
Device 2
Device 3
Wi-Fi AP
Thread Border Router
Wi-Fi AP
Thread Border Router
Wi-Fi AP
Thread Border Router
BT/BLE
UWB
Device 4
Device 1
Device 1
Time
Increasing IDC issues
Device 1
√
Current
Notes: *

## Slide 8: Conclusion
We summarized the IDC use cases for non-AP STAs and Mobile APs that were discussed previously
IDC use cases for infrastructure APs were examined through studying industries and products
We believe that infrastructure APs with multiple connectivity technologies can feasibly cover various industries, such as smart homes, smart factories, smart buildings, and more
We should also consider applying the IDC mechanism to infrastructure APs

## Slide 9: Straw Poll 1
Do you agree to include the following into the 11bn SFD?
  11bn defines a mechanism for a UHR AP to report unavailability at TxOP level and defines or reuse/update existing mechanism a UHR AP to report long term (periodic) unavailability
    Applies when the peer STA(s) supports the mechanism

## Slide 10: References
[1] 11-24/831r0, Periodic IDC use cases and considerations for signaling
[2] 11-24/1108r1, Periodic IDC signaling for UHR Mobile AP
[3] 11-24/1490r0, More Consideration of ICR/CRF for in-device-coexistence
[4] 11-23/1103r0, In-Device Interference Discussion
[5] 11-23/1934r0, In-Device Interference Mitigation Follow Up