## Slide 1: NPCA Listening Channel
Date: 2024-11-11
Authors:

## Slide 2: Introduction
TGbn agreed to define NPCA primary channel [1]
  A single NPCA primary channel on which STAs contend during an OBSS TXOP
An AP may set NPCA primary channel outside of the operating BW of a non-AP STA
  A non-AP STA whose operating channel does not include the NPCA primary channel may not be enable to participate in NPCA operation unless it switches its operating channel
In this contribution, we propose to introduce ‘NPCA listening channel’ to help non-AP STAs to participate in NPCA operation without switching their operating channel

## Slide 3: Recap: NPCA primary channel and STA’s operating CH [2]
There are cases where an AP selects the NPCA primary channel outside of the operating channels of some NPCA non-AP STAs
In this case, there will be two groups of NPCA STAs:
  Group 1: NPCA non-AP STAs for which the NPCA primary channel is within their operating channels
  Group 2: NPCA non-AP STAs for which the NPCA primary channel is outside of their operating channels
P20
NPCA P20
80 MHz STA
(Group 2)
160 MHz STA
(Group 1)
S80
P80

## Slide 4: Recap: NPCA primary channel and STA’s operating CH [2]
P20
NPCA P20
Operating channel
P20
NPCA P20
OBSS TXOP
Group 2 STA (80 MHz) operation
Operating channel
Operating channel
Operating channel
Group 1 STA (160 MHz) operation
OBSS TXOP
S80
P80
S80
P80
Contending channel
Contending channel
Contending channel
NPCA operation based on STA’s operating BW
  Group 1 STAs do not switch its operating channel, but changes contending channel (primary channel  NPCA primary channel)
    Similar capabilities as the TB PPDU responding procedure (switching to indicated RU) are required
  Group 2 STAs need to switch its operating channel to cover the NPCA primary channel
    Similar capabilities as the Dynamic Sub-band Operation are required
NPCA operations that require changing the operating channel and those that do not require are actions at different levels. Therefore, they may need to be classified as separate NPCA modes

## Slide 5: Problem statement
An AP may designate any of the secondary subchannels as the NPCA primary channel, even if it is outside of the operating channels of some NPCA STAs
  Additionally, an AP may change the designated NPCA primary channel, which could result in the NPCA primary channel being located outside of the operating channels of certain NPCA STAs
If an NPCA STA cannot support NPCA operation using the NPCA primary channel outside of its operating channels, the STA will be unable to participate in NPCA TXOP, even if it supports NPCA operations
  If the expected benefits of NPCA operation are lost due to the location of the NPCA primary channel designated by the AP, the motivations for non-AP STAs to support NPCA operations would be diminished
Therefore, 11bn should ensure that all the NPCA STAs can participate in NPCA frame exchange sequences, regardless of the designated NPCA primary channel and their channel-switching capabilities

## Slide 6: Proposal: NPCA Listening Channel(s)
In addition to the NPCA primary channel, an AP may designate an ‘NPCA listening channel’ for NPCA STAs
  NPCA STAs that cannot support NPCA operations on the NPCA primary channel will conduct NPCA operation using the NPCA listening channel within their operating BW
  The NPCA listening channel will be closer to the P20 channel than the NPCA primary channel
The NPCA listening channel is designated for frame exchanges and is not intended for contention
  Thus, EDCA-based channel access is not permitted on the listening channel
NPCA STAs operating on the NPCA listening channel can participate in NPCA frame exchange sequence initiated by its AP operating on the NPCA primary channel
  The AP can allocate an RU located within operating channel of each NPCA STA
  NPCA non-AP STAs can receive DL PPDU and respond TB PPDU on the NPCA listening channel

## Slide 7: Example of the NPCA listening channel operation
Operating channel
(80 MHz STA)
P20
NPCA primary channel
NPCA listening channel
OBSS TXOP
ICF
ICR
ICR
Frame exchanges for the NPCA STAs operating on the NPCA listening channel
(Rx DL PPDU or Tx TB PPDU)
Frame exchanges for the NPCA STAs operating on the NPCA primary channel
(Rx DL PPDU or Tx TB PPDU)
PD channel
Packet Detection & Contending channel
P20
S40
S80
PD & Contending channel
ICF
Operating channel
(160 MHz STA)
1-1. AP and 160 MHz NPCA STAs that support NPCA operation using the NPCA primary channel switch to the NPCA primary channel
1-2. 80 MHz NPCA STAs switch their packet detection channel to the NPCA listening channel
2. The AP allocates RUs on the S40 to the 80 MHz NPCA STA
ICF
ICF
ICF
ICF
ICR
ICR
ICR
ICR
3-1. The AP and the NPCA STAs operating on the NPCA Primary channel perform frame exchanges on the (S40) and S80
3-2. The AP and the 80 MHz NPCA STA perform frame exchanges on the S40
MSD…
2. The AP allocates RUs on the S40/S80 to the 160 MHz NPCA STA
S40
S80

## Slide 8: Multiple NPCA listening channels
AP may designate multiple NPCA listening channels
  Each NPCA listening channel is for each operating BW NPCA STA
    The NPCA listening channel for a 40 MHz NPCA STA is S20
    The NPCA listening channel for a 80 MHz NPCA STA is one of the subchannel in S40
      The AP designates one of the two subchannels as NPCA listening channel for 80 MHz non-AP STAs
    The NPCA listening channel for 160 MHz NPCA STA is one of the subchannel in S80
      The AP designates one of the four subchannels as NPCA listening channel for 160 MHz non-AP STAs
  *320 MHz NPCA STAs and NPCA STAs supporting NPCA operation using NPCA primary channel use the NPCA primary channel
OBSS TXOP
P20
NPCA primary channel
(for AP and 160 MHz NPCA STAs)
ICF
ICR
RUs for 160 MHz non-AP STAs
RUs for 160/80 MHz non-AP STAs
BA
BA
DL MU PPDU
NPCA listening channel 1
for 40 MHz NPCA STAs
TF
from 160 MHz non-AP STAs
from 160/80 MHz non-AP STAs
TB PPDU
BA
NPCA listening channel 2
for 80 MHz NPCA STAs
RUs for 160/80/40 MHz non-AP STAs
BA
from 160/80/40 MHz non-AP STAs

## Slide 9: Summary
The introduction of an NPCA listening channel has been proposed
  NPCA listening channel is a channel for frame exchanges and is not for a channel for contention
  An AP may designate one or more NPCA listening channel for the NPCA STAs
The NPCA STAs do not support NPCA operation using the NPCA primary channel can use the NPCA listening channel to participate in NPCA TXOP

## Slide 10: Straw Poll 1
Do you agree that an AP can designate any subchannel within its operating bandwidth, except the primary 20 MHz subchannel, as the NPCA primary channel of its BSS?

## Slide 11: Straw Poll 2
Do you agree that a BSS enabling NPCA operation may have one or more NPCA listening channel(s) (name TBD)?
  The NPCA listening channel is a 20 MHz subchannel that used for frame exchanges but not for EDCA based channel access
  A non-AP STA with a designated NPCA primary channel outside its operating bandwidth uses the NPCA listening channel for exchanging frames

## Slide 12: References
[1] 11-24/0209r5 Specification Framework for TGbn Ross Jian Yu
[2] 11-24/1155r0 Further discussions on NPCA Sanghyun Kim
[3] 11-23/0631r0 Secondary channel usage and secondary 20MHz channel backoff Liwen Chu
[4] 11-23/1891r0 Nonprimary channel access – follow up Gaurang Naik
[5] 11-23/2023r1 Further discussion on Non-Primary Channel Access Sindhu Verma
[6] 11-24/0070r2 Some details about non-primary channel access Yunbo Li
[7] 11-24/0426r0 EDCA for Non-Primary Channel Access Dongju Cha
[8] 11-24/0458r1 Considerations on Non-Primary Channel Access Salvatore Talarico
[9] 11-24/0486r1 Some considerations on non-primary channel access Ming Gan
[10] 11-24/0495r0 Non-Primary Channel Access (NPCA) – Follow Up Minyoung Park
[11] 11-24/0868r0 Additional Considerations on Non-Primary Channel Access Leonardo Lanante