## Slide 1: Backscattering UL data rate and modulation
Date: 2024-11-09
Authors:

## Slide 2: Introduction
The low power tag hardware characteristics have been discussed and compared [1, 2]
The design implication to DL data rate and SYNC design is discussed [2]
In this presentation, we focus on the discussion on the UL data rates and modulation.

## Slide 3: Recap: Backscattering Tag Reading
Reader sends carrier waveform to the tag
Tag backscatter the carrier waveform and modulates the Control response and Data payload
The backscattering data rate is limited by the achievable clock rate.
Control Frame
Data backscattering
WiFi reader
Tag
Control Response
Control Frame
AMP DL PPDU
Control Frame
Wakeup portion
Read control Exchange
Backscattering data read

## Slide 4: UL Data Rate
The nominal operation clock of backscattering tags is ~2MHz, [2].
With Manchester coded data, maximum backscattering UL data rate can be supported 1Mbps.
Good to have another low data rate to enhance detection reliability and range
  E.g. support reading range with blockage

## Slide 5: Backscattering UL Modulation
Manchester Encoding (ME) is agreed as non-backscattered communication modulation scheme [4].
For backscattering,
  UHF Gen2 standards [5] define FM0, with transition at every bit’s boundary
  ME has transition within each bit
  Reader can detect transition with tag modulation clock ppm
Suggest to unify backscattering modulation to ME.

## Slide 6: Backscattering UL Modulation
Manchester Encoding (ME) is agreed as non-backscattered communication modulation scheme [4].
For backscattering,
  UHF Gen2 standards [5] define FM0, with transition at every bit’s boundary
  ME has transition in the middle of each bit
  Differential Manchester Encoding is similar to FM0 with per-bit boundary transition.
  Reader can detect transition with tag modulation clock ppm
Suggest to unify backscattering modulation to ME.

## Slide 7: Simulation Settings
2x2 WiFi device in “1Tx + 1Rx” mode
  Antenna isolation is 20dB  Rx power of -20dBm
    Effective Rx noise floor of -35dBr
WiFi reader Rx BW = 40MHz, 10-bit ADC
  Fixed AGC gain to get I/Q samples
  Leakage removal using reference symbols
  Matched filter to detect modulation boundary
AMP tag:
  Backscattering data rate: 250kbps and 1Mbps
  Manchester Encoded OOK modulation: -20 dBr Tx noise
  Payload: 1000 bits
  2MHz Tag Rx nominal clock rate with high ppm
Leakage signal: 0dBr
Rx noise floor: e.g. -35dBr
BS signal level: e.g. -30dBr

## Slide 8: Tag reading performance
Coherent detector
6dB better sensitivity of 250kbps than 1mbps

## Slide 9: Tag Reading Performance: Distance
Coherent Detector
1mbps barely meet 10cm reading distance

## Slide 10: Tag reading performance
Non-coherent detector, 3~5dB loss
4dB better sensitivity of 250kbps than 1mbps

## Slide 11: Tag Reading Performance: Distance
Non-coherent Detector
1mbps reading distance is below 10cm

## Slide 12: Discussions
High rate of 1Mbps can
  barely meet the 10cm reading distance with coherent detector
  Miss the 10cm target with non-coherent detector
Good to have a lower data rate
  250Kbps with 6dB margin
  To accommodate different practical cases, like penetration loss, hardware impairments
  Can use as a retry mode to better use experience
  For common use case with smaller payload (96 bits EPC), the duration is ~400us.

## Slide 13: Summary
Discuss AMP backscattering UL design requirement
  Nominal clock rate of 2MHz  minimum pulse duration of 0.5us
  High ppm  Bit-level synchronization
With Manchester Encoding (ME)
  High data rate of 1Mbps
  Low data rate of 250Kbps

## Slide 14: SP
Do you agree that 11bp backscattering UL defines two data rate 1mbps and 250kbps?

## Slide 15: SP
Do you agree that 11bp backscattering modulation is defined as Manchester Encoded OOK?

## Slide 16: References
[1] 11-24/1475, Discussion on ultra-low power timing clock
[2] 11-24/1237, AMP-Tag-requirements-for-Mono-static-Backscattering
[3] 11-24/1163, WUR for Integrated Energizer Case
[4] 11-24/1345, High-Level Requirements for Downlink PHY in 2.4 GHz
[5] EPC UHF Gen2 Air Interface Protocol

## Slide 17: Appendix

## Slide 18: Differential Manchester Coding
Manchester coding requires coherent detection
  channel estimation and symbol demodulation
Differential Manchester coding
  the differential information between two adjacent symbols and
  utilized energy detection to perform decoding
  equivalent to half symbol left shifted FM0 waveform
  Same receiver design

## Slide 19: Tag Reading Performance: Attenuation
Differential MC, Coherent detection

## Slide 20: Tag Reading Performance: Distance
Differential MC, Coherent detection