## Slide 1: Seamless Roaming through a Target AP - Follow Up
Date: 2024-11-08
Authors:

## Slide 2: Introduction
In [1] we proposed seamless roaming through target AP MLD within an SMD, for the scenarios when seamless roaming through serving AP may not be possible
Use case: a non-AP MLD has to perform a last-minute/panic roam and does not have strong enough RSSI to perform roaming through serving AP MLD
  This could be a common scenario in many enterprise deployments due to different building materials, obstacles, shafts, elevators etc.
  Supporting seamless roaming through target AP is important to improve roaming across all use cases
In [1] we covered two cases for seamless roaming through the target AP:
  Case 1: when roaming preparation is done before with the serving AP
  Case 2: when no roaming preparation is done before with the serving AP
In this presentation, we provide further details on roaming through the target AP

## Slide 3: Roaming Through Target AP (1)
Case 1: Roaming through Target AP MLD w/ roaming preparation
PTK/PMK installed on target AP
Roaming request is PMF protected
Target AP MLD needs to:
  Identify the non-AP MLD
  Use the corresponding PTK to decrypt roaming req
  Perform replay detection
  Fetch context from serving AP
  Perform DS mapping update
NOTE: roaming prep can be done with just one Target AP as well.

## Slide 4: Roaming Through Target AP (2)
Case 2: Roaming through Target AP MLD w/o roaming preparation
PTK/PMK may or may not be installed on the target AP
Roaming request is PMF protected
Target AP MLD needs to:
  Identify the non-AP MLD
  Fetch (if needed) corresponding PTK to decrypt roaming req
  Perform replay detection
  Fetch context (dynamic and static) from serving AP
  Perform DS mapping update

## Slide 5: Solution Considerations (1)
Identifying the non-AP MLD at the target AP MLD (within same SMD)
  Roaming request is PMF protected
  TA (Transmitter Address) of the frame is used to identify the non-AP MLD
  We propose that a non-AP MLD provides a Roaming MAC Address (RMA) to its serving AP as part of initial 4-way HS, and uses that as TA in roaming request to target AP MLD
    This addresses 11bi cases where non-AP MLD randomly changes its STA MAC addresses
    Non-AP MLD also provides a new RMA in the roaming request for use in the next roaming
  Serving AP MLD shares the RMA with neighboring APs of the SMD (in a pre-roaming step, see next slide)
  Target AP MLD processes a roaming request if it recognizes the TA (set to RMA)
    Uses the TA to retrieve the PTKSA for that non-AP MLD
    Else, if TA is not recognized, target AP won’t know which PTK to use and drops the roaming request

## Slide 6: Solution Considerations (2)
Pre-roaming preparation by the serving AP
  A serving AP can proactively prepare its neighboring APs (e.g. all its 1-hop neighbors) with static context –such as roaming MAC Address and security associations (PMKSA, PTKSA)
  This enables a non-AP MLD to perform roaming through target AP with these neighboring APs, for cases when roaming can’t be done through serving AP
  Pre-roaming prep with neighboring APs can be done by the serving AP right after the association or after roaming to a new AP, without any client trigger

## Slide 7: Solution Considerations (3)
Replay detection at the target AP
  Roaming request is PMF protected with PTK
  PN based replay detection can only be done after the dynamic context is fetched from serving AP MLD
  However, it is important to check for replay i.e. liveness of the roaming request before target AP initiates any context fetch over the backhaul to avoid DoS attacks
  This can be achieved as follows:
    Option1: Roaming request includes an estimated TSF of the target AP. Can be computed by the non-AP MLD based on the latest beacon, probe response, RNR it has acquired for the target AP. Estimated TSF can be included as part of AAD data for encryption. Target AP verifies if received TSF is within some threshold of current TSF, if not then roaming request is discarded.
    Option 2: Roaming request includes a Roaming Transition Seq Num (RTSN) that is provided and incremented by the non-AP MLD for each roaming in the SMD. RTSN is synced between neighboring APs over the backhaul (e.g. as part of pre-roaming step). If a target AP receives an RTSN that is <= its latest RTSN state, the roaming request is discarded.
  PN based replay detection is preformed as 2nd level of replay detection after PN context is fetched from the old serving AP

## Slide 8: Solution Considerations (4)
Context transfer and DS mapping change
  If roaming prep was done with the target AP MLD, then near static context (SCS, TWT etc) are already transferred/negotiated with the target AP. In the roaming req, non-AP MLD does not signal to transfer any static context
  If roaming prep was not done with the target AP, then in the roaming req non-AP MLD signals which specific static context to transfer from old serving AP MLD (SCS, TWT etc) + include any static context that it wants to renegotiate
  Target AP MLD fetches dynamic context (SN, PN, BA) + any static context indicated by the non-AP MLD from the serving AP MLD
  Target AP MLD initiates DS mapping change after receiving context from the serving AP MLD and then sends a roaming response

## Slide 9: Summary
In many deployments STA may need to perform last-minute/panic roam because its RSSI suddenly dropped due to obstacles/shafts/elevators and/or power save etc.
Supporting seamless roaming through target AP is important to provide improved roaming across different types of deployments and conditions
Roaming through target AP must be supported for both - a) when a roaming prep done, & b) when roaming prep was not done; because a STA may need to perform last-minute roam in both cases
We propose following solutions:
  Roaming request/response exchange through target AP is PMF protected
  Use a Roaming MAC Address (RMA) as TA to identify the non-AP MLD, RMA is provided by the STA during assoc or last roaming procedure, target AP retrieves corresponding PTK based on TA
  Serving AP performs a pre-roaming prep to share static context (roaming MAC addr, PMKSA, PTKSA) with neighboring APs (e.g. a subset of APs in the SMD)
  Roaming request includes parameter for replay detection to avoid DoS attacks – e.g. an estimated TSF of target AP, or a Roaming Transition Seq Num
  Roaming request can signal which static context to be fetched and which to be renegotiated (same as roaming through serving AP), the data exchange context (PN, SN, BA) is preserved

## Slide 10: SP1
Do you agree to add following to 11bn SFD?
11bn defines that as part of seamless roaming procedure a non-AP MLD in state 4 can perform roaming transition through a target AP MLD.

## Slide 11: SP2
Do you agree to add following to 11bn SFD?
11bn defines that as part of seamless roaming procedure, a non-AP MLD in state 4 can send a protected request frame over-the-air to a target AP MLD:
  The request frame initiates context transfer from the current AP MLD to the target AP MLD or the context can be negotiated with the target AP MLD
  The request frame initiates necessary changes of the DS mapping from the current AP MLD to the target AP MLD
  Define a response frame sent by the target AP MLD to the non-AP MLD to indicate the readiness for the non-AP MLD to send class 3 frames to the target AP MLD
  NOTE: Details on what context can be transferred or negotiated is TBD

## Slide 12: References
[1] 11-24-398 “Coordinated Roaming through Target AP MLD”
[2] 11-24-396 “Seamless Roaming within a Mobility Domain – Follow Up”
[3] 11-23-2157 “Seamless Roaming within a Mobility Domain”
[4] 11-22-1910 “Seamless Roaming for UHR”
[5] 11-23-1996 “Improve roaming between MLDs”
[6] 11-24-0052 “Seamless Roaming Details”