## Slide 1: On OFDMA and MU-MIMO
Date: 2025-01-12
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 
Karim Toussi | Broadcom |  |  | 
Youhan Kim | Qualcomm |  |  | 

## Slide 2: Introduction
Supporting MU-MIMO on one or more RUs in an OFDMA PPDU exist since 11ax but not utilized
In 11be an attempt was made to simplify it by limiting MU-MIMO to RU>=242 (as opposed to 106RU) but it didn’t help spur the adoption of this feature
In this contribution we propose a set of combinations of OFDMA+MU-MIMO which we think are important to implement and test

## Slide 3: Use Cases
Two main use cases are driving our renewed interest in MU-MIMO+OFDMA in 11bn:
  DSO – in order to keep spectral efficiency high we need to be able to do MU-MIMO on the primary channel as well as the secondary channel servicing DSO clients
  Mix of higher BW and lower BW clients where the lower BW clients on the primary channel and the higher BW clients on the secondary channel can use MU-MIMO
Based on these use cases we therefore limit ourselves to a maximum of two MU-MIMO RUs in 160MHz and 320MHz UHR PPDUs only

## Slide 4: Proposal
In order to minimize options and spur adoption we propose to focus on the following RU sizes for MU-MIMO in OFDMA:
  160MHz PPDU – 996 and 484+242
    996 being half the BW and 484+242 to enable puncturing
  320 MHz PPDU: 996+484, 2x996, 2x996+484, 3x996
    Either 160MHz or 240Hz belong to one group (with allowance to puncturing)
As mentioned in slide 3 a maximum of 2 RUs can support MU-MIMO
Furthermore, each 80 MHz segment should be either MU-MIMO or OFDMA

## Slide 5: Proposed Changes in the RU Allocation Table (1)
Value | RU Alloc subfield | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
64-71 | 0 0100 0xxx | 242 |  |  |  |  |  |  |  |  | 8
72-79 | 0 0100 1xxx | 484 |  |  |  |  |  |  |  |  | 8
80-87 | 0 0101 0xxx | 996 |  |  |  |  |  |  |  |  | 8
88-95 | 0 0101 1xxx | 2x996 |  |  |  |  |  |  |  |  | 8
96-103 | 0 0110 0xxx | 484+242 (x111) |  |  |  |  |  |  |  |  | 8
104-111 | 0 0110 1xxx | 484+242 (1x11) |  |  |  |  |  |  |  |  | 8
112-119 | 0 0111 0xxx | 484+242 (11x1) |  |  |  |  |  |  |  |  | 8
120-127 | 0 0111 1xxx | 484+242 (111x) |  |  |  |  |  |  |  |  | 8
128-135 | 0 1000 0xxx | 996+484 (x111) |  |  |  |  |  |  |  |  | 8
136-143 | 0 1000 1xxx | 996+484 (1x11) |  |  |  |  |  |  |  |  | 8
144-151 | 0 1001 0xxx | 996+484 (11x1) |  |  |  |  |  |  |  |  | 8
152-159 | 0 1001 1xxx | 996+484 (111x) |  |  |  |  |  |  |  |  | 8
160-167 | 0 1010 0xxx | 3x996 (x111) |  |  |  |  |  |  |  |  | 8
168-175 | 0 1010 1xxx | 3x996 (1x11) |  |  |  |  |  |  |  |  | 8
176-183 | 0 1011 0xxx | 3x996 (11x1) |  |  |  |  |  |  |  |  | 8
184-191 | 0 1011 1xxx | 3x996 (111x) |  |  |  |  |  |  |  |  | 8
EHT
Value | RU Alloc subfield | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
64 | 0 0100 0000 | 242 |  |  |  |  |  |  |  |  | 1
65-71 | 0 0100 0001~0 0100 0111 | Validate |  |  |  |  |  |  |  |  | 7
72 | 0 0100 1000 | 484 |  |  |  |  |  |  |  |  | 1
73-79 | 0 0100 1001~0 0100 1111 | Validate |  |  |  |  |  |  |  |  | 7
80-87 | 0 0101 0xxx | 996 |  |  |  |  |  |  |  |  | 8
88-95 | 0 0101 1xxx | 2x996 |  |  |  |  |  |  |  |  | 8
96-103 | 0 0110 0xxx | 484+242 (x111) |  |  |  |  |  |  |  |  | 8
104-111 | 0 0110 1xxx | 484+242 (1x11) |  |  |  |  |  |  |  |  | 8
112-119 | 0 0111 0xxx | 484+242 (11x1) |  |  |  |  |  |  |  |  | 8
120-127 | 0 0111 1xxx | 484+242 (111x) |  |  |  |  |  |  |  |  | 8
128-135 | 0 1000 0xxx | 996+484 (x111) |  |  |  |  |  |  |  |  | 8
136-143 | 0 1000 1xxx | 996+484 (1x11) |  |  |  |  |  |  |  |  | 8
144-151 | 0 1001 0xxx | 996+484 (11x1) |  |  |  |  |  |  |  |  | 8
152-159 | 0 1001 1xxx | 996+484 (111x) |  |  |  |  |  |  |  |  | 8
160-167 | 0 1010 0xxx | 3x996 (x111) |  |  |  |  |  |  |  |  | 8
168-175 | 0 1010 1xxx | 3x996 (1x11) |  |  |  |  |  |  |  |  | 8
176-183 | 0 1011 0xxx | 3x996 (11x1) |  |  |  |  |  |  |  |  | 8
184-191 | 0 1011 1xxx | 3x996 (111x) |  |  |  |  |  |  |  |  | 8
UHR
Keep 242RU and 484RU only for full BW MU-MIMO

## Slide 6: Proposed Changes in the RU Allocation Table (2)
EHT
UHR
Value | RU Alloc subfield | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
192-199 | 0 1100 0xxx | 3x996+484 (x1111111) |  |  |  |  |  |  |  |  | 8
200-207 | 0 1100 1xxx | 3x996+484 (1x111111) |  |  |  |  |  |  |  |  | 8
208-215 | 0 1101 0xxx | 3x996+484 (11x11111) |  |  |  |  |  |  |  |  | 8
216-223 | 0 1101 1xxx | 3x996+484 (111x1111) |  |  |  |  |  |  |  |  | 8
224-231 | 0 1110 0xxx | 3x996+484 (1111x111) |  |  |  |  |  |  |  |  | 8
232-239 | 0 1110 1xxx | 3x996+484 (11111x11) |  |  |  |  |  |  |  |  | 8
240-247 | 0 1111 0xxx | 3x996+484 (111111x1) |  |  |  |  |  |  |  |  | 8
248-255 | 0 1111 1xxx | 3x996+484 (1111111x) |  |  |  |  |  |  |  |  | 8
256-263 | 1 0000 0xxx | 2x996+484 (x11111) |  |  |  |  |  |  |  |  | 8
264-271 | 1 0000 1xxx | 2x996+484 (1x1111) |  |  |  |  |  |  |  |  | 8
272-279 | 1 0001 0xxx | 2x996+484 (11x111) |  |  |  |  |  |  |  |  | 8
280-287 | 1 0001 1xxx | 2x996+484 (111x11) |  |  |  |  |  |  |  |  | 8
288-295 | 1 0010 0xxx | 2x996+484 (1111x1) |  |  |  |  |  |  |  |  | 8
296-303 | 1 0010 1xxx | 2x996+484 (11111x) |  |  |  |  |  |  |  |  | 8
304-319 | 1 0011 xxxx | Disregard |  |  |  |  |  |  |  |  | 16
320-383 | 1 01xx xxxx | Disregard |  |  |  |  |  |  |  |  | 64
384-511 | 1 1xxx xxxx | Disregard |  |  |  |  |  |  |  |  | 128
Value | RU Alloc subfield | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
192 | 0 1100 0000 | 3x996+484 (x1111111) |  |  |  |  |  |  |  |  | 1
193-199 | 0 1100 0000~0 1100 0111 | Validate |  |  |  |  |  |  |  |  | 7
200 | 0 1100 1000 | 3x996+484 (1x111111) |  |  |  |  |  |  |  |  | 1
201-107 | 0 1100 1001~0 1100 1111 | Validate |  |  |  |  |  |  |  |  | 7
208 | 0 1101 0000 | 3x996+484 (11x11111) |  |  |  |  |  |  |  |  | 1
209-215 | 0 1101 0001~0 1101 0111 | Validate |  |  |  |  |  |  |  |  | 7
216 | 0 1101 1000 | 3x996+484 (111x1111) |  |  |  |  |  |  |  |  | 1
217-223 | 0 1101 1001~0 1101 1111 | Validate |  |  |  |  |  |  |  |  | 7
224 | 0 1110 0000 | 3x996+484 (1111x111) |  |  |  |  |  |  |  |  | 1
225-231 | 0 1110 0001~0 1110 0111 | Validate |  |  |  |  |  |  |  |  | 7
232 | 0 1110 1000 | 3x996+484 (11111x11) |  |  |  |  |  |  |  |  | 1
233-239 | 0 1110 1001~0 1110 1111 | Validate |  |  |  |  |  |  |  |  | 7
240 | 0 1111 0000 | 3x996+484 (111111x1) |  |  |  |  |  |  |  |  | 1
241-247 | 0 1111 0001~0 1111 0111 | Validate |  |  |  |  |  |  |  |  | 7
248 | 0 1111 1000 | 3x996+484 (1111111x) |  |  |  |  |  |  |  |  | 1
249-255 | 0 1111 1001~0 1111 1111 | Validate |  |  |  |  |  |  |  |  | 7
256-263 | 1 0000 0xxx | 2x996+484 (x11111) |  |  |  |  |  |  |  |  | 8
264-271 | 1 0000 1xxx | 2x996+484 (1x1111) |  |  |  |  |  |  |  |  | 8
272-279 | 1 0001 0xxx | 2x996+484 (11x111) |  |  |  |  |  |  |  |  | 8
280-287 | 1 0001 1xxx | 2x996+484 (111x11) |  |  |  |  |  |  |  |  | 8
288-295 | 1 0010 0xxx | 2x996+484 (1111x1) |  |  |  |  |  |  |  |  | 8
296-303 | 1 0010 1xxx | 2x996+484 (11111x) |  |  |  |  |  |  |  |  | 8
304-319 | 1 0011 xxxx | Disregard |  |  |  |  |  |  |  |  | 16
320-383 | 1 01xx xxxx | Disregard |  |  |  |  |  |  |  |  | 64
384-511 | 1 1xxx xxxx | Disregard |  |  |  |  |  |  |  |  | 128
Keep 3x996+484RU only for punctured full BW MU-MIMO

## Slide 7: Summary
Proposed a limited set of combinations to support MU-MIMO +OFDMA to spur adoption of this feature in light of DSO and mixed BW devices

## Slide 8: SP#1
Do you agree to add to the 11bn SFD?
  MU-MIMO+OFDMA in both DL and UL is limited to UHR PPDU of 160 and 320MHz only
    160MHz PPDU – 996 and, when the PPDU is punctured, 484+242
    320 MHz PPDU: 2x996, 3x996 and, when the PPDU is punctured, 996+484, 2x996+484
  MU-MIMO+OFDMA is further limited to a maximum of 2RUs supporting MU-MIMO and each 80MHz segment is either MU-MIMO or OFDMA
  RU Allocation table in UHR-SIG is the same as that in EHT-SIG except that the rows for RU 242, 484 and 3x996+484 with two or more users are changed to Validate