## Slide 1: Efficient UHR-SIG encoding
Date: 7-Nov-24
Authors:

## Slide 2: Introduction
Several proposals have been made for encoding modulation/coding information in UHR-SIG [1, 3, 5, 6, 7]
Currently (11be), User fields are 22 bits long
Keeping UHR User fields the same length (22 bits) wil improve compatibility with 11be
One of the main questions is whether all information can fit into a 22-bit User field
Note: focus is on non-MU MIMO User field

## Slide 3: Goal of the submission
Demonstrate that it is possible to accommodate all required signaling within a 22 bits User Field
  Existing EQM 1-8 SS (with BF/Coding Type)
  New MCS EQM 1-8 SS (with BF/Coding Type)
  UEQM 1-4 SS, all agreed patterns
  (if needed): 1x/2x LDPC CW
Present a specific proposal of such signaling that:
  Uses 22 bits User Field
  Naturally reverts to EHT signaling when none of the new features (UEQM, new MCS, 2xLDPC, …) are used
  Maintains reserved bit(s) for future extension

## Slide 4: How many UEQM Combinations?
Proposals [1, 6, …] specify the UEQM as a combination of Base MCS and UEQM Pattern.
The UEQM pattern specifies the modulation index over the different streams
  E.g.: Base MCS=7, Pattern [M, M, M-1] corresponds to a 3-stream UEQM (64 QAM, 64 QAM, 16 QAM) with code rate 5/6.
However, this ignores the fact that many combinations of (Base MCS, UEQM Pattern) are in fact not valid UEQM
  M-1 or M-2 may not be a valid value
  M-1, M-2 may not share a code rate with the base MCS

## Slide 5: Signaling – Valid UEQM Combinations
There are 162 combinations that can be signaled
  9 Patterns x 18 MCS †, see Appendix 1
Of the 162 possible combinations, 60 do not map to a valid UEQM (See Appendix 2)
  12 out of 36 for NSS=2
  20 out of 54 for NSS=3
  28 out of 72 for NSS=4
† Including new MCS

## Slide 6: Signaling – UEQM Summary
There are really only 102 UEQM that need to be signaled
Defining UEQM as a (Base MCS, Pattern) combination is inefficient as it would result in a significant number of invalid combinations

## Slide 7: UHR required signaling
Prior to discussing ways to encode the information in the User field, let’s establish how many combinations need to be covered
  Will it fit in 10 bits?
The combinations contain the following:
  “Legacy” EQM MCS/NSS/BF/Coding combinations:
    16 x 8 x 2 x 2 = 512†
  New MCS/NSS/BF/Coding combinations
    4 x 8 x 2 x 2 = 128
  UEQM
    102††
† Strictly speaking, MCS 14 and 15 only support one SS, so the actual number would be (14 x 8 + 2) x 2 x 2 = 456
†† This assumes that UEQM always uses BF. There is already an agreement that UEQM always uses LDPC, so no need for Coding Type indication

## Slide 8: UHR Required signaling
The total number of combinations is therefore 742
Since log2(742) ≈ 9.5, this information would (theoretically) fit within 10 bits
Assuming the STAID field is kept at 11 bit, it should therefore be possible to encode all information in a User field of 22 bits, leaving one more (reserved) bit available for additional signaling
While theoretically possible, the encoding also needs to be convenient and practical

## Slide 9: Practical encoding
The set of 742 could be split into two subsets requiring 9 bits each
It was proposed earlier to have an EQM/UEQM split
However, this results in a very unbalanced split of the required combinations
The EQM signaling alone (640 combinations) would require 10 bits, making it no longer possible to maintain a 22-bit User field

## Slide 10: Practical encoding (2)
A more convenient split is “existing MCS” (i.e., already supported in EHT) vs. “newly added MCS”
This split allows each subset to be encoded in 9 bits, achieving the theoretical value of 10 bits for signaling all combinations
The next step is to determine a practical encoding for each subset

## Slide 11: Encoding of “EHT combinations”
The encoding of the “legacy” combinations can maintain the 9-bit structure used in EHT
The 9 bits would consist of the following fields:
This covers all MCS up to 8 SS, allowing for BF and Coding Type indication
  Same as in EHT – no regression

## Slide 12: Encoding of “new MCS”
For the new EQM (see Appendix 1), the information can be encoded in 7 bits following a similar structure:
For the 102 UEQM combinations, the most efficient way is to refer to each combination as an entry in a lookup table
  This also requires only 7 bits

## Slide 13: Encoding of “new MCS” – EQM and UEQM
All (230) new MCS (EQM and UEQM) can then be combined into 8 bits:

## Slide 14: Encoding of “new MCS”
For EQM, we maintain the “traditional” encoding fields (MCS, NSS, Coding, BF)
  No unused bits, 7 bits to signal 128 values
For UEQM, the valid UEQM are listed in a lookup table and the index to the corresponding entry is coded in U-SIG
  Partitioning per NSS doesn’t make sense since different NSS values required different number of UEQM
  7 bits to signal 102 values  consistent with agreed patterns
  Most efficient way of storing and communicating the information

## Slide 15: 22-bit User field Proposal
Use B19 as “MCS extension” bit
Same format as EHT

## Slide 16: UHR Signaling Properties
User field of 22 bits
For all “Legacy” Modes, User field is identical to EHT – by design
  Appropriate since Data Field will be indistinguishable from EHT
New modes (MCS, LDPC, …) are easily distinguishable from EHT
  New MCS are comprehensively separated in EQM and UEQM
Simple decision tree to derive modulation parameters
One or two of the 22 bits have reserved value

## Slide 17: Use of reserved bits
At least one reserved bit is available for all MCS
  It has been suggested that 1x/2x LPDC CW size should be signaled
One additional reserved bit is available for the “new MCS”
  Flexibility for future extension

## Slide 18: Summary
UHR signaling can be accommodated in a 22-bit User field
  Theoretically and practically
An efficient encoding of 22-bit U-SIG fields was proposed
Reserved bit available for possible 2x CW signaling
Future extension possible through use of additional reserved bit
Naturally extends 11be User field

## Slide 19: References
[1] 11-24/1411, Signaling for UHR PPDU
[2] 11-24/1186r1, 11-24-1186-01-00bn-new-mcss-for-11bn-follow-up
[3] 11-24/1409r0, 11-24-1409-00-00bn-unequal-pattern-discussion-follow-up
[4] 11-24/0474r3, 11-24-0474-03-00bn-uhr-unequal-modulation-pattern-and-new-mcs
[5] 11-24/1427r0, Signaling for MCS and UEQM in 11bn
[6] 11-24/1695r0, 11bn signaling design for extra MCS, UEQM, 2xLDPC
[7] 24/1461r0, UHR preamble signaling

## Slide 20: Straw Poll 1
Do you agree to include the following into the 11bn SFD?
  In a non-MU-MIMO User field, UEQM shall only be used with BF
Y/N/A:

## Slide 21: Straw Poll 2
Do you agree to include the following into the 11bn SFD?
  The length of a User field in UHR-SIG shall be the same as the User field in EHT- SIG (22 bits).
Y/N/A:

## Slide 22: Appendix 1: Base MCSs and UEQM Patterns
Rows in yellow are newly defined in 802.11bn
2SS Patterns
3SS Patterns
4SS Patterns

## Slide 23: Appendix 2: Invalid NSS=2 combinations
12 (MCS, Pattern) Combinations (out of 36) do not map to a valid UEQM

## Slide 24: Appendix 2: Invalid NSS=3 combinations
20 (MCS, Pattern) Combinations (out of 54) do not map to a valid UEQM

## Slide 25: Appendix 2: Invalid NSS=4 combinations
28 (MCS, Pattern) Combinations (out of 72) do not map to a valid UEQM