## Slide 1: Stream Parser for Unequal Modulation
Date: 2024-11-09
Authors:
Name | Affiliations | Address | Phone | email
Qinghua Li | Intel |  |  | qinghua.li@intel.com
Juan Fang |  |  |  | 
Shlomi Vituri |  |  |  | 
Assaf Gurevitz |  |  |  | 
Robert Stacey |  |  |  | 
Carlos Cordeiro |  |  |  | 

## Slide 2: Introduction
Unequal modulation across spatial streams was introduced in HT [2]
It has been revisited and adopted in UHR SFD [1]
A stream parser is needed to distribute coded bits to the spatial streams according to the modulation order of each stream, respectively
In this work, we investigate whether HT stream parser can be reused by UHR
Qinghua Li, Intel
Nov 2024

## Slide 3: Stream Parser in EHT
After post-FEC padding, coded bits are distributed into different spatial streams in a round robin fashion according to the modulation order
If the allocated bandwidth is greater than 80 MHz, the distributed bits per stream are then distributed to each frequency segment in a round robin fashion
Qinghua Li, Intel
Nov 2024
Pre-FEC PHY Padding
Scrambler
LDPC Encoder
Post-FEC Padding
Stream Parser
Segment Parser
Segment Parser

## Slide 4: 2-Stream Parsing in EHT
Qinghua Li, Intel
The stream parsing is bits by bits, where is the number of bits carried by each QAM component (real or imaginary)
For modulation order ,
where
s
s
s
s
s
s
…
s
s
s
s
s
s
…
…
Nov 2024

## Slide 5: HT Stream Parser
Qinghua Li, Intel
Nov 2024

## Slide 6: 2-Stream Parsing in HT
Qinghua Li, Intel
For modulation order, ,
s2
s2
s1
s1
s1
s2
…
s1
s1
s1
s2
s2
s2
…
…
Nov 2024

## Slide 7: Exclusion of BPSK from UEQM
Qinghua Li, Intel
BPSK has only one axis, the real axis, while the other QAMs has two axes
The per-axis round-robin parsing can’t be applied to BPSK without modification [3]
For implementation simplicity, it is desired that BPSK is excluded from UEQM
Nov 2024

## Slide 8: Reuse of HT Stream Parser for UHR UEQM with Slight Modifications
Qinghua Li, Intel
Reuse HT stream parser for UHR UEQM with the following restrictions and extension
  , for
  The encoder type is LDPC [1]
Nov 2024
Include 4K QAM and exclude BPSK

## Slide 9
Qinghua Li, Intel
Summary
Propose to reuse HT stream parser for UHR UEQM with slight modifications
Nov 2024

## Slide 10: Reference
Qinghua Li, Intel
[1] 11-24-0209-06-00bn-specification-framework-for-tgbn, Ross Jian Yu
[2] IEEE Std 802.11‐2020
[3] 11-24-1451-02-00bn-ueqm-transmission-over-spatial-streams, Ying Wang
Nov 2024

## Slide 11
Qinghua Li, Intel
SP 1
Do you support to add the following to UHR SFD?
Exclude BPSK from UHR UEQM.
Y:
N:
A:
Nov 2024

## Slide 12
Qinghua Li, Intel
SP 2
Do you support to add the following to UHR SFD?
Include 4K QAM in UHR UEQM.
Y:
N:
A:
Nov 2024

## Slide 13: SP 3
Qinghua Li, Intel
Do you support to add the following to UHR SFD?
add the following to UHR SFD?
Reuse HT stream parser for UHR UEQM with the following restrictions and extension
  , for
  The encoder type is LDPC
Nov 2024
Y:
N:
A:

## Slide 14
Qinghua Li, Intel
SP 4
Do you support to add the following to UHR SFD?
For equal modulation, UHR stream parser remains the same as EHT.
Y:
N:
A:
Nov 2024

## Slide 15
Qinghua Li, Intel
SP 5
Do you support to add the following to UHR SFD?
For bandwidths greater than 80 MHz, the coded bit parsing of UHR is stream parsing first followed by segment parsing.
Y:
N:
A:
Nov 2024

## Slide 16
Qinghua Li, Intel
SP 6
Do you support to add the following to UHR SFD?
Reuse HT stream parser in Slide 5 with the modifications in Slide 8 for UHR UEQM.
Y:
N:
A:
Nov 2024