## Slide 1
November 2024
Consideration on cascading channel switching for NPCA
Date: 2024-11-08
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Abstract
This document discusses the NPCA channel switch triggering conditions for NPCA-supporting STAs from another perspective (i.e., not about the PPDU format, not based on TXOP/PPDU/Service Period(SP), etc) when the primary channel is occupied due to a transmission caused by the NPCA operation of OBSS

## Slide 3: Motivation
Non-Primary Channel Access (NPCA) channel switch trigger conditions have been discussed in TGbn [1-5]
  TXOP/PPDU/Service Period based NPCA
  Control frame exchange/Pre-HE and HE+ format
If OBSS’s transmissions occupy the MyBSS primary channel and these transmissions are caused by NPCA operation of OBSS’s NPCA STA, should MyBSS NPCA STAs perform channel switching?
  It may be needed to consider whether NPCA operation should be performed for all OBSS frames detected on the BSS primary channel

## Slide 4: Channel switching for NPCA
The NPCA operation may increase spectral utilization of the unused secondary channel when the primary channel is occupied
However, it might be necessary to consider the advantages of NPCA when the BSS p-channel is occupied due to a transmission generated by NPCA operations between OBSS’s NPCA STAs
  When NPCA STAs are allowed to switch to the NPCA p-channel regardless of whether the OBSS frame is generated by NPCA operations, frequent channel switching may occur
    It can reduce power efficiency and degrade overall performance of the BSS
  Moreover, if a PPDU generated by OBSS NPCA STAs occupy the MyBSS p-channel, it can cause MyBSS NPCA STAs to switch to its NPCA p-channel(Ch1); this may also trigger another OBSS NPCA STAs, which use the aforementioned NPCA p-channel(Ch1) as their BSS p-channel, to switch to their designated NPCA p-channel(Ch2)
    It can lead to cascading channel switching behavior, which may impact the entire network throughput

## Slide 5: Cascading channel switching for NPCA
If the NPCA channel switching conditions can be triggered by NPCA operation of an OBSS, we can consider it from two scenarios
  S1) When OBSS NPCA STAs switch to MyBSS p-channel
    The number of backoff contenders on the MyBSS p-channel could be increased
      OBSS NPCA STAs have an advantage, but it can lead to disadvantage to MyBSS STAs
      If MyBSS STAs cannot access the channel, allowing MyBSS NPCA STAs to perform NPCA might be an efficient way
    However, there may be situations where waiting until the end of the frame exchange between OBSS’s NPCA STAs (i.e., at the time when switching back to their p-channel) on the MyBSS p-channel is more beneficial at some points than performing NPCA
      This is because we cannot ensure the NPCA p-channel for MyBSS NPCA STAs will be IDLE;
      In addition, since congestion due to OBSS NPCA STAs can be merely temporary, having MyBSS NPCA STAs switch channels while consuming power could reduce power effieciency
  S2) When MyBSS NPCA STAs switch channel due to NPCA operation of an OBSS (e.g., OBSS1)
    The other OBSS (e.g., OBSS2) that using the MyBSS NPCA p-channel as its BSS p-channel, this could increase the number of backoff contenders and potentially trigger NPCA operation in that OBSS (e.g., OBSS2)
      It can bring S1) recursively

## Slide 6: Example of cascading channel switching
BSS1
BSS2
BSS3
AP1
AP2
AP3
OBSS TXOP
BSS1 NPCA
STAs switch
BSS1 NPCA STAs switch back
BSS1 NPCA
BSS3 NPCA
STAs switch
BSS3 NPCA STAs switch back
BSS2 NPCA
BSS2 NPCA
STAs switch
BSS2 NPCA STAs switch back
BSS3 NPCA
Description :
  The NPCA available channels of BSS1/BSS2 overlap with the primary channels of BSS2/BSS3, respectively
Scenario :
  BSS1 NPCA STAs switch channel to its NPCA p-channel
    BSS1 NPCA STAs contend with BSS2 STAs, and with the channel contention
  BSS2 NPCA STAs switch channel to its NPCA p-channel
    BSS2 NPCA STAs contend with BSS3 STAs, and with the channel contention
  BSS3 NPCA STAs switch channel to its NPCA p-channel
    BSS3 NPCA STAs contend with BSS_X STAs and with the channel contention
  ……
…
Freq.
BSS1 NPCA available channel
(BSS2 primary channel)
BSS2 NPCA available channel
(BSS3 primary channel)

## Slide 7: Prevent cascading channel switching
Since the NPCA p-channel during the NPCA operation can cause cascading channel switching of OBSS NPCA STAs, we consider methods to limit cascading channel switching
Proposal 1: Switch to the NPCA p-channel when an NPCA triggering event occurs from an OBSS with the same p-channel as MyBSS
  It can prevent cascading channel switching in advance
  However, when there are few OBSSs with the same p-channel with MyBSS, NPCA opportunities may be relatively limited

## Slide 8: Prevent cascading channel switching
Proposal 2: Including an explicit indication in the PPDU to notify that this PPDU is generated from the NPCA operation
  If the NPCA STA initiates frame exchange on the NPCA p-channel with an ICF, it may include an indication within the ICF to prevent NPCA operation of OBSS; and/or
  Indicate the NPCA mark within the UHR SIG field when transmitting UHR PPDU format
When NPCA STAs overhear the NPCA indication on their BSS p-channel, they may optionally choose whether to perform NPCA or not as follows :
  Opt 1) Do not perform NPCA until the OBSS NPCA STAs switch back to their p-channel
  Opt 2) Switching to NPCA p-channel to perform NPCA; After that, do not use untriggered transmission, considering the trade-off between the benefits of NPCA and the increase in backoff contenders due to NPCA
    Allow only the NPCA AP to attempt channel contention

## Slide 9: Summary
In this presentation, we discuss some approaches for NPCA STAs to mitigate the excessive NPCA which can cause cascading channel switching
  Switch to the NPCA primary channel when an NPCA triggering event occurs from an OBSS with the same primary channel as MyBSS
  Including an explicit indication in the PPDU
    ICF when NPCA STAs initiate frame exchange on the NPCA primary channel; and/or
    Transmission of UHR PPDU format between NPCA STAs on the NPCA available channel

## Slide 10: Reference
[1] 24/0495r0, Non-Primary Channel Access (NPCA) - Follow up
[2] 24/0496r1, Secondary Channel Usage Follow Up
[3] 24/1115r1, Channel Switching Rules for NPCA
[4] 24/1259r0, SP-based non-primary channel access follow-up
[5] 24/1218r1, NPCA – Next level discussions

## Slide 11: SP1
Do you agree to include an explicit indication in the ICF and/or UHR PPDU on the NPCA primary channel during NPCA operation?
  The details are TBD

## Slide 12: SP2
Do you agree to allow NPCA operation when the event triggering the switch to the NPCA primary channel is from an OBSS with the same primary channel as MyBSS primary channel?

## Slide 13: SP3
Do you agree to define a mode to decide whether or not performing NPCA when the BSS primary channel is occupied due to frame exchange between OBSS’s NPCA STAs based on NPCA operation?
  This mode can be enabled/disabled by the AP