## Slide 1: OBSS Sounding for C-BF
Date: 2024-11-xx
Authors:
Name | Affiliation | Address | Phone | Email
Insik Jung | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insik0618.jung@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
OBSS sounding is one of key feature to realize coordinated beamforming (C-BF) technology
  BSS STA estimates DL channel which comes from OBSS AP
  We simply point out that some signaling in NDPA might be required to trigger OBSS NDP
To prevent the OBSS packet decoding burden on the STA side, [1]-[3] have proposed using NDPA or BFRP Trigger frame only towards the in-BSS stations.
  Therefore, AP need to ‘overhear’ the required OBSS channel feedback matrix from the OBSS stations.
In this contribution, we propose a method to improve the ‘overhearing’ performance to realize C-BF

## Slide 3: OBSS Sounding (1/2)
Basic sounding principle proposed in [1]-[3] is as follows
  NDPA and BFRP trigger only address the BSS stations
    This is because addressing OBSS STA makes STAs to decode every OBSS packets, which can be huge computation burden
    We agree with this direction to minimize impact to client STAs
NDPA
NDP
BFRP
NDPA
NDP
BFRP
CSI
CSI
AP 1
AP 2
STA 1
STA 2
BSS channel information
OBSS channel information

## Slide 4: OBSS Sounding (2/2)
For the OBSS channel sounding, ‘AP2’ has to be ready to transmit NDP in response to the AP1’s NDPA
  This capability of NDPA/NDP procedure between APs should be negotiated in advance
  AP1 may need some signaling to indicate that the NDPA is now triggering OBSS NDP
NDPA
NDP
BFRP
CSI
OBSS channel information
AP 1
AP 2
STA 1
Indication to trigger OBSS NDP

## Slide 5: Problem Statement (1/2)
C-BF eliminates OBSS interference by applying null beamforming
  For this, each AP needs to know OBSS channel information
But the sounding procedures proposed in [1]-[3], OBSS CSI feedback frames do not address the AP that actually needs to utilize the OBSS CSI information
  The AP have to ‘overhear’ the OBSS CSI
Other possible solutions are additionally delivering the CSI information or using wired backhaul if implemented, but it’s not recommended due to medium overhead or backhaul capacity burden

## Slide 6: Problem Statement (2/2)
AP 1 does not know the quality of overhearing link
  For this reason, BFRP would trigger the CSI feedback frame based on the quality of CSI reporting link
However, receivable MCS/Nss can be different between reporting and overhearing link
  Note that In-BSS SNR is mostly better than OBSS SNR  we may need some AP collaboration to enable AP 2’s decoding
CSI reporting link
OBSS CSI reporting link
AP 1
AP 2
STA 1
STA 2

## Slide 7: OBSS Overhearing Link Quality Report
If AP 2 directly deliver its overhearing link quality information to AP 1, the problem can be solved
AP 1
AP 2
STA 1
STA 2
CSI reporting link (L1, addressed)
OBSS CSI reporting link (L2, overhearing)
L2 quality information
L2 quality information can be one of the followings:
  Overhearing link SINR
    AP 1 can determine the MCS/Nss of the CSI report based on the overhearing link SINR
  Preferred MCS/Nss
    AP 1 can trigger with the recommended MCS/Nss from AP 2

## Slide 8: Required Informations
We propose to deliver the following information through AP to AP signaling
  STA-ID: Identifier to specify a station
  L2 Information: Information related to the overhearing link. It can be a SINR of the overhearing link or preferred MCS/Nss
  We may need to signal multiple sets of (STA-ID, L2 information)
Let us call this information as ‘OBSS CSI reporting link information’
STA-ID
L2 information
STA-ID
L2 information
…

## Slide 9: Proposed Sequence
Once the overhearing link quality is obtained by AP 2, it can be transmitted anytime before the AP 1’s BFRP
  How AP 2 get the overhearing link quality information is TBD (e.g. from AP1’s in-BSS frame exchange or sounding)
  One example can be as below:
NDPA
OBSS CSI reporting link information
BFRP
CSI
AP 1
AP 2
STA 1
STA 2
NDP
Overhearing quality acquisition

## Slide 10: Conclusion
OBSS sounding mechanism for C-BF has been handled in this contribution
  We simply pointed out that some signaling in NDPA might be required to trigger OBSS AP’s NDP
We then have pointed out the feedback overhearing problem for C-BF
  We found that feedback overhearing may fail because of the link quality mismatch between the BSS reporting link and the overhearing link
  To solve the problem, we have proposed an AP to AP frame exchange to deliver the overhearing channel quality information

## Slide 11: References
[1] 11-24-1582-00, Coordinated Sounding for CoBF
[2] 11-24-1568-00, Sounding Design for C-BF
[3] 11-24-1542-00, Sounding Schemes for Coordinated Beamforming

## Slide 12: Straw Poll #1
Do you agree to include following to the 11bn SFD?
  11bn defines sounding procedures (i.e. sequential and joint) to measure the downlink channel heading to the OBSS STAs for C-BF
    NDPA and BFRP frames only address the in-BSS stations in the C-BF sounding sequence.
    A UHR AP may indicate to another AP its capability of transmitting NDP in response to the AP’s NDPA
Y/N/A: //

## Slide 13: Straw Poll #2
Do you agree to include following to the 11bn SFD?
  UHR NDPA frame that an AP transmits may include a signaling where it enables a neighboring AP to transmit NDP
Y/N/A: //

## Slide 14: Straw Poll #3
Do you agree to include following to the 11bn SFD?
  Defines a mechanism where an AP transmits to a neighboring AP link quality information measured from a PPDU transmitted from STAs associated with the neighboring AP that are capable of participating in C-BF
Y/N/A: //
Notes: Between보다는 방향성 언급해주는게 나을 듯
-Measured link is STA associated with neighboring AP to the AP

## Slide 15: Straw Poll #4
Do you agree to include following to the 11bn SFD?
  11bn supports a frame containing the link quality information between the AP and a STA associated with a neighboring AP that includes information as follows
    STA-ID field
    OBSS CSI reporting link SINR or preferred MCS/Nss
  NOTE
    There can be multiple sets of the above information in a single container
Y/N/A: //