## Slide 1
Name | Affiliation | Address | Phone | Email
Rojan Chitrakar | Huawei | Singapore |  | rojan.chitrakar@huawei.com
Lei Huang |  |  |  | 
Ian Bajaj |  |  |  | 
AMP client STA types
Date: 8 November 2024
Notes: Jul 12, 2010
Page 1

## Slide 2: Recap: Proposed AMP Terminology [1]
The following terminologies for client STA types were proposed in [1]:
AMP non-AP STA: A non-AP STA that supports AMP operation. AMP non-AP STA can be subdivided into 3 categories based on functionality:
  Type-A AMP STA: An AMP non-AP STA that support existing WLAN standards (e.g. 2.4 GHz 11b/n).
  Type-B AMP STA: An AMP non-AP STA that only support low power active transmitter which is not compliant with existing WLAN standard.
  Type-C AMP STA: An AMP non-AP STA that only support backscatter operation.
Some feedback were received at the time that the AMP non-AP STAs sub-types could be defined as STA capabilities.

## Slide 3: Selected examples from previous 802.11 amendments
sensor station (STA): [sensor STA] A sub 1 GHz (S1G) non-access point (non-AP) STA that has certain
traffic and device characteristics (e.g., limited payload size, limited traffic volume, battery operated device)
and is allowed to associate with an access point (AP) that transmits an S1G Beacon, a Probe Response, or a
PV1 Probe Response frame containing the S1G Capabilities element with the STA Type Support subfield
indicating a sensor basic service set (BSS) or a mixed BSS.
quality-of-service (QoS) management frame (QMF) station (STA): [QMF STA] A quality-of service STA that implements the QMF service.
WUR non-AP STA: A WUR non-AP STA is a non-HT, HT, VHT, or HE non-AP STA that is capable of receiving WUR PPDUs and supports the WUR operation. A WUR non-AP STA has a capability to receive a WUR PPDU at a power
consumption of less than 1 milliwatt.
20 MHz-only non-access point (non-AP) extremely high throughput station (EHT STA): [20 MHz-only non-AP EHT STA] A non-AP EHT STA that indicates in the Supported Channel Width Set subfield in the HE PHY Capabilities Information field in the HE Capabilities element that it supports only 20 MHz channel width for the frequency band in which it is operating.

## Slide 4: Various names used for client STAs in 802.11bp contributions
Name used in AMP Technical Report [2] | AMP only IoT STA |  |  | AMP Assisted STA
Contributors |  |  |  | 
Bin Qian et. al. | Mono-static Backscatter Tag | Bi-static Backscatter Tag | Active Transmitter tag/STA | Enhanced Legacy STA
Steve et. al. | Close range mono-static backscatter | Bi-static backscatter | Active TX Uplink | Low Power Legacy STA
Weijie et. al. | Short range backscatter | Long range backscatter | Active transmitter | Legacy OFDM transmitter
Rui Cao et. al. | Mono-static backscattering AMP tags | - | - | -
Amichai et. al. | - | Long distance backscatter | Active transmitter | -
Our Proposal (Based on hardware capabilities) | Backscatter non-AP AMP STA (Mono-static*1) | Backscatter non-AP AMP STA (Bi-static*1) | Active Uplink Tx non-AP AMP STA | AMP Assisted non-AP STA
Note 1: Indicates the mode of operation and is not part of the STA name. |  |  |  | 

## Slide 5: Proposed definitions
We propose the following terminologies for AMP client STAs for ease of specification drafting:
Backscatter non-AP AMP STA: An non-AP AMP STA that supports reception of AMP PPDU and is only capable of backscatter transmission.
Active Uplink Tx non-AP AMP STA: An non-AP AMP STA that supports reception of AMP PPDU and is only capable of low power active uplink transmission of AMP PPDU.
AMP Assisted non-AP STA: A non-AP AMP STA that is also a non-HT or HT non-AP STA that supports reception of AMP PPDU.

## Slide 6: SP 1
Do you agree to add the following terminologies to the 802.11 SFD:
Backscatter non-AP AMP STA: An non-AP AMP STA that supports reception of AMP PPDU and is only capable of backscatter transmission.
Active Uplink Tx non-AP AMP STA: An non-AP AMP STA that supports reception of AMP PPDU and is only capable of low power active uplink transmission of AMP PPDU.
AMP Assisted non-AP STA: A non-AP AMP STA that is also a non-HT or HT non-AP STA that supports reception of AMP PPDU.

## Slide 7: References
[1] 11-24/0482r1, AMP Terminology, Shuqiao Chen et. al.
[2] 11-23-0436-00-0amp-technical-report-on-support-of-amp-iot-devices-in-wlan