## Slide 1: TGbp PPDU preamble follow up
Date: 2024-11-11
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
In previous 802.11bp meeting, multiple DL PPDU formats were proposed and discussed [1-2].
Passed motion [3]:
    IEEE 802.11bp will specify, in 2.4 GHz, an AMP Downlink PPDU containing at least an 802.11 preamble field, an AMP-Sync field and an AMP-Data field. Inclusion of an AMP-SIG field is TBD.
      The details of the 802.11 preamble field are TBD.
      Additionally, for transmission to backscatter STAs there will be one or more Excitation fields
      Additionally, for transmission to backscatter STAs there may be more than one AMP-Data field
      Additionally, AMP-Sync and AMP-SIG field may precede each AMP-Data field
In this presentation, we would like to discuss our thought on the DL preamble part.

## Slide 3: TGbp OFDM-based preamble
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG1
U-SIG2
[2]
In our previous contribution [2], we proposed to have U-SIG for a better co-existence:
  PPDU of different Wi-Fi amendment can be differentiated via PHY version in U-SIG.
  For 802.11be and beyond, third-party STA receives an 802.11bp PPDU, it will honor the version independent fields in U-SIG, e.g., TXOP (less collision)
OFDM based Preamble
AMP Sync
AMP SIG
AMP Data
Third-party STAs (even for 802.11be and beyond): treat as 11a PPDU
[1]
L-STF
L-LTF
L-SIG
BPSKMark1
BPSKMark2
11ba
For 802.11be and beyond, third-party STAs:
decode U-SIG and honor the version independent fields, e.g., TXOP.

## Slide 4: Proposed U-SIG indication method for TGbp
PHY version and a Validate bit set to 0 in U-SIG can be used to indicate 802.11bp PPDU:
  For 802.11be and beyond, third-party STA can check the indicator and early terminate its RX processer. (save power)
  More than one bit can be applied to indicate different AMP PPDU if needed.
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
U-SIG1 | PHY version |  |  | Bandwidth |  |  | UL/DL | BSS color |  |  |  |  |  | TXOP |  |  |  |  |  |  | Disregard |  |  |  |  | Validate
U-SIG2 | PPDU Type |  | Validate | punctured channel info |  |  |  |  | Validate | UHR-SIG MCS |  | Number Of UHR-SIG Symbols |  |  |  |  | CRC |  |  |  | Tail |  |  |  |  | 

## Slide 5: Straw Poll #1
Do you agree to add the following text to the SFD:
  802.11 preamble field in an AMP DL PPDU includes L-STF, L-LTF, L-SIG, RL-SIG, and U-SIGs.

## Slide 6: Straw Poll #2
Do you agree to add the following text to the SFD:
  PHY version set to 0 and Validate bit(s) in U-SIG to indicate AMP PPDU(s).

## Slide 7: References
[1] 11-24/1530, Discussion of AMP-SIG Field, Bin Qian et al., Huawei.
[2] 11-24/0861, AMP DL PPDU consideration, You-Wei Chen et al., Mediatek.
[3] 11-24/1322, IEEE 802.11 TGbp Motion Dock