## Slide 1: Further Consideration for NPCA Operation
Date: 2025-03-05
Authors:

## Slide 2: Introduction
NPCA in TGbn SFD [1]
  [Motion #11]: TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
NPCA operation can increase the transmission opportunities when the primary channel is busy
  It can reduce the latency of data delivery, especially for the low latency(/urgent) traffic
It would be better for STA to have more NPCA chances especially when STA has low latency (higher priority) traffic
Current NPCA switching condition is based on the OBSS traffic but we can consider other conditions for more NPCA opportunities
AP and non-AP STA may have different views on channel idle/busy
  AP may not receive OBSS frame while the non-AP STA receives the OBSS frame vice versa.
  Unnecessary NPCA switching operation may happen

## Slide 3: NPCA operations
For enabling NPCA in TGbn D0.1
  NPCA AP can enable NPCA operation by setting NPCA Operation Information Present field to 1
  A non-AP NPCA STA may enable the NPCA mode only if it is associated with an NPCA AP. It is TBD how the non-AP STA enables NPCA mode.
Non-AP STA will transmit QoS null frame or Action frame to enable/disable the NPCA mode rather than (re) association frame
Legacy non-AP STA and non-NPCA non-AP STA may associate with NPCA AP
NPCA AP should not switch to NPCA primary channel if the NPCA AP can know no NPCA non-AP STA will be on NPCA primary channel
  if all NPCA non-AP STAs associated with the NPCA AP disabled the NPCA mode
  if there is no NPCA non-AP STA associated with the NPCA AP

## Slide 4: NPCA considering P2P transmission
P2P transmission in Intra-BSS looks very similar to OBSS transmission in terms of resource utilization
While P2P STA (STA3) communicates with the peer STA (STA4) on primary channel, the AP and non-AP STAs (STA1, 2) that detect the P2P transmission can not use the primary channel
We can consider Intra-BSS P2P transmission as a condition for NPCA operation

## Slide 5: NPCA considering P2P transmission
NPCA STA may switch to NPCA PCH when the NPCA STA detects Intra-BSS DL PPDU (e.g., DL/UL flag = DL)
  NPCA AP regards the Intra-BSS DL PPDU as P2P PPDU
  NPCA non-AP STA, for the Intra-BSS DL PPDU that is not addressed to the non-AP STA
They can perform NPCA operation during the duration indicated in the P2P PPDU
Non-AP STA can enable this mode when it has low latency(/urgent) traffic stream with AP
Non-AP STA may disable this operation if the STA wants to save more power

## Slide 6: NPCA considering P2P transmission
If the AP does not communicate with any non-AP STA during the Intra-BSS PPDU length, the AP returns to primary channel before the end of the PPDU

## Slide 7: NPCA considering P2P transmission
After switching to NPCA PCH, if the non-AP STA does not receive a frame from AP during the Intra-BSS PPDU length, the non-AP STA returns to primary channel before the end of the duration of the PPDU

## Slide 8: Conclusion
Currently, NPCA STA can switch to NPCA channel on the condition of OBSS traffic on primary channel
We proposed NPCA operation considering P2P transmission
  STA switches to NPCA channel when the STA detects Intra-BSS DL PPDU
  If the STA does not communicate with AP/non-AP STA during the PPDU length, the STA returns to primary channel before the end of the PPDU
This will increase TX opportunities by more NPCA usages and it will be very useful especially when non-AP STA has low latency traffic or urgent traffic
Non-AP STA can also decide to disable this mode if it wants to reduce power consumption

## Slide 9: References
[1] 24/0209r7, Specification Framework for TGbn
[2] 24/1762, PDT-MAC-NPCA

## Slide 10: Straw Poll 1
Do you agree the following text?
  An NPCA AP shall not switch to the NPCA primary channel for NPCA operation if all NPCA non-AP STAs associated with the NPCA AP disabled the NPCA mode.

## Slide 11: Straw Poll 2
Do you agree the following text?
  An NPCA AP shall not switch to the NPCA primary channel for NPCA operation if there is no NPCA non-AP STA associated with the NPCA AP.

## Slide 12: Straw Poll 3
Do you agree the following text?
  An NPCA STA may switch to NPCA primary channel when it receives an intra-BSS HE/EHT/UHR DL PPDU on primary channel
    Detailed conditions and procedures are TBD.

## Slide 13: Appendix
TGbn D0.1:
An NPCA AP shall not switch to the NPCA primary channel for NPCA operation if the value of its most recently transmitted NPCA Operation Information Present field is equal to 0