## Slide 1: Opportunistic Channel Access Mechanism for Buffer Reporting
Date: November 8, 2024
Authors:

## Slide 2: Introduction
UHR aims to provide more predictable delays and reduce tail latency
  One of the objectives of 802.11bn is: “Enabling at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation, with mobility between BSSs” [11-23/0480r3]
For aperiodic low-latency (LL) traffic, the AP must have up-to-date information regarding the current needs of STAs to effectively allocate communication resources
Buffer report requesting: the AP can actively request buffer report (e.g., BSR) from STAs
Buffer report collection can be employed during TXOPs
  e.g., When an AP plans to share its TXOP with non-AP STAs (e.g., TXS Mode 2)
  e.g., When an AP plans to share its TXOP with other APs

## Slide 3: An Example Method of LL Traffic Exchange during TXOPs
A sample application of buffer report requesting is during TXOPs
While a STA is in possession of a TXOP (the "TXOP holder"), other STAs cannot use the channel to exchange Low-Latency (LL) traffic
If the TXOP holder is the AP, it can use a portion of its acquired TXOP to poll non-AP STAs if they need to transmit UL LL traffic
If the TXOP holder is a non-AP STA, it may share a portion of its TXOP with AP to poll non-AP STAs if they need to transmit UL LL traffic
Sample methods have been proposed in [11-24/0390r0] [11-24/0870r0] [11-24/629r0] [11-23/1886r3] [11-24/0168r0] [11-23/1874r0]

## Slide 4: An Example Method of LL Traffic Exchange during TXOPs
Transmission Period refers to the intervals during which the AP communicates (e.g., send DL traffic) to one or more non-AP STAs
LL Traffic Exchange refers to a period during which the AP uses the TXOP to poll non-AP STAs to perform LL traffic exchange with them
The existing method to perform buffer report requesting is through polling
  The AP sends BSRP, and in response, the STAs respond with BSR frames [11-24/0168r0] [11-24/0390r0] [11-23/2076r0]
Transmission Period
TXOP Duration
LL Traffic Exchange
Transmission Period
AP communicates with STAX (UL/DL)
AP communicates with STAY (UL/DL)
AP polls other STAs and performs LL traffic exchange with them

## Slide 5: Problem Statement
Polling non-AP STAs (e.g., BSRP/BSR) can be used to determine if they carry LL traffic
Shortcoming: The duration of polling can be long, and its overhead depends on the number of STAs and available bandwidth [11-24/1870r0]
Since the number of STAs with LL traffic is usually lesser than the total number of STAs in the network (e.g., 20%), more efficient ways of sending buffer reports (BSRs) from the STAs are required
We propose an efficient method for requesting and collecting buffer reports from STAs
Transmission Period
TXOP Duration
LL Traffic Exchange
Transmission Period
Phase 1:
Determine the STAs with UL LL traffic
Phase 2:
UL/DL Traffic Exchange
During the LL Traffic Exchange period
Phase 1: The AP needs to determine which STAs need to perform UL LL transmission
Phase 2: UL, DL, or both types of communication are performed
Phase 1 must be as short as possible to maximize the efficiency of utilizing LL Traffic Exchange period

## Slide 6: Opportunistic Buffer Reporting by STAs
We propose a structure named Buffer Status Collection Period (BSCP)
This structure allows the AP to request and collect BSRs from STAs based on the priority of their traffic
Buffer Status Collection Period (BSCP) |  |  |  |  |  | 
Initial Actions (IA) (e.g., ICR/BSRP) | SIFS | Sub-window 1 (e.g., AC_VO) | PIFS | Sub-window 2 (e.g., AC_VI) | PIFS | Final Actions (FA) (e.g., TF)
Transmission Period
TXOP Duration
LL Traffic Exchange
Transmission Period
Phase 1:
Determine the STAs with UL LL traffic
Phase 2:
UL/DL Traffic Exchange
Resource Units
(RUs)
Time
e.g., 52-tone RU

## Slide 7
The Buffer Status Collection Period (BSCP) structure is composed of the following components
  One or more sub-windows, where each sub-window is associated with one or more traffic Access Categories (ACs)
  One or more RUs, where each RU may represent a number of tones
    Example: An RU may represent a 52-tone RU
  Inter-Frame Spacing (IFS) between sub-windows, to allow the AP to modify or terminate the BSCP
    e.g., when enough BSR frames are received, the AP may immediately send a TF to schedule UL
  An optional Initial Actions (IA) period at the beginning of the BSCP
    Allows the AP to send management or control frames to structure BSCP (signaling details TBD)
    e.g., the AP announces the structure of the BSCP, such as the number of RUs and number of timeslots
  An optional Final Actions (FA) period at the end of the BSCP
    e.g., the AP sends a TF to schedule UL traffic from STAs

## Slide 8
BSR transmissions are managed by the following rules
  Each STA carrying LL traffic can use only its associated sub-window to sends its BSR
  For example, if a STA has LL traffic belonging to AC_VO, it can only use the sub-window associated with this AC to send its BSR
  Each STA is allowed to select one of the RUs to sends its BSR
  Various methods can be used for performing STAs-to-RUs association
    e.g., A STA carrying LL traffic selects one of the available RUs randomly (similar to UORA)
    e.g., The AP sends a TF during the IA period to assign STAs to RUs based on their AID

## Slide 9
BSR
BSR
Transmission Period
STA 1 (TXOP Holder)
AP
STA 2 (with AC_AVO traffic)
BSR
STA 3 (with AC_AVO traffic)
STA 4 (with AC_VO traffic)
Buffer Status Collection Period (BSCP) |  |  |  |  |  |  |  | 
Initial Actions (IA) | SIFS | AC_AVO | PIFS | AC_VO | PIFS | AC_VI | PIFS | Final Actions (FA)
BSR (STA 2)
BSR (STA 3)
STA 5 (with AC_VO traffic)
STA 6 (with AC_VI traffic)
STA 7 (with AC_VI traffic)
BSR
BSR
BSR
BSR (STA 7)
BSR (STA 6)
BSR (STA 4)
BSR (STA 5)
LL Data
LL Data
LL Data
LL Data
LL Data
LL Data
Example:
The AP sends a TF during the IA period; this frame may announce the start of BSCP and its parameters
The AP sends a TF during the FA period to schedule UL transmissions from STAs
LL Traffic Exchange
TF
BSCP
TF

## Slide 10
BSR
BSR
Buffer Status Collection Period (BSCP) |  |  |  |  |  |  |  | 
Initial Actions (IA) | SIFS | ACMAX | SIFS | ACTXOP+1 | PIFS | ACTXOP | PIFS | Final Actions (FA)
Transmission Period
STA 1 (TXOP Holder)
AP
BSR (STA 2)
BSR (STA 3)
LL Data
LL Data
Example: After the first sub-window, the AP determines that enough BSR frames have been received, therefore, the AP terminates the BSCP and sends a TF to schedule UL traffic
TF
TF
LL Traffic Exchange
BSCP
Trigger Frame
(TF)
STA 2 (with AC_AVO traffic)
STA 3 (with AC_AVO traffic)
STA 4 (with AC_VO traffic)
STA 5 (with AC_VO traffic)
STA 6 (with AC_VI traffic)
STA 7 (with AC_VI traffic)

## Slide 11
Evaluation
Increasing the number of STAs from 20 to 100
10% of STAs need to send BSR
Percentage of STAs whose BSRs are received successfully versus the number of tones per RU and number of sub-windows (SWs)
BSCP duration versus the number of tones per RU and number of sub-windows (SW)

## Slide 12: Summary
Efficiently collecting buffer reports from STAs is essential to assess their needs for sending uplink low-latency (UL LL) traffic
Since the number of STAs with LL traffic is lower than the total STAs in the network, utilizing the polling method may introduce significant overhead
In this contribution, we propose a method to structure and improve the efficiency of buffer report transmissions from STAs:
  First, only STAs with specific LL traffic types are permitted to send their buffer reports
  Second, based on the priority of their buffered data, STAs are given varying time-domain priorities for sending their buffer reports
  Third, STAs randomly pick RUs and utilize OFDMA to increase the likelihood of successful transmission

## Slide 13: Straw Poll
Do you agree that 11bn should include methods based on opportunistic or random access to solicit buffer reports to determine which STAs need to send LL UL traffic?
YES/NO/ABSTAIN

## Slide 14
Appendix

## Slide 15
Sample BSCP structure
Buffer Status Collection Period (BSCP) |  |  |  |  |  | 
Initial Actions (IA) | SIFS | AC_VO | PIFS | AC_VI | PIFS | Final Actions (FA)
Time
Sub-window 1 for Voice AC
52-tone RU
20 MHz bandwidth is divided to four RUs, each including 52 tones
Sub-window 1 for Video AC

## Slide 16
Evaluation
Increasing the number of STAs from 20 to 100
10% of STAs need to send BSR
The following figure shows the percentage of STAs that whose BSRs are received successfully