## Slide 1: Opportunistic Channel Access Mechanism for Buffer Reporting
Date: November 8, 2024
Authors:

## Slide 2: Introduction
UHR aims to provide more predictable delays and reduce tail latency
  One of the objectives of 802.11bn is: “Enabling at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation, with mobility between BSSs” [11-23/0480r3]
One of the challenges of shortening communication latency is managing aperiodic low-latency (LL) traffic
Two main approaches
  Random access mechanisms, i.e., EDCA
  Trigger-Based (TB) communication
To use Trigger-Based (TB) UL transmission of aperiodic LL traffic, the AP must have up-to-date information regarding the current needs of STAs to effectively allocate communication resources
AP needs to perform buffer report collection (using BSRP and BSR)

## Slide 3: An Example Method of LL Traffic Exchange during TXOPs
When the AP acquires a TXOP, it can allocate a portion of it to poll non-AP STAs to determine if they need to transmit UL LL traffic
  Example 1: When the AP decides to trigger UL transmissions
  Example 2: When the AP decides to share its TXOP with non-AP STAs (e.g., TXS Mode 1 or 2)
  Example 3: When the AP decides to share its TXOP with other APs
Note: If the TXOP holder is a non-AP STA, it may allocate a portion of its TXOP to the AP, allowing the AP to poll other non-AP STAs and assess their need to transmit UL LL traffic
Sample methods have been proposed in [11-24/0390r0] [11-24/0870r0] [11-24/629r0] [11-23/1886r3] [11-24/0168r0] [11-23/1874r0]

## Slide 4: An Example Method of LL Traffic Exchange during TXOPs
LL Traffic Exchange refers to a period during which the AP uses the TXOP to poll and perform LL traffic exchange with other non-AP STAs
The existing method to perform buffer report collection is polling
  The AP sends BSRP, and in response, the STAs respond with BSR frames
  [11-24/0168r0] [11-24/0390r0] [11-23/2076r0]
Regular Transmission Period:
AP communicates with STAX
AP’s TXOP
LL Traffic Exchange
(UL)
Regular Transmission Period:
AP communicates with STAY
AP polls other STAs and performs LL traffic exchange with them

## Slide 5: Problem Statement
Polling non-AP STAs (e.g., BSRP/BSR) can be used to determine if they carry LL traffic
  Shortcoming: The duration of polling can be long, and its overhead depends on the number of STAs that are polled and available bandwidth [11-24/1870r0]
Since only a small fraction of STAs typically have LL traffic (e.g., around 20%), polling all or a large percentage of STAs is inefficient and incurs significant overhead
  More efficient ways of sending buffer reports (BSRs) from the STAs are required
We propose an efficient method for requesting and collecting buffer reports from STAs
Regular Transmission Period
AP’s TXOP
LL Traffic Exchange (UL)
Regular Transmission Period
Phase 1:
Determine the STAs with UL LL traffic
Phase 2:
UL Transmissions
During the LL Traffic Exchange period
Phase 1: The AP determines which STAs need to perform UL LL transmission
Phase 2: UL transmissions are scheduled (DL may be allowed too)
Phase 1 must be as short as possible to maximize the efficiency of utilizing LL Traffic Exchange period

## Slide 6: Opportunistic Buffer Reporting by STAs
We propose a structure named Buffer Status Collection Period (BSCP)
This structure allows the AP to request and collect BSRs from STAs based on the priority of their traffic
Buffer Status Collection Period (BSCP) |  |  |  |  |  | 
Initial Actions (IA) (e.g., ICR/BSRP) | SIFS | Sub-window 1 (e.g., LL AC_VO) | PIFS | Sub-window 2 (e.g., LL AC_VI) | PIFS | Final Actions (FA) (e.g., TF)
Regular Transmission Period
AP’s TXOP
LL Traffic Exchange (UL)
Regular Transmission Period
Phase 1:
Determine the STAs with UL LL traffic
Phase 2:
UL Transmissions
Resource Units
(RUs)
Time
e.g., 52-tone RU
Each ‘entry’ can be used to send a BSR frame

## Slide 7
The Buffer Status Collection Period (BSCP) structure is composed of the following components
  One or more sub-windows, where each sub-window is associated with one or more traffic Access Categories (ACs) (or deadline values, etc.)
  One or more RUs, where each RU may represent a number of tones
    Example: An RU may represent a 26-tone or 52-tone RU
  Inter-Frame Spacing (IFS) between sub-windows, to allow the AP to modify or terminate the BSCP
    e.g., when enough BSR frames are received, the AP may immediately send a TF to schedule UL
  An optional Initial Actions (IA) period at the beginning of the BSCP
    Allows the AP to send control frames to structure BSCP (e.g., BSRP)
    e.g., the AP announces the structure of the BSCP, such as the number of RUs and number of timeslots
  An optional Final Actions (FA) period at the end of the BSCP
    e.g., the AP sends a TF to schedule UL traffic from STAs

## Slide 8
BSR transmissions are managed by the following rules
  Each STA carrying LL traffic can use only its associated sub-window to sends its BSR
  e.g., If a STA has LL traffic belonging to AC_VO, it can only use the sub-window associated with this AC to send its BSR
  e.g., Only STAs whose packets’ deadline is less than 2 ms can report their BSR in the first sub-window
  Each STA is allowed to select one of the RUs to send its BSR
  Various methods can be used for STAs-to-RUs association
    e.g., A STA carrying LL traffic selects one of the available RUs randomly (similar to UORA)
    e.g., The AP sends a TF during the IA period to assign STAs to RUs based on their AID

## Slide 9
BSR
BSR
Transmission Period
AP
STAA
BSR
STAB
STAC
Buffer Status Collection Period (BSCP) |  |  |  |  |  |  |  | 
Initial Actions (IA) | SIFS | LL AC_VO (Deadline < 3 ms) | PIFS | LL AC_VO (Deadline < 7 ms) | PIFS | LL AC_VI | PIFS | Final Actions (FA)
BSR from STAA
BSR from STAB
STAD
STAE
STAF
BSR
BSR
BSR
BSR from STAF
BSR from STAE
BSR from STAC
BSR from STAD
LL Data
LL Data
LL Data
LL Data
LL Data
LL Data
Example:
The AP sends a TF during the IA period; this frame may announce the start of BSCP and its parameters
The AP sends a TF during the FA period to schedule UL transmissions from STAs
TF
TF
LL Traffic Exchange
BSCP

## Slide 10
BSR
BSR
Buffer Status Collection Period (BSCP) |  |  |  |  |  |  |  | 
Initial Actions (IA) | SIFS | LL AC_VO (Deadline < 3 ms) | SIFS | LL AC_VO (Deadline < 7 ms | PIFS | LL AC_VI | PIFS | Final Actions (FA)
Transmission Period
AP
BSR from STAA
BSR from STAB
LL Data
LL Data
Example: After the first sub-window, the AP determines that enough BSR frames have been received, therefore, the AP terminates the BSCP and sends a TF to schedule UL traffic
TF
TF
LL Traffic Exchange
BSCP
Trigger Frame
(TF)
STAA
STAB
STAC
STAD
STAE
STAF

## Slide 11
Evaluation
Increasing the number of STAs from 20 to 100
10% of STAs need to send BSR
Percentage of STAs whose BSRs are received successfully versus the number of tones per RU and number of sub-windows (SWs)
BSCP duration versus the number of tones per RU and number of sub-windows (SW)
Tones per RU
Note: A smaller RU size results in a higher number of RUs per sub-window, thereby lesser collisions

## Slide 12: Summary
Efficient buffer report collection from STAs is essential for accurately assessing their transmission needs and scheduling of UL aperiodic low-latency (UL LL) traffic
Since the number of STAs with LL traffic is smaller than the total number of STAs in the network, using the polling method may introduce significant overhead
In this contribution, we proposed a method to structure and improve the efficiency of buffer report collection from STAs:
  First, only STAs with specific LL traffic types are permitted to send their buffer reports
  Second, based on the priority of their buffered data, STAs are given varying time-domain priorities for sending their buffer reports
  Third, STAs randomly pick RUs and utilize OFDMA to report their BSRs

## Slide 13: Straw Poll
Do you agree that 802.11bn should include opportunistic (or random access) methods to solicit buffer reports and identify which STAs need to transmit aperiodic LL UL traffic?
YES/NO/ABSTAIN

## Slide 14
Appendix

## Slide 15
Sample BSCP structure
Buffer Status Collection Period (BSCP) |  |  |  |  |  | 
Initial Actions (IA) | SIFS | AC_VO | PIFS | AC_VI | PIFS | Final Actions (FA)
Time
Sub-window 1 for Voice AC
52-tone RU
20 MHz bandwidth is divided to four RUs, each including 52 tones
Sub-window 1 for Video AC

## Slide 16
Evaluation
Increasing the number of STAs from 20 to 100
10% of STAs need to send BSR
The following figure shows the percentage of STAs whose BSRs are received successfully