## Slide 1: Further Details on Improving Roaming between MLDs
Date: 2024-11-06
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Ido Ouzieli |  |  |  | 
Danny Alexander |  |  |  | 
Danny Ben-Ari |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
High level roaming procedure is agreed to achieve data continuity
  Exchange of request/response to initiate DS mapping change and context transfer from current AP MLD to target AP MLD
  A transient period to receive DL data from current AP MLD and allow DL/UL data exchange with target AP MLD
We provide further details for the following aspects in this presentation:
  Contexts related to BA agreement
  Context related to security
Current AP MLD
Target AP MLD
Non-AP MLD
State 4
Current AP MLD
Target AP MLD
Non-AP MLD
State 4
Current AP MLD
Target AP MLD
Non-AP MLD
Roam with DS mapping notification
End of roaming procedure

## Slide 3: DL Consideration
The key consideration is during the transient period, where we need the design to support data coming from both current AP MLD and target AP MLD, which can be done sequentially
The simplest approach to minimize implementation complexity on non-AP MLD is for non-AP MLD to keep using the existing receiving reordering buffer
  This aligns with existing BA setup because receive reordering buffer size depends only on the buffer size indication of non-AP MLD for DL agreement
Current AP MLD
Target AP MLD
Non-AP MLD
State 4
Current AP MLD
Target AP MLD
Non-AP MLD
State 4
Current AP MLD
Target AP MLD
Non-AP MLD
Roam with DS mapping notification
End of roaming procedure
Example for DL only:
Current AP MLD
Target AP MLD
Non-AP MLD
WinStartO
WinEndO
WinStartO
WinEndO
WinStartB
WinEndB

## Slide 4: DL Consideration
Relevant context from current AP MLD to target AP MLD to enable the operations
  Block Ack Parameters and Block Ack Timeout Value indicated by the non-AP MLD for existing DL BA agreement
  Next SN to be assigned for DL individually addressed data frame of each TID, which can have a large gap to make it semi-static
  WinStartO of an existing DL BA agreement so that the target AP MLD does not exceed reordering buffer window of the non-AP MLD
Current AP MLD
Target AP MLD
Non-AP MLD
WinStartO
WinEndO
WinStartO
WinEndO
WinStartB
WinEndB

## Slide 5: UL Consideration
The key consideration is for non-AP MLD to continue transmission of data in the queue
  SN/PN that has been assigned shall be allowed to be reused rather than reassignment, which complicates the transmission queue implementation
Relevant context from current AP MLD to target AP MLD to enable the operations
  Block Ack Parameters and Block Ack Timeout Value indicated by the non-AP MLD for existing UL BA agreement (Note that these are advisory information)
  latest SN that has been pass up to the next MAC process for TID with UL BA agreement, which can be used by target AP MLD to construct WinStartB
  Latest duplicate receiver cache for TID without BA agreement. This avoids cases when non-AP MLD retransmits data that has been passed up to target AP MLD, which happens when non-AP MLD misses the Acknowledgement
Current AP MLD
Target AP MLD
Non-AP MLD
State 4
Current AP MLD
Target AP MLD
Non-AP MLD
State 4
Current AP MLD
Target AP MLD
Non-AP MLD
Roam with DS mapping notification
End of roaming procedure
Example for UL only:
WinStartO
WinEndO
WinStartO
WinEndO
WinStartO
WinEndO

## Slide 6: Context related to security
The option to preserve one PN space during roaming is useful due to following consideration
  For DL, simplify replay check implementation on one received reordering buffer
  For UL, simplify existing transmission queues implementation without the need to reassign PN
  Potentially, no need to be burdened with additional key derivation during roaming
Note that this requirement is natural with one PTK, but can also be done with different PTK, which is currently under discussion
Relevant context from current AP MLD to target AP MLD to enable the operations
  Starting PN to be assigned for DL individually addressed frame by the target AP MLD, which can have a large gap to make it semi-static

## Slide 7: Conclusion
We discuss the essential contexts that needs to be transferred from current AP MLD to target AP MLD during roaming to enable data continuity
  Block Ack Parameters and Block Ack Timeout Value indicated by the non-AP MLD for existing BA agreement of a TID
  Starting SN to be assigned for DL individually addressed data frame of each TID by the target AP MLD
  Starting PN to be assigned for DL individually addressed frame by the target AP MLD
  WinStartO of an existing DL BA agreement so that the target AP MLD does not exceed reordering buffer window of the non-AP MLD
  latest SN that has been pass up for TID to the next MAC process with UL BA agreement
  Latest duplicate receiver cache for TID without BA agreement

## Slide 8: Straw Poll
Do you support to enable the following contexts to be transferred to target AP MLD to preserve the data exchange context for the non-AP MLD?
  Block Ack Parameters and Block Ack Timeout Value indicated by the non-AP MLD for existing BA agreement of a TID
  Starting SN to be assigned for DL individually addressed data frame of each TID by the target AP MLD
  Starting PN to be assigned for DL individually addressed frame by the target AP MLD
  WinStartO of an existing DL BA agreement so that the target AP MLD does not exceed reordering buffer window of the non-AP MLD
  Latest duplicate receiver cache for TID without BA agreement
  latest SN that has been pass up for TID to the next MAC process with UL BA agreement
  TBD for other contexts
Note – TBD on the agreed buffer size with the target AP MLD