## Slide 1: Further details on improving roaming between MLDs
Date: 2025-02-17
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Ido Ouzieli |  |  |  | 
Danny Alexander |  |  |  | 
Danny Ben-Ari |  |  |  | 
Das Dibakar |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
There have been many options that are proposed to UHR roaming
In this presentation, we focus on a specific scenario based on SMD with DS mapping change
  A common use case for general implementation
  Can be justified to have improvements compared with existing roaming scheme
  Flow already agreed in SFD

## Slide 3: Illustration of the common use case
With preparation, the best strategy is to finish all the contexts transfer during preparation to minimize exchange time of roaming execution
Not listing data forwarding due to unpredictable support/backhaul on AP MLD
During transient period non-AP MLD can switch to target AP MLD for data exchange, but due to single radio constraints, the best strategy is to finish DL data with current AP MLD ASAP without switching back and forth

## Slide 4: Gains compared with existing Roaming
Enable data exchange after roaming without additional frame exchange due to context transfer
Minimize pause time of roaming execution exchange due to preparation finishing all context transfer
Transient period to finish remaining DL data of current AP MLD if desired without loss
Continue UL data without loss and avoid UL data duplicate

## Slide 5: Simplify the preparation operation
Roaming preparation request only focus on one target AP MLD
A SMD unified timeout indicated in initial connection
  Already the case for FT reassociation deadline
  Non-AP MLD knows the time beforehand to send roaming execution request
  Target AP MLD deletes preparation information if no follow up after timeout
No Target AP MLD setup link change until roaming execution exchange is finished
Roaming execution request is not rejected if preparation beforehand

## Slide 6: Simplify the transient period operation
All the information in reassociation request frame needs to be in roaming preparation request or roaming execution request
  Including listen interval for beacon wakeup
However, requirement to listen Beacon of target AP MLD needs to be suspended during transient period to avoid switching back and forth for single radio non-AP MLD
Setup links with target AP MLD also needs to be in power save mode by default

## Slide 7: When the transient period ends?
A timeout indicated in roaming execution response
Indication through More Data bit to know if there are existing data even in Active mode
Early termination frame from non-AP MLD when DL data is finished early or needs to go to target AP MLD

## Slide 8: Minimal Context Transfer for Data Operations
UL/DL BA parameters
  Avoid ADDBA exchange
Next PN for DL
  Security requirement and can be done with big gap
Latest UL forward up SN
  Avoid duplicate and can be sent to non-AP MLD during roaming execution
All relevant UL replay counters
  Avoid replay
  Client can indicate next UL PN to target AP MLD to help
How about DL SN?
  DL SN is required if having DL data from target AP MLD during transient period
  If can not reliability support due to dynamic nature, then capability indication from AP MLD

## Slide 9: Conclusion
We discuss the important proposals for the following common scenario

## Slide 10: Straw Poll
Do you support the following for roaming preparation request/response exchange?
After the roaming preparation request/response exchange, there is an indicated timeout
  If there is no successful transmission of the roaming execution request frame from the non-AP MLD within the indicated timeout, then the target AP MLD may delete all preparation information related to the non-AP MLD
    NOTE - This includes security context, i.e., new derived TK if new TK is derived
  if the roaming preparation request for a target AP MLD is accepted in the roaming preparation response, and the non-AP MLD sends a following roaming execution request for the target AP MLD received within the indicated timeout, then the roaming execution request shall be accepted in the roaming execution response
  TBD on indication of the timeout
After the latest roaming preparation request/response exchange, the setup links with the target AP MLD is not modified until after the roaming execution request/response exchange is finished.

## Slide 11: Straw Poll
Do you support the following for roaming preparation request/response exchange?
  There is only one target AP MLD indicated in the roaming preparation request frame from a non-AP MLD

## Slide 12: Straw Poll
Do you support the following?
  The roaming preparation request frame includes Listen Interval field of the non-AP MLD for the target AP MLD
  The roaming execution request frame includes Listen Interval field of the non-AP MLD for the target AP MLD if there is no roaming preparation request/response exchange beforehand
  After the roaming execution request/response exchange with the current AP MLD, the non-AP MLD is by default in power save mode for all the setup links with the target AP MLD
  After the roaming execution request/response exchange with the current AP MLD, during the TBD period to receive DL data from the current AP MLD, the non-AP MLD is not required to listen to any Beacon frames of the APs affiliated with the target AP MLD

## Slide 13: Straw Poll
Do you support that after the roaming execution request/response exchange with the current AP MLD, the TBD period to receive DL data from the current AP MLD ends after the indicated timeout in the roaming execution response?

## Slide 14: Straw Poll
Do you support to enable the following contexts to be transferred to target AP MLD to preserve the data exchange context for the non-AP MLD?
  Block Ack Parameters and Block Ack Timeout Value indicated by the non-AP MLD for existing BA agreement of a TID
  Next SN to be assigned for DL individually addressed data frame of each TID
  Latest duplicate receiver cache for TID without BA agreement
  latest SN that has been pass up for TID with UL BA agreement
  Starting PN to be assigned for DL individually addressed frame by the target AP MLD
  Initial value to be used by each replay counter of the target AP MLD for UL individually addressed frame
  WinStartO of an existing DL BA agreement so that the target AP MLD does not exceed reordering buffer window of the non-AP MLD
  TBD for other contexts