## Slide 1: 11bn Link Addition Procedure for Seamless Roaming
Chittabrata Ghosh, Apple
Date: 2024-11-11
November 2024
Authors:

## Slide 2: Background and Problem Statement
Chittabrata Ghosh, Apple
Background:
  802.11bn should provide “make-before-break” connection with Roaming target AP MLD
    Minimize duration when roaming non-AP MLD experiences low RSSI with Serving AP MLD and is also unable to do frame exchange with Roaming target AP MLD
  Initiation of roaming through Serving AP MLD is a new operation proposed in 802.11bn
Problem Statement:
  Roaming through Serving AP MLD may result in roaming failure
  Roaming failure may cause interruption in data exchange during roaming, especially if selected Roaming target AP MLD has limited resources (e.g., number of links, supported BW, etc.) available
Goals for seamless roaming:
  Allow a STA to discover Roaming target AP MLD prior to roaming to this AP MLD
  Allow a non-AP MLD to initiate roaming while data exchange is in progress in same link
  Minimize number of management frame exchanges for roaming by using mobility domain framework
November 2024

## Slide 3
AP 12
AP 22
AP MLMD
AP MLD 1
AP MLD 2
STA 1
Non-AP MLD 1
Link ID:1
Serving AP MLD
Roaming target AP MLD
Seamless Roaming Entity Definitions
Chittabrata Ghosh, Apple
AP Multi-link Multi-device (MLMD) (e.g., per-floor network): Non-collocated APs affiliated to unique AP MLDs share a common management entity for roaming, termed as AP MLMD
        In other words, an AP is affiliated to an AP MLD, which is a member of an AP MLMD
        Mobility domain (MD) (e.g., building network): It constitutes one or multiple AP MLMDs
        Serving AP MLD: An AP MLD is a member of AP MLMD to which a non-AP MLD sends initial Association Request frame to set up at least one link
        Roaming target AP MLD: An AP MLD is a member of AP MLMD with which a non-AP MLD decides to roam to from the Serving AP MLD
Static context
Static context
November 2024

## Slide 4: Proposal: General Flow for Seamless Roaming
Non-AP MLD 1
Data exchange
AP MLD 1
AP MLD 2
Serving AP MLD
Roaming target AP MLD
Query / Scan Phase
Data exchange
Data exchange
Query req
Query resp
Link Add Req
Link Add Res
Data exchange
Route switch
Roaming Phase
OTA
Over-the-DS
Chittabrata Ghosh, Apple
Seamless roaming may precede a query/scan phase
Query / Scan phase:
  Query phase used to request for available resources
    Customized for non-AP MLD requirements
  Provide a level of assurance (e.g., requested links will be accepted) – details TBD
  Query phase allows to discover a single Roaming target AP MLD and list of AP MLDs that are potential candidates for roaming
Roaming Phase:
  Roaming is initiated by non-AP MLD with explicit link addition request sent to Serving AP MLD
    STA requirements (static context) shared with Roaming target AP MLD
    Roaming target AP MLD identifier (discovered in query phase) shared with Serving AP MLD
    Data exchange continues with Serving AP MLD
      If link addition request is rejected, initiate roaming with an AP MLD from the list created during query phase (no disruption to data exchange)
  Route switch is then initiated for DS mapping switch
Static context
November 2024

## Slide 5: Proposal: Link Addition Procedure before Route Switch
Non-AP MLD 1
Link Setup Response
Data exchange
AP MLD 1
AP MLD 2
Link addition request
Link addition response
Serving AP MLD
Roaming target AP MLD
Link setup complete
Data exchange
Link Setup Request
(STA cap/req.)
Data exchange
Route switch initiation
Query/Scan to discover Target AP MLD
OTA
Over-the-DS
Logical
Chittabrata Ghosh, Apple
Non-AP MLD has discovered the Roaming target AP MLD
Non-AP MLD initiates roaming through Serving AP MLD
  It sends link addition request to Serving AP MLD with Roaming target AP MLD identifier
Upon receipt of the request, Serving AP MLD sends a link setup request frame to indicated Roaming target AP MLD
  Non-AP MLD requirements and capabilities are included in this frame
Link setup response from Roaming target AP MLD contains decision about link addition request from the non-AP MLD
Link setup is complete with Roaming target AP MLD after reception of link addition response frame from Serving AP MLD
  Non-AP MLD and Roaming target AP MLD are in State 4
Specific frames and frame format for link addition procedure are TBD
November 2024

## Slide 6: Conclusion
Chittabrata Ghosh, Apple
    We proposed that roaming is initiated with link addition procedure
  Prior to initiating link addition procedure, non-AP MLD has knowledge of the Roaming target AP MLD that it intends to roam to
We proposed details of the link addition procedure
We have also proposed content of the static context shared during link addition procedure
November 2024

## Slide 7: SP
Do you agree to define a seamless mobility domain (SMD), characterized by an identifier, encompassing multiple AP MLDs, where a non-AP MLD can use the seamless roaming procedure to roam between such AP MLDs?
Chittabrata Ghosh, Apple
November 2024