## Slide 1: Seamless Roaming
Date: 2025-01-15
Authors:

## Slide 2: Introduction
TGbn has agreed to specify a new mechanism [Jan 2024] for seamless roaming of a non-AP MLD from a current AP MLD to a target AP MLD with the following characteristics:
  [Jul 2024] Context related to the non-AP MLD can be (at least partially) transferred from the current to the target AP MLD
  [Jul 2024] After a request/response exchange initiating the DS mapping change, buffered DL data can be:
    Delivered by the current AP MLD – retrieved by the non-AP MLD on the old link
    Forwarded from the current AP MLD to the target AP MLD so that the non-AP MLD may retrieve it on the new link
  [Sept 2024] A request/response exchange is defined from a non-AP MLD in state 4 to
    Transfer the context
    Perform necessary DS mapping change
  [Nov 2024] A preparation phase is defined from a non-AP MLD in state 4 to
    Transfer the context
    Setup the links with the target AP MLD

## Slide 3: Seamless Roaming requirements
Should be seamless
  No disruption to on-going QoS flows
  Avoid unnecessary overhead (reduce frame exchange/processing)
  Reliable roaming (can be prepared in advance and correct expectations are set for clients)
Should be scalable
  To support mobility within a network consisting of large number of APs
Should be simple
  E.g., Rely on existing frameworks as much as possible
Should be flexible
  To cover different use cases such as home, enterprise, warehouse, etc.

## Slide 4: Seamless Mobility Domain (SMD)
To fulfill the requirements of Seamless Roaming (SR), one of the key aspects is to identify the group of AP MLDs over which the SR protocol can be used.
A Seamless Mobility Domain (SMD) shall be defined and identified with a unique identifier (SMD ID) to facilitate the operations involved in the transition between a current AP MLD and a target AP MLD belonging to the same SMD can be carried while referring to such an SMD ID, for example:
  Discovery of the AP MLDs within the SMD across which the non-AP MLD can use SR
  Security (single PMKSA/PTKSA)
  Consistency of BA operation
  Set up links
While SR can provide the most seamless experience within the SMD, it is expected mobility in larger ecosystems (e.g., between SMDs) can be aided by fast BSS transition (FT).
FT MD
SMD 1
SMD 2
SR
SMD 3
FT
AP MLD 1
AP MLD 2
AP MLD 4
AP MLD 3

## Slide 5: Seamless Roaming In Steps
Recommendations
To deliver a smooth experience, Seamless Roaming extends over different steps:
  Discovery: the client discovers the neighboring AP MLDs in the SMD
  Recommendations: the client can receive recommendations on suitable candidate AP MLDs in the SMD that can meet the client’s requirements
    E.g., considering client’s context, loading conditions, check on the backhaul, etc.
    BTM signaling can be considered, e.g.:
      BTM query/request  solicited
      BTM request  unsolicited
  Preparation: the client requests the current AP MLD to set up a target AP MLD in the SMD over the backhaul
    Set up of the links
    First instance of context transfer
    Signaling for the client/current AP MLD request/response exchange is TBD (e.g., ML reconfiguration)
  Execution: the client request to roam to the target AP MLD in the SMD
    Second instance of context transfer and optionally link reconfiguration
    If necessary, DS mapping switch
    Both exchange client-current and client-target AP MLD can be considered (current in the figure)
    Shall be accepted if request is received within a timeout after Setup completion
    ML reconfiguration can be considered for signaling (e.g., to cover the case where Preparation is not performed.)
AP MLD0
AP MLD1
AP MLD2
Client
Discovery/Scanning
Set up links
context transfer (1)
Prep. Request
AP MLD 1
Prep. Response
context transfer (2)
Optional: set up links
Necessary DS map switch
Execution request
AP MLD 1
Execution Response
Prep. timeout
(Execution request is accepted if performed within timeout after Prep. completion)

## Slide 6: Discussion on the Roaming Setup
Some of the key operations for SR that are expected are
  Context transfer
  Link set up
Such operations are expected to require some latency (e.g., some tens of ms), therefore it is preferable to avoid service disruption (e.g., interruption of DL/UL communications) while such operations are carried out.
Propose to decouple the request/response exchange for the roaming execution (which can involve DS mapping switch and therefore service interruption) by introducing a Preparation step before Execution (4 messages). The context transfer can initiate at this time.
  It can be further considered that after the Setup is performed, the current AP MLD shall accept the Transition request at least if received within a timeout after Setup completion, in this way the expectation is set for successful roaming execution.
In some other cases a single request/response exchange should take care of the various operations (2 messages)
The signaling should be consistent between Preparation and Execution (i.e., provision for link addition) to cover the cases of 4 messages and 2 messages sequence

## Slide 7: Security
Single PMKSA/PTKSA in roaming has been discussed as a key feature to obtain a seamless experience and should be supported for a client that roams when remaining in state 4 in the SMD.
  To maintain state 4 in roaming at least some components of the authenticator shall be associated with the SMD
  An SMD management entity (SMD ME) with functions of authenticator should be defined
Since some members expressed security concerns with the PTK sharing in some deployments, extensions of the PTKSA can be considered to provision for different (per AP MLD) PTKs

## Slide 8: FT updates
An FT MD can include one or more SMDs.
When initial secure association is established within an SMD within an FT MD, the secure association is performed such that
  Seamless roaming can be used within the SMD
  FT can be used between SMDs
The updates of FT consist of the following:
  The R0KH derives PMK R0 and PMK R1 according to the SMD identity (the single PMKSA to be used in the SMD is PMK R1 SA)
  The R1KH derives PTK R1 according to PMK R1 and the SMD identity (the single PTKSA to be used in the SMD is PTK R1 SA)

## Slide 9: Conclusion
A Seamless Roaming Mobility Domain (SMD) is introduced and identified by a unique identifier
  A client can use the SR protocol between the AP MLDs within the SMD
The SR protocol develops in steps including:
  Discovery: AP MLDs within the SMD
  Recommendation: network recommendation for candidate AP MLDs
  Preparation: set up the links and transfer the context to the target AP MLD
  Transition: context transfer and necessary DS mapping switch (optional link addition to provision for absence of Preparation).
PMKSA and PTKSA are established with the SMD for seamless experience
Minimal FT updates can be introduced so that FT can be used between SMDs (and seamless roaming can be used within such SMDs)

## Slide 10: SP1
Do you agree to define a seamless mobility domain (SMD), characterized by an identifier, encompassing multiple AP MLDs, where a non-AP MLD can use the seamless roaming procedure to roam between such AP MLDs.

## Slide 11: SP2
Do you support the following for security in seamless roaming?
  when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD within the SMD, the same PMKSA, established with the SMD-ME, shall be used to protect communications with the current AP MLD and the target AP MLD

## Slide 12: SP3
Do you support the following for security in seamless roaming?
  when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD within the SMD, the same PTKSA, established with the SMD-ME, shall be used to protect communications with the current AP MLD and the target AP MLD

## Slide 13: Thank You