## Slide 1: Seamless Roaming
Date: 2025-01-15
Authors:

## Slide 2: Introduction
TGbn has agreed to specify a new mechanism [Jan 2024] for seamless roaming of a non-AP MLD from a current AP MLD to a target AP MLD with the following characteristics:
  [Jul 2024] Context related to the non-AP MLD can be (at least partially) transferred from the current to the target AP MLD
  [Jul 2024] After a request/response exchange initiating the DS mapping change, buffered DL data can be:
    Delivered by the current AP MLD – retrieved by the non-AP MLD on the old link
    Forwarded from the current AP MLD to the target AP MLD so that the non-AP MLD may retrieve it on the new link
  [Sept 2024] A request/response exchange is defined from a non-AP MLD in state 4 to
    Transfer the context
    Perform necessary DS mapping change
  [Nov 2024] A preparation phase is defined from a non-AP MLD in state 4 to
    Transfer the context
    Setup the links with the target AP MLD

## Slide 3: Seamless Roaming requirements
Should be seamless
  No disruption to on-going QoS flows
  Avoid unnecessary overhead (reduce frame exchange/processing)
  Reliable roaming (can be prepared in advance and correct expectations are set for clients)
Should be scalable
  To support mobility within a network consisting of large number of APs
Should be simple
  E.g., Rely on existing frameworks as much as possible
Should be flexible
  To cover different use cases such as home, enterprise, warehouse, etc.

## Slide 4: Seamless Mobility Domain (SMD)
To fulfill the requirements of Seamless Roaming (SR), one of the key aspects is to identify the group of AP MLDs over which the SR protocol can be used.
A Seamless Mobility Domain (SMD) shall be defined and identified with a unique identifier to facilitate the operations involved in the transition between a current AP MLD and a target AP MLD belonging to the same SMD can be carried while referring to such an SMD ID, for example:
  Discovery of the AP MLDs within the SMD across which the non-AP MLD can use SR
  Security (single PMKSA/PTKSA)
  Consistency of BA operation
  Set up links
While SR can provide the most seamless experience within the SMD, it is expected mobility in larger ecosystems (e.g., between SMDs) can be aided by fast BSS transition (FT).
FT MD
SMD 1
SMD 2
SR
SMD 3
FT
AP MLD 1
AP MLD 2
AP MLD 4
AP MLD 3

## Slide 5: Seamless Roaming In Steps
Recommendations
To deliver a smooth experience, Seamless Roaming extends over different steps:
  Discovery: the client discovers the neighboring AP MLDs in the SMD
  Recommendations: the client can receive recommendations on suitable candidate AP MLDs in the SMD that can meet the client’s requirements
    E.g., considering client’s context, loading conditions, check on the backhaul, etc.
    BTM signaling can be considered, e.g.:
      BTM query/request  solicited
      BTM request  unsolicited
  Preparation: the client requests the current AP MLD to set up a target AP MLD in the SMD over the backhaul
    Set up of the links
    First instance of context transfer
    Signaling for the client/current AP MLD request/response exchange is TBD (e.g., ML reconfiguration)
  Execution: the client request to roam to the target AP MLD in the SMD
    Second instance of context transfer and optionally link reconfiguration
    If necessary, DS mapping switch
    Both exchange client-current and client-target AP MLD can be considered (current in the figure)
    Shall be accepted if request is received within a timeout after Setup completion
    ML reconfiguration can be considered for signaling (e.g., to cover the case where Preparation is not performed.)
AP MLD0
AP MLD1
AP MLD2
Client
Discovery/Scanning
Set up links
context transfer (1)
Prep. Request
AP MLD 1
Prep. Response
context transfer (2)
Optional: set up links
DS map switch (if necessary)
Execution request
AP MLD 1
Execution Response
Prep. timeout
(Execution request is accepted if performed within timeout after Prep. completion)

## Slide 6: Discussion on the Roaming Setup
Some of the key operations for SR that are expected are
  Context transfer
  Link set up
Such operations are expected to require some latency (e.g., some tens of ms), therefore it is preferable to avoid service disruption (e.g., interruption of DL/UL communications) while such operations are carried out.
TGbn agreed to decouple the request/response exchange for the roaming execution (which can involve DS mapping switch and therefore service interruption) by introducing a Preparation step before Execution (4 messages). The context transfer can initiate at this time.
  After a successful Preparation, the current AP MLD shall accept the Execution request at least if received within a timeout after Setup completion, in this way the expectation is set for successful roaming execution.
The signaling should be consistent between Preparation and Execution (i.e., provision for link addition)

## Slide 7: Security (two security modes)
TGbn agreed on single PMKSA/PTKSA as a key feature to obtain a seamless experience for a client that roams when remaining in state 4 with the SMD-ME.
  First mode: single encryption key (in the single PTKSA) for all AP MLDs within the SMD
Since some members expressed security concerns with the PTK sharing in some deployments, extensions of the PTKSA can be considered to provision for a second mode using different (per-AP MLD) TKs for encryption.
  It is expected that Preparation Req/Resp (via the Current PA MLD) can be used to convey the necessary support for establishing the new TK (e.g., Public Ephemeral Keys and/or Nonces), and after that the new TK can be used to protect the Execution Request/Response (if sent directly to the Target AP MLD)

## Slide 8: PN Continuation (current assumption)
To facilitate reordering packets that may come from different AP MLDs during seamless roaming, the PN space can continue (i.e.., monotonically increasing) between the serving AP MLD and the target AP MLD regardless of which TK is used
PN is maintained per PTKSA (which is at the SMD level)
Since we allow TWO TKs during the SR transitional period, the PN continues (thanks to context transfer) and increases monotonically from the serving AP MLD to the AP MLDs regardless of which TK value is used to encrypt the frame.

## Slide 9: FT updates
An FT MD can include one or more SMDs.
When initial secure association is established within an SMD-ME within an FT MD, the secure association is performed such that
  Seamless roaming can be used within the SMD
  FT can be used between SMDs
The updates of FT consist of the following:
  PMK R1 is bound to the SMD-ME identity (the single PMKSA to be used in the SMD is PMK R1 SA)
  PTK is derived according to PMK R1 and is bound to the SMD identity (the single PTKSA to be used in the SMD is based on PMK R1 SA)

## Slide 10: Discussion: Execution Request via Current or via Target AP MLD
Case 1: When the non-AP MLD wished to roam as fast as possible, and/or, lost the signal from the Current AP MLD, it is more appropriate to send a Execution Request to the Target AP MLD. In this case draining of DL data is not performed (e.g., would require switch back on other links, etc.)
Case 2: When the non-AP MLD wishes to retrieve DL data from the Current AP MLD, it is more appropriate to Send a Execution Request to the Current AP MLD, so that the non-AP MLD can stay on the same link(s) to retrieve the data
  In this case early termination of the transitory is desirable (e.g., no more DL data, signal lost, etc.)

## Slide 11: Case 1 – Execution via Target AP MLD
When the Execution Request is transmitted to the Target AP MLD2, the operation is simple since the focus is on moving to AP2 as quickly as possible
  PM=0 indication is provided and DL from AP2 can flow as soon as Execution Response is received and DS mapping is changed
The transitory duration is 0 (no DL draining with AP1), and AP2 indicates to AP1 (over the backhaul) that it shall interrupt all operations with STA.
AP2 shall confirm over the backhaul
AP MLD1
(Current)
AP MLD2
(Target)
Non-AP
MLD
Execution Response
Preparation omitted in this figure
DL AP MLD1
DL AP MLD2
DL can start (all TIDs mapped to the awakened link(s))
Execution Request
Carries PM=0 indication
No more DL
AP MLD2 is indicated to interrupt all the operations with STA, and confirms

## Slide 12: Case 2 – Execution via Current AP MLD
STA transmit Execution Request to AP1
AP1 tunes up a cutoff time for the DL draining (all TIDs), transfers it to AP2, and provides it to STA
  Cutoff time may depend on multiple aspects as:
    Desired experience of STA (e.g., indication in Execution Request)
    Capability of the network of data forwarding
    Congestion over backhaul
AP1 may transmit DL data until cutoff time
AP2 may transmit DL starting from reception of an UL frame with PM=0 indication
AP2 assumes that all the operations STA-AP1 are concluded after the cutoff time
AP MLD1
(Current)
AP MLD2
(Target)
Non-AP
MLD
Preparation omitted in this figure
AP MLD2 is provided with
Cutoff time (all TIDs)
DL AP MLD1
Cutoff time
DL AP MLD2
PM=0 indication of link(s) awake
DL can start (all TIDs mapped to the awakened link(s))
Operations STA-AP1 are concluded
Execution Request
No more DL
Execution Response
Cutoff time (all TIDs)

## Slide 13: Case 2 – Execution via Current AP MLD (+ early termination of transitory)
An indication of ‘No more DL’ can be provided by AP1 to STA
STA can provide ‘early transitory termination’ to AP2
  The indication can use ‘No more DL’ as supporting information, or can come out of an autonomous decision of STA (e.g., signal fading, too long transitory, LL traffic coming up, etc.)
  If provided, AP2 assumes termination of STA-AP1 operations ahead of cutoff time (e.g., can move BA window forward for any TID freely)
AP MLD1
(Current)
AP MLD2
(Target)
Non-AP
MLD
Execution Response
Cutoff time (all TIDs)
Preparation omitted in this figure
AP MLD2 is provided with
Cutoff time (all TIDs)
DL AP MLD1
DL AP MLD2
PM=0 indication of link(s) awake
DL can start (all TIDs mapped to the awakened link(s))
Execution Request
No more DL
No more DL
Early Transitory Termination
Cutoff time
Operations STA-AP1 are concluded ahead of cutoff time

## Slide 14: Management frame handling (in transitory)
There should be a separation of the time window during which STA exchanges Management frames with AP1, and the time window for AP2
  Otherwise there could be some confusion of the SN used for such management frames
TGbn should discuss solutions for this problem for Case 2 (Execution via Current AP MLD)

## Slide 15: Conclusion
A Seamless Roaming Mobility Domain (SMD) is introduced and identified by a unique identifier
  A client can use the SR protocol between the AP MLDs within the SMD
Seamless Roaming phases are showcased
A second security mode with per-AP MLD encryption key can be specified, and used as alternative to the first mode with per-SMD encryption key
Minimal FT updates can be introduced so that FT can be used between SMDs (and seamless roaming can be used within such SMDs)
An analysis of transitory in two cases (Execution via Target vs. via Current AP MLD) is given, and ‘early termination’ signaling is proposed for the latter.

## Slide 16: SP1 (per-AP MLD encryption key mode within single PTKSA)
Do you support allowing a second mode for security in roaming (in addition to the first mode with single TK used across all AP MLDs of the SMD) where a non-AP MLD can derive a new TK under the same PTKSA with the target AP MLD?
The new TK is derived as part of the single PTKSA
The PN is maintained per PTKSA: The new TK negotiated with the target AP MLD shares the same PN space with the TK of the current AP MLD (PN is monotonically increasing)”

## Slide 17: SP2 (STA->AP2 indication of ‘early termination of transitory’)
Do you agree that, during the TBD time for retrieving DL from the Current AP MLD, the non-AP MLD may provide an indication to the Target AP MLD that the TBD time for DL retrieval is early-terminated before the TBD time?
TBD signaling of the indication

## Slide 18: Thank You