## Slide 1: BSRP TF response rules changes for M-BA
Date: 2024-11-09
Authors:

## Slide 2: ICF-ICR for dynamic unavailability operation (DUO)
We have agreed to have a mode where a non-AP STA can include its unavailability information (start time and duration) in an initial control frame sent in response to an initial control frame sent by the AP
Taking into account all the constraints, it seems that the group is converging toward using BSRP as the initial control frame and to have Multi-STA BA frame being sent in response (as initial control response) and be the container for the unavailability information (See contributions 24/1226r0, 24/1562r0)
  There were no existing ICF-ICR exchanges that were well fitted for this and we therefore have suggested to define such new exchange

## Slide 3: BSRP TF rules
The current rules for the response to a BSRP trigger frames are defined in subclause 26.5.5 (Buffer status report operation) and currently mandate to include in the response
The non-AP STA shall include in the HE TB PPDU (in response to a BSRP Trigger frame) one or more QoS Null frames containing one or more of the following:
  The QoS Control field(s) with Queue Size subfields for each of the TIDs for which the nonAP STA has queue size to report to the AP.
  The BSR Control subfield with the Queue Size All subfield indicating the queue size for the ACs, indicated by the ACI Bitmap subfield, for which the non-AP STA has queue size to report to the AP if the AP has indicated its support in the BSR Support subfield of its HE Capabilities element. The non-AP STA shall set Delta TID, Scaling Factor, ACI High, and Queue Size High subfields of the BSR Control subfield as defined in 9.2.4.7.4 (BSR Control).
In order to enable the new ICF-ICR sequence, we need so slightly change these rules

## Slide 4: BSRP TF response rules changes for M-BA
Proposal is simple:
  allow the scheduled STA to include M-BA frame in the PPDU sent in response.
If the BSRP TF solicits a response in TB PPDU format, then aggregation is possible
  We need to allow that the scheduled STA can aggregate QoS Null frames (for BSR) with M-BA frame (to include unavailability info)
If the BSRP TF solicits a response in Non-HT (Dup) PPDU format, then aggregation is not possible
  We need to allow that the scheduled STA to include in the PPDU in response only the M-BA frame
  Under this mode, the BSR is not included

## Slide 5: Straw poll #1
Do you support to include the following in the 11bn SFD:
modify the rules for responding to a BSRP TF so that the scheduled non-AP STA that is in Dynamic Unavailability Operation (DUO) mode, in addition to baseline rules:
  Is allowed to aggregate QoS Null frame(s) with M-STA BA if the response is TB PPDU
  Is allowed to include only M-STA BA if the response is in non-HT (Dup) mode
    And therefore not include BSR in the response