## Slide 1: Seamless Roaming Follow Up
Date: 2024-11-09
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Seamless Roaming
Seamless roaming procedure:
  (optional) step1: Candidate target serving AP MLD acquiring
    A non-AP MLD acquires the candidate target serving AP MLDs through its current serving AP MLD.
  Step 2: establishing the links with the target serving AP MLD.
  Step 3: roaming from the current serving AP MLD to the target AP MLD
    DS mapping update with access server, router, or ethernet switch.
    Frame exchange context transfer to the target AP MLD
    The UL frame changes for UL Data frames are suspended during step 3.
  Step 4: stopping the frame exchanges of Data frames with the current serving AP MLD, and executing the frame exchanges of Data frames with the target serving AP MLD.
    It is possible that both AP MLDs transmit the DL Data frames for some times after step 4.
    The UL Data frames can only be transmitted to the target AP MLD.
Frame exchange context:
  DL: Parameters of Block Ack agreement, SN space, maximal SN being allocated to the frame.
  UL: Parameters of Block Ack agreement, Maximal SN whose frame being sent to the up layer, duplicate detection information.
    The reorder buffer may be forwarded to the target AP MLD.

## Slide 3: Cross AP MLD Frame
An Action frame (cross AP MLD Action frame) may be transmitted to target AP MLD (the peer AP MLD of the serving AP MLD) through the serving AP MLD.
  Such Action frame carries the Peer AP MLD element or updating the current element.
An Action frame (cross AP MLD Action frame) may be transmitted to target AP MLD directly. In this case the Target AP MLD needs to know the non-AP MLD’s serving AP MLD (the peer AP MLD of the target AP MLD).
  Such Action frame carries the Peer AP MLD element.
The Peer AP MLD element carries the AP MLD ID of the peer AP MLD or the MAC address of the peer AP MLD.
  The AP MLD ID is used when the RNR is the only way to acquire the information of the target AP MLD where the RNR doesn’t carry the target AP MLD MAC address.
Element ID
Length
Element ID
Extension
Peer AP MLD ID/Address

## Slide 4: Beacon, Authentication, EAPOL Key
An AP MLD can indicate whether it is in a group of AP MLDs that can be seamlessly roamed among them.
  As an example, such indication can be in Basic Multi-Link element by repurposing one current reserved bit in Presence Bitmap subfield of the Multi-Link Control field.
An AP MLD can indicate the identifier of the group of AP MLDs for seamless roaming in a new defined element (Seamless Roaming Domain (SRD) element) in Authentication Request/Response, Probe Response, EAPOL Key.
  Besides seamless roaming domain identifier (MAC address), the SRD element carries the other information related to seamless roaming, e.g.
    AP MLD ID space (the AP MLD IDs no less than the announced AP MLD ID) to identifying the remote AP MLDs that a non-AP MLD associated with the reporting AP MLD can seamlessly roam to.
    Whether the simultaneous DL frame exchanges with the two AP MLDs is allowed.
    Whether data forwarding to target AP MLD is supported.
  The association is with the roaming domain. The SCS agreement, BA agreement, EPCS are the agreements with the roaming domain.
  In the Authentication, EAPOL key negotiation, the seamless roaming domain identifier is used as the authenticator address.

## Slide 5: Candidate Target AP MLD Announcement
RNR vs Neighbor Report
  RNR can use less octets to provide the candidate Target AP MLD information.
  Probe procedure with some changes if required can be naturally used.
    Beacon frame will not carry such information.
  Neighbor Report can easily provide additional information of the candidate target AP MLD for the roaming.
    MAC address of the candidate roaming AP MLD.
    When a non-AP MLD solicits whether the candidate AP MLDs satisfy the new resource request.
  Neighbor reporting procedure or BTM with some changes if required can be used.
    Beacon frame will not carry such information.
Based on these observation, it is ok to allow both RNR and Neighbor Report to report the candidate AP MLD information.

## Slide 6: Candidate Serving AP MLD Recommendation
The target AP MLD recommendation can be done through BTM procedure.
In Neighbor Report element,
  The Multi-Link subelment with a bit can be used to indicate whether the AP MLD belonging to the same seamless roaming domain as the serving AP MLD is recommended.
  A new subelement with the seamless roaming domain MAC address indicates that the AP MLD belonging to the same seamless roaming domain as the serving AP MLD is recommended.

## Slide 7: ML Probe Procedure
The Multi-Link Probe Request, Multi-Link Probe Response are used for a non-AP MLD to acquire the full information of the neighbor AP MLD that can be seamlessly roamed to.
  The Probe Request Multi-Link element can indicate the candidate target AP MLD through the AP MLD ID. (preferred method)
  Another variant is to indicate the candidate target AP MLD through the Peer AP MLD element.
Element ID
Length
Element ID
Extension
Peer AP MLD ID/Address

## Slide 8: Establishing Link with Target AP MLD
Link Reconfiguration Request/Response are updated for establishing link with the target AP MLD.
  The Link Reconfiguration Request carries the AP MLD address of the Target AP MLD that the non-AP MPD transmitting the request intends to seamlessly roam to.
    The AP MLD address can be carried in Reconfiguration Multi-Link element.
    Another variant is to indicate the candidate target AP MLD through the Peer AP MLD element.
Element ID
Length
Element ID
Extension
Peer AP MLD ID/Address
The Link Reconfiguration Request/Response frame are used to reserve the resource with the target AP MLD
  TWT agreements,
  TID to Link mapping,
  BA agreement if new agreement is required,
  SCS agreement establishment
    By default, SCS agreement is transfer from the current AP MLD to the new AP MLD. Unless the SCS new agreement is required by the non-AP MLD in roaming process, the SCS agreement establishment is not needed.
  Another variant is that the resource reservation is done during Roaming Request/Response for DS mapping updating, frame exchange context transfer procedure.

## Slide 9: Resource Reservation Method 1 with the Target AP MLD
one or multiple Resource Reservation elements are used for encapsulating the resource request(s)/response(s) in Link Reconfiguration Request/Response, Roaming Request/Response between non-AP MLD and target serving AP MLD through current serving AP MLD.
The Resource Reservation element carries the following
  Action field of the request/response Action being encapsulated.
  The new defined element (Target AP MLD ID) carrying the target AP MLD ID or target AP MLD MAC address if the frame carrying the Resource Reservation element doesn’t include the element to identify the target AP MLD.

## Slide 10: Resource Reservation Method 2 with the Target AP MLD
Instead of doing the resource reservation negotiation with the target AP MLD through MLD reconfirmation procedure or Roaming Request/Response, the resource reservation can also be done through separate resource negotiation before finishing the DS mapping updating
  The related request/response frame is exchanged with the target carries through the current AP MLD
    The request/response frame carries the target AP MLD ID or target AP MLD MAC address in a new defined element.
      A request/response frame for MLD level resource reservation at the target AP MLD carries the new defined element.
        For example, the TID-to-Link Mapping Request, Response frame carry the new element that identifies the target AP MLD.
      A request/response frame for link level resource reservation at the target AP MLD carries the new defined element and carries the applied link (e.g. MLO Link Info element).
        For example, the TWT Setup frame carries the new element that identifies the target AP MLD, the TWT element with Link ID Bitmap field.
  The related request/response frame is exchanged with the target carries directly.
Element ID
Length
Element ID
Extension
Peer AP MLD ID/Address

## Slide 11: Summary
The following are discussed in the presentation:
  The elements assisting the seamless roaming
  The candidate target AP MLD recommendation
  The link establishment with the target AP MLD
  The authentication, ML Probe update for seamless roaming.

## Slide 12: SP 1
Do you support that a serving AP MLD can use the BTM procedure with update(s) (if required) to recommend one or more candidate target AP MLDs within the UHR seamless roaming mobility domain to a non-AP MLD for roaming?
  Note – An AP can transmit the BTM Request frame unsolicited or as a response to BTM Query from a non-AP MLD.
  TBD – detailed information to be carried

## Slide 13: Backup Slides

## Slide 14: Candidate Target AP MLD Announcement----RNR (1)
RNR is used to announce the links of the reported AP MLDs that can be seamlessly roamed to from the serving AP MLD.
  A non-AP MLD can solicit the candidate target AP MLDs that are in the same roaming domain as the serving AP MLD.
  If an AP MLD can’t be roamed to seamlessly from the serving AP MLD, the APs affiliated with the AP MLD are not carried in the RNR.
    Indicating the soliciting of candidate target AP MLDs in Probe Request
  One optimization is to only carry RNR with information of neighbor AP MLDs for seamless roaming through probe procedure.
    Probe Response carrying only the information of the candidate target AP MLDs is in UHR PPDU.

## Slide 15: Candidate Target AP MLD Announcement----RNR (2)
Reuse current TBTT Information Type vs New TBTT Information Type
  The new TBTT Information Type provides flexibility to carry the required information of the candidate target AP MLD.
  The current TBTT Information Type has the restriction to add the new information specific to the candidate target AP MLDs.
    The repurposing of the current subfields is required if we don’t want a longer TBTT Information field.
We prefer the new TBTT Information Type but ok with the current TBTT Information Type.

## Slide 16: Candidate Target AP MLD Announcement----RNR (3)
Method : New TBTT Information Type
  The TBTT Information Set includes one or multiple TBTT Information field.
  Each TBTT Information field includes:
    Neighbor AP TBTT offset,
    BSSID.
    BSS Parameter
    Tx power restriction (20Hz PSD or Tx power restriction in dbm).
    Non-AP MLD’s Resource Supported (SCS agreements, BA agreements, TWT agreements)
      Supported, not supported, not known
      Another variant is to carrying the target AP MLD load.
    AP MLD ID,
      The AP MLD ID is the identifier of the candidate target AP MLD with which the reported AP is affiliated.
        A non-AP MLD can seamlessly roam to it from the current serving AP MLD.
        The AP MID ID space for identifying seamless roaming is announced by the reporting AP MLD or 11bn spec.
        The AP MLD ID spaces for the candidate roaming AP MLDs announced in all the links of an AP MLD (or virtual AP MLDs in an AP MLD device) are same.
          A candidate roaming AP MLD has same ID announced by an AP MLD.

## Slide 17: Candidate Target AP MLD Announcement----Neighbor Report
Neighbor Report element indicates whether the reported AP MLD with which the reported AP is affiliated is in a seamless roaming domain, and the seamless roaming domain ID with which the reported AP MLD is affiliated with.
  The Multi-Link subelment with a bit can be used to indicate whether the AP MLD belong to a seamless roaming domain.
  A new subelement indicates the roaming domain identifier that the AP MLD is in. This may not be needed when only the candidate target AP MLDs in the same roaming domain as the serving AP MLD are reported.
Neighbor Report element indicates the resource supported by the candidate target AP MLD (SCS agreement support, BA agreement support, TWT agreement support)
  Such indication can be a subelement.
  SCS agreement support indicates whether the candidate target AP MLD satisfies the SCS agreement of the non-AP MLD.
  BA agreement support indicates whether the candidate target AP MLD satisfies the DL/UL BA agreements with the non-AP MLD.
  TWT agreement support indicates whether the candidate target AP MLD satisfies the TWT agreements of the non-AP MLD.