## Slide 1: NPCA Follow Up
Date: 2024-11-09
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: NPCA Primary Channel Location
Each 80MHz channel covered by a BSS with > 80MHz operating channel can’t have more than one backoff 20MHz channel (a backoff 20MHz channel is either the NPCA backoff 20MHz channel or the primary channel)
  NPCA is not allowed in a BSS with <80MHz operating channel
Considering that most deployed enterprise WLAN network has no more than 80MHz BSS operating BW, it is better to allow an AP to enable NPCA operation in an 80MHz BSS.
  Only one NPCA primary channel is allowed in the BSS

## Slide 3: RU Index
Observation:
  When an AP solicits TB PPDU from STAs after NPCA primary channel’s backoff, the BW of the soliciting Trigger frame may cover both primary channel and NPCA primary channel.
  The RU index for the same 20MHz channels may be different when the different channel being treat as primary channel for RU index coding.
    The STAs don’t do the NPCA channel switch since the OBSS activity is missing and the STAs do the NPCA channel switch have the different view of the backoff channel.
  Such ambiguity may also happen when MU-RTS is used to solicit CTS frame.
Solution:
  The Trigger frame indicates whether the NPCA Primary channel is used as the reference for RU index coding.

## Slide 4: Beacon and Group-Addressed Frames
Observation:
  If an AP in NPCA primary channel transmits Beacon and group-addressed frames, the associated STAs that don’t enable NPCA will miss the Beacon and group-addressed frames.
Observation:
  If the OBSS activity on the BSS primary overlaps with the AP’s TBTT and the AP switch to the NPCA primary channel
    NPCA AP & non-AP STA(s) need not switch back to BSS Primary at the TBTT
    AP shall transmit the Beacon/group addressed frames after switching back to BSS Primary channel.

## Slide 5: Summary
This presentation discusses the following of the NPCA:
  The condition to allow NPCA primary channel in a BSS and the location of the NPCA primary channel.
  The RU index coding of Trigger frame when switching to NPCA primary channel.
  The Beacon, group addressed frames under NPCA operation.

## Slide 6: SP 1
Do you agree that an AP shall not allow the use of NPCA within its BSS if the BSS operating bandwidth is less than or equal to 40 MHz?

## Slide 7: SP 2
Do you support that:
  When transmitting a Trigger frame on the NPCA Primary channel, the NPCA AP shall signal the RU index considering the NPCA Primary channel as the reference primary channel.
  The Trigger frame shall explicitly indicate that it is transmitted via the NPCA Primary channel (details TBD).

## Slide 8: SP 3
Do you support that:
  If a TXOP on the NPCA Primary channel overlaps with the TBTT, the AP shall not transmit the Beacon frame or group addressed frames until it switches back to the BSS Primary channel.
    NOTE – The NPCA AP and non-AP STA participating in frame exchanges must not switch back to the BSS Primary channel at the TBTT and can continue operating on NPCA Primary until the OBSS transmission ends on BSS Primary channel.

## Slide 9: Reference
[1] 11-24/1563 NPCA Follow Up