## Slide 1: ICF Follow Up
Date: 2024-11-09
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: ICF
The ICF transmitted by a non-AP STA or an AP has single addressed device can solicit a non-HT (duplicate) PPDU.
  The User Info field needs to be clarified.
A TXOP holder being the non-AP STA can report its available time and unavailable time in ICF.
The available time and unavailable time in ICF needs to be clarified.

## Slide 3: Single TXO Responder Soliciting by ICF
The ICF transmitted by a non-AP STA or an AP addressed to a single destination can solicit the ICR in a non-HT (duplicate) PPDU.
The RA of the ICF is the BSSID of the addressed AP or the MAC address of the addressed STA.
The User Info field addressed to the recipient has all bits reserved with AID12 field indicating the addressed device.
  The bits of the User Info field other than AID12 field are reserved.

## Slide 4: Available Time and Unavailable Time in ICF
The unavailable time is defined by an unavailable start time, unavailable time duration.
The available time is defined by the current time to the unavailable start time.
The unavailable time is carried in the frame body of ICF.
  Option 1:
    The unavailable time is carried in a special User Info field ( Common Dynamic User Info field).
    The Common Dynamic User Info field has special value (e.g. >2007) in its AID12 field to indicate the dynamic control information being carried in it.
    The Common Dynamic User Info field has no Trigger Dependent User Info field.
    B12 to B39 of the User Info field carries
      Control Type ID (e.g. 4-bit field by using B12 to B15) with special value in Control Type ID to indicate feedback control type
      Unavailable Start Time (9-bit field) in unit of 64us,
      Unavailable Duration (9-bit field) in unit of 64us, and
      Reserved (e.g. 6-bit field) following Unavailable Duration.

## Slide 5: Summary
We proposed the following in this presentation:
  The ICF format when the ICF is transmitted by a non-AP STA.
  The available information and unavailable information in ICF.
  The ICF frame format to carry available time and unavailable time.

## Slide 6: SP1
Do you agree to make all fields reserved after the AID12 field in the user info field addressed to the STA for a BSRP TF soliciting non-HT PPDU?