## Slide 1: SMD Architecture
Date: 2024-11-04
Authors:

## Slide 2: Introduction
TGbn SFD Motion 279 defines a logical SMD-ME (SMD management entity) that provides SMD level association, authentication and RSNA key management (PMKSA and PTKSA) functions
SFD Motion 280 defines support for following two SMD roaming architectures:
  SMD arch with separate MAC-SAP per AP MLD – this enables roaming between AP MLDs of an SMD, where each AP MLD exposes its own MAC-SAP to the DS for data path within the SMD.
  SMD arch with a single MAC-SAP for the SMD – this enables roaming within AP MLDs of an SMD covering multiple non-collocated AP MLDs, where a single MAC-SAP is exposed to the DS across all AP MLDs for the data path within the SMD.
In this presentation we consider a common SMD framework that would support both variants of SMD roaming architecture

## Slide 3: SMD Architecture (1)
SMD defines a set of AP MLDs across which a non-AP MLD can perform seamless roaming
The logical SMD management entity (SMD-ME) provides single anchor point for management functions that include IEEE 802.1X authenticator, RSNA Key Mgmt and Association, across all AP MLDs of the SMD.
  SMD-ME has a unique identifier (e.g. 48-bit MAC Address), which is also the 802.1X authenticator address (AA) of the SMD-ME
  PMKSA and PTKSA keys are established between 802.1X Authenticator address (AA) and non-AP MLD MAC address (SPA)
Upper MAC functions at SMD-ME include at a minimum authentication, association and security association mgmt.
  Split of other upper MAC functions between SMD-ME and AP MLDs is based on distributed vs centralized SMD roaming arch.
  AP MLDs interface with each other for context transfer (in distributed mode)
(11be D7.0: 5.1.5.1a MLD MAC sublayer functions)

## Slide 4: SMD Architecture (2)
Logical SMD-ME can be hosted on a centralized controller/WLC or on individual AP MLDs of the SMD
SMD-ME hosted on a WLC:
WLC provides the SMD level 802.1X authenticator, association and RSNA key management functions for non-AP MLDs
Context related to a non-AP MLD is transferred between AP MLDs when SMD-ME is not exposing a single MAC-SAP
SMD-ME hosted on AP MLDs:
SMD level 802.1X authenticator, association and RSNA key management functions for non-AP MLDs are hosted in a distributed manner on AP MLDs (distributed mode)
Context related to a non-AP MLD is transferred between AP MLDs during seamless roaming

## Slide 5: SMD Architecture (3)
The logical SMD-ME has one 802.1X Authenticator that provides authentication functions for non-AP MLDs when authenticating with SMD-ME
The 802.1X Controlled and Uncontrolled Port filtering is performed at each AP MLD
The 802.1X Authenticator component of SMD-ME manages the blocking and unblocking of 802.1X Controlled ports at each AP MLD, based on the point of latest attachment for the non-AP MLD.
  At initial SMD association with AP MLD1, the Controlled Port for AP MLD1 is unblocked
Case 1: SMD arch exposing separate MAC-SAP to DS per AP MLD (logical view)
  Access to DS via C-port is enabled only through MAC-SAP of one of the AP MLDs at a time
  During seamless roaming execution, 802.1X Authenticator in SMD-ME blocks Controlled port at current AP MLD1 (for UL) and unblocks Controlled port at target AP MLD2.
  After DS mapping change, Tx/Rx with DS is opened through C-port of target AP MLD2.

## Slide 6: SMD Architecture (4)
Case 1b: SMD-ME hosted at each AP MLD, with separate MAC-SAP to DS per AP MLD
  Each AP MLD is hosting 802.1X Authenticator component as part of SMD-ME
  During SR, after receiving roaming execution request, 802.1X Authenticator of SMD-ME at current AP MLD1 blocks Controlled port for UL
  After DS mapping change is initiated by the target AP MLD, 802.1X Authenticator of SMD-ME at target AP MLD2 unblocks the Controlled port of the target AP MLD2
  802.1X Authenticator of the SMD-ME at the current and target AP MLDs is identified by same AA address, e.g. the SMD MAC address
  The MAC-SAP of each AP MLD is identified by the AP MLD MAC address (as in EHT)
SMD-ME exposing different MAC-SAPs (physical deployment)

## Slide 7: DS Mapping change for SMD roaming
For SMD roaming (when each AP MLD has a separate MAC-SAP), the SMD-ME component on the target AP MLD should initiate DS mapping change, since non-AP MLD associates with the SMD-ME. The DS SAP primitive may need to be enhanced to support this:
  Add a new APMLDMACAddress parameter that specifies the MLD MAC address of the AP MLD trough which the non-AP MLD specified by the STAAddress is now connected within the SMD.
  DS-STA-NOTIFY.request(
STAAddress,
APMLDMACAddress,
UpdateType
)

## Slide 8: SMD Architecture (5)
Case 2: SMD-ME exposes a single MAC-SAP to the DS across all AP MLDs of the SMD
  SMD-ME is hosted at a centralized entity that exposes the single MAC-SAP
  The single MAC-SAP is identified by the SMD MAC Address
  The 802.1X Authenticator (identified by SMD MAC Address) manages the blocking and unblocking of 802.1X Controlled ports for the non-AP MLD
  During SR between AP MLDs, no DS mapping change is initiated
  Split of Upper MAC data path functionality between AP MLD and SMD-ME can be implementation dependent

## Slide 9
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
1. Non-AP MLD is connected to DS through the links of AP MLD1.
Case 1: SR with SMD exposing separate MAC-SAP per AP MLD (1)

## Slide 10
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
2. Non-AP MLD is in roaming transition to AP MLD2. UL data to DS is paused from AP MLD1 during roaming transition. After DS mapping change is initiated by AP MLD 2, UL and DL data are enabled with AP MLD2
Case 1: SR with SMD exposing separate MAC-SAP per AP MLD (2)
Context transfer

## Slide 11
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
3. Non-AP MLD has completed roaming transition and is now connected to DS through the links of AP MLD2.
Case 1: SR with SMD exposing separate MAC-SAP per AP MLD (3)

## Slide 12: Case 2: SR with SMD exposing single MAC-SAP (1)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
1. Non-AP MLD is connected to DS through the links of AP MLD1.

## Slide 13: Case 2: SR with SMD exposing single MAC-SAP (2)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
2. Non-AP MLD is in roaming transition to AP MLD2. UL and DL are enabled through AP MLD1 and AP MLD2 during roaming transition.

## Slide 14: Case 2: SR with SMD exposing single MAC-SAP (3)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
3. Non-AP MLD has completed roaming and is connected to DS through the links of AP MLD2.

## Slide 15: Hierarchical SMD Architecture
In some deployments, there can be SMD with single MAC SAP deployed for smaller/targeted areas to provide improved reliability of connecting over links of multiple AP MLDs (e.g. in IIoT). Other areas may have AP MLDs deployed.
For such deployments, a higher level SMD (SMD-H) can provide seamless roaming across a lower level SMD with single MAC SAP (SMD-L) and other AP MLDs, leading to a hierarchical SMD deployment with SMD of (AP MLDs + lower level SMD(s) with single MAC SAP)
Here, PMKSA and PTKSA can be established at SMD-H level and used for SMD-L and other AP MLDs
Client would perform seamless roaming between an AP MLD 2 (in SMD-L) and another AP MLD3 in SMD-H

## Slide 16: Conclusion
We covered a common SMD roaming framework to support both variants of SMD roaming arch.
  SMD roaming with separate MAC-SAP per AP MLD of the SMD
  SMD roaming with a single MAC-SAP for the SMD
In the case of separate MAC-SAP per AP MLD architecture, the 802.1X Authenticator in the SMD-ME manages blocking and unblocking of 802.1X Controlled ports for the non-AP MLD at the AP MLDs, as the non-AP MLD roams within the SMD
  SMD-ME supports upper MAC functionality for authentication, association and security association (PMKSA, PTKSA)
In the case of single MAC-SAP per SMD, the 802.1X Authenticator in the SMD-ME manages the blocking and unblocking of 802.1X Controlled ports for the non-AP MLD at the SMD-ME level
  SMD-ME supports upper MAC data path functionality
  Split of upper MAC data path functionality between AP MLD and SMD-ME can be implementation dependent
A hierarchical SMD architecture can enable SR in hybrid deployments of these two variants

## Slide 17: SP1
Do you support that for a Seamless Mobility Domain (SMD), the SMD and the 802.1X Authenticator component in the corresponding SMD-ME are uniquely identified by an SMD Identifier?
The SMD identifier is in the format of a 48-bit MAC address
The SMD Identifier is used in establishing single PMKSA and PTKSA for a non-AP MLD that associates with the SMD-ME

## Slide 18: SP2
Do you support that for a Seamless Mobility Domain (SMD), in the case of a separate MAC-SAP per AP MLD architecture, the 802.1X Authenticator in the SMD-ME manages the blocking and unblocking of 802.1X Controlled ports for the non-AP MLD at the AP MLDs of the SMD, as the non-AP MLD roams within the SMD?
At initial SMD association through an AP MLD1, the 802.1X Authenticator unblocks Controlled Port at AP MLD1 for the non-AP MLD
During seamless roaming execution, 802.1X Authenticator blocks Controlled port at the current AP MLD1 for UL direction and unblocks Controlled port at the target AP MLD2, after the DS mapping change is initiated at the target AP MLD for the non-AP MLD
Access to DS for a non-AP MLD via the Controlled port is enabled only through MAC-SAP of one of the AP MLDs of the SMD at a time